CONTROL MEASURE SUMMARY FOR 
Auto Refinish Coatings – Area Source

| Control Measure Summary: Limiting the concentration of solvents in Auto Refinishing Coatings in order to reduce VOC emissions. Encourage the use of high transfer-efficiency painting methods (e.g., high volume low pressure spray guns), and controls on emissions from equipment (e.g., spray gun) cleaning, housekeeping activities (e.g., use of sealed containers for clean-up rags), and operator training. | Emissions (tons/year) in Ozone Transport Region |
| --- | --- |
| 2002 existing measure: Federal Auto Body Refinishing rules 40CFR Part 59 Subpart B Emission Reductions: 37% reduction from Part 59 (from Pechan OTC Model Rule Report) due to Part 59 VOC content limits Control Cost: $118 per ton for Part 59 rules Timing of Implementation: Part 59 compliance required by January 1999 Implementation Area: Part 59 – Nationwide; | VOC Uncontrolled: 2002 Reduction: 2002 Base: | 50,759 -18,781 31,978 |
| OTB Control Measure: OTC Model Rule for Mobile Equipment Repair and Refinishing Emission Reductions: 38% reduction from 2002 Levels in those States that adopted OTC model Rule (per Pechan March 31, 2001 OTC Model Rule Report) Control Cost: $1,534 per ton of VOC Timing of Implementation: Assuming 2007 effective date of rule, emission reductions are achieved 01/01/09. Implementation Area: All counties in the OTR. | VOC: 2009 Reduction: 2009 Remaining: | -10,468 21,510 |
| Candidate measure: CARB October 20, 2005 SCM Staff Report – Lowers VOC limits, combines coatings categories, simplifies recording. Emission Reductions: CARB estimates a 65% reduction in VOC emissions from a 2002 baseline; the OTC model rule is very similar to the CARB 2002 baseline, so a similar reduction would be expected in the OTR. Control Cost: $2,860 per ton Timing of Implementation: TBD. Implementation Area: All counties in the OTR. | VOC: 2009 Reduction: 2009 Remaining: | -13,981 7,529 |
| Policy Recommendation of State/Workgroup Lead: The SCAQMD adopted the CARB SCM on December 2, 2005. Other California districts are expected to adopt the SCM in 2006. Environment Canada is also creating a rule based on the same CARB limits. The OTC should develop a model rule based on the 2005 CARB SCM in conjunction with Environment Canada to be presented at the June OTC meeting. |
| Brief Rationale for Recommended Strategy: After implementing the OTC model regulation with its requirements for use of spray gun technology with high transfer efficiency and enclosed spray gun cleaners, the next most effective strategy is to significantly reduce the VOC content of the coatings. Next Steps: Define the categories of finish coatings that are being examined. Define the extent of controls on paints versus controls on shop exhaust systems. |

REFERENCES: 2002 Existing Measure (Federal Part 59 Rules): E.H. Pechan & Associates, Inc., AirControlNET Version 4.1: Documentation Report, September 2005. Pages III-1364 shows the Federal Part 59 rule at a cost of $118 per ton (1990$) and a reduction of 37 percent from uncontrolled levels. 2009 On-the-Books Measure (OTC Model Rule): E.H. Pechan & Associates, Inc., Control Measure Development Support Analysis of Ozone Transport Commission Model Rules, March 31, 2001. Table II-6 shows 37% reduction for Federal Part 59 rule and 38% (OTC Model Rule beyond Federal rule). Page 17 presents cost of $1,534 per ton based on estimates used for PA Rule 129.75. Candidate Measure (CARB 2005 Suggested Control Measure): California Air Resources Board. Staff Report for the Proposed Suggested Control Measure for Automotive Coatings. October 2005. Table V-3 shows the estimated 65% reduction from 2002 baseline emissions for new automotive coatings limits. A similar reduction is expected for the OTR. Page VII-6 indicates that the cost-effectiveness of the SCM is estimated to be $1.43 per pound of VOC reduced ($2,860 per ton). The CARB SCM coating categories and VOC limits are: The OTC 2002 Model Rule coating categories and VOC limits are: OTC Model Rule Limit Coating Type Grams per Liter Pounds per gallon Automotive pretreatment primer 780 6.5 Automotive primer-surfacer 575 4.8 Automotive primer-sealer 550 4.6 Automotive topcoat: single stage-topcoat 600 5.0 2 stage basecoat/clearcoat 600 5.0 3 or 4-stage basecoat/clearcoat 625 5.2 Automotive Multi-colored Topcoat 680 5.7 Automotive specialty 840 7.0

- Stakeholder Comment Summary:

Since most auto body shops use solvent-borne coating technology, regulatory agencies must take into account the fact that the end users require additional training to be able to apply low VOC-content and water-borne coating products successfully.  The use of water-borne technology involves the updating of current spray booths and ovens…this may lead to long lead-in time for equipment upgrades.