Reduced Load Growth

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  GHG emissions reductions associated with a series of 2.5% reductions in electricity consumption load growth from 2017 to 2025.

Other Involved Agencies: PUC

Possible New Measure(s): This initiative identifies the carbon emissions benefits associated with curbing the rate of growth in electricity consumption in PA.  This strategy builds upon the conservation requirements of House Bill 2200, which requires 1.0% and 2.5% reductions in overall consumption in 2011 and 2013, respectively.  House Bill 2200 requires the PUC to assess the potential of further cost-effective reductions in 2018.  This work plan asserts that significant potential opportunities exist, through appliance efficiency upgrades and efficiency improvements within new and existing buildings, to yield sizeable reductions in consumption.

Please note that this analysis does not include the very modest consumption and associated system losses from municipalities that are service providers or the rural electric cooperatives.

Potential GHG Reduction: 	10.7 MMTCO2 additional;

15.52 MMTCO2 total w/ HB 2200

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under two different scenarios; Reduced Load Growth (RLG) and business as usual (BAU).  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates of consumption were made beginning with the last year of reported data to the PUC (2006).

- A similar set of projections was made that incorporated the load curtailments as required for in HB2200 coupled with a series of 2.5% reductions occurring in even number years from 2018 through 2024.

- The sum total MWh for consumption and system losses for each scenario (RLG and BAU) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) for electricity produced in PA.  The emissions rates were calculated from generation and emissions data reported to the EIA.

- The difference between these two scenarios yields the actual projected reduction in CO2 emissions in year 2025.

  - The result is a cumulative effect curtailing load growth to less than would be the case under the projected BAU scenario in 2016.

  - This scenario facilitates reductions in electricity consumption while still realizing growth in electricity demand.  The projected emissions reductions from this work plan yield an additional 10.7 MMTCO2 beyond that which is provided by HB2200.

- The tables at the end provide the data used throughout this analysis.

Assumptions:

- Adequate cost-effective reductions exist or will exist, through year 2024, to provide the estimated 25 million MWh of curtailment as compared to the unchecked, projected rate of growth in electricity consumption.

- No reductions would be required if not supported through an analysis of cost-effective measures.

Economic Cost:

- Cost to DEP - None

- Cost to the Commonwealth – HB 2200 requires the PUC to hire a program administrator to oversee this process and to provide assessments as to the cost-effectiveness and level of additional reductions that may be possible within PA.  The cost for this service is unknown.

- Cost to regulated community or consumer – Not quantified, as of yet.  Short-term capital costs may be experienced, depending on a host of issues but short and long-term savings are anticipated.  Requires detailed analysis.

- Are there Federal funds available? – Implementation will be a facet of PUC requirements under HB2200 and are required to be cost effective.  Therefore, federal funding is not required.  U.S. DOE State Energy Plan funding may be available, if shown to be necessary and would require coordination between the PUC and DEP.

- Do these costs fund other programs? No.  Any costs are expected to result in changes to consumer behavior.

- Are cost savings realized from this initiative? Cost savings are expected but this does require a detailed analysis.  The assumption is that reductions will only be required such that can be sustained through cost-effective measures.

Implementation Steps:  The following, and other, considerations should be examined as policy tools to support this measure:

- As required in HB 2200, a study must be undertaken to identify the full suite of cost-effective measures that should be given consideration.  Any notion of a Tier IV for energy efficiency must also be viewed as a complementary strategy to achieving reduced load growth.

- Legislation may need to be approved that builds on the current structure of House Bill 2200 and which supports the framework and/or intent of this reduced load growth work plan.

- A legislative amendment to the AEPS to establish a dedicated market for energy efficiency credits (new tier or carve out).  This would reward over-compliance and provide a highly cost-effective measure to achieving greater reductions.

- Requiring electric distribution companies to invest in demand side response initiatives, including rebates to consumers.

- Requiring that all cost-effective supply-side and demand-side measures have been identified and acted upon before approvals for new generation are granted.  ACEEE estimates that the investment in these efficiency measures is about $3/MWh vs. $10/MWh to construct new generation.

- Requiring distribution companies to provide all PA consumers with access to time-of-day metering and real time pricing options for electricity.

- Implementing and enforcing high performance building standards for the commercial, institutional, state and municipal government sectors that establish minimum green building practices and energy efficiency standards.

- Coupled with the high performance building standard, we should establish resources to educate and encourage annual benchmarking of all commercial, institutional, state and municipal government buildings, similar to that established by the U.S. EPA that documents the gains or losses in energy consumption on a per square foot basis, based on the type of activity occurring.  This information is publicly accessible.  It empowers building owners and operators to achieve higher performance (efficiency).

- Work with neighboring states to establish regional efficiency standards for appliances and electronics where none currently exist or where minimum standards are less than optimal.

- Establish an aggressive phase-out of compact fluorescent lights and/or establish a pricing/tax structure that preferentially treats lighting with a higher lumens to watts ratio.

- Rate decoupling

Potential Overlap:

- HB 2200, Transmission and Distribution Loss, etc.

- AEPS Tier I @ 8%, 15%, 20%

- All Electricity Efficiency Initiatives (Energy Audits, High Performance Buildings, Appliance Standards, etc)

| Reduced Load Growth Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,389,357 | 15,098,028 | 14,851,407 | 4,712,258 | 42,692,668 | 39,742,478 | 1,056,176 | 22,671,240 | 155,213,613 |
|  | 2012 | 14,542,758 | 15,394,107 | 15,045,070 | 4,727,394 | 43,594,030 | 40,237,475 | 1,070,771 | 23,066,236 | 157,677,842 |
|  | 2013 | 14,330,349 | 15,303,592 | 14,860,228 | 4,624,014 | 43,401,561 | 39,720,171 | 1,058,429 | 22,881,412 | 156,179,756 |
|  | 2014 | 14,483,120 | 15,603,702 | 15,054,007 | 4,638,867 | 44,317,890 | 40,214,889 | 1,073,055 | 23,280,070 | 158,665,600 |
|  | 2015 | 14,637,520 | 15,909,697 | 15,250,313 | 4,653,767 | 45,253,565 | 40,715,770 | 1,087,883 | 23,685,673 | 161,194,188 |
|  | 2016 | 14,793,566 | 16,221,693 | 15,449,178 | 4,668,715 | 46,208,994 | 41,222,889 | 1,102,917 | 24,098,344 | 163,766,296 |
|  | 2017 | 14,951,275 | 16,539,807 | 15,650,637 | 4,683,711 | 47,184,595 | 41,736,325 | 1,118,158 | 24,518,204 | 166,382,712 |
|  | 2018 | 14,732,899 | 16,442,556 | 15,458,355 | 4,581,287 | 46,976,274 | 41,199,751 | 1,105,269 | 24,321,745 | 164,818,136 |
|  | 2019 | 14,889,962 | 16,765,001 | 15,659,933 | 4,596,002 | 47,968,075 | 41,712,898 | 1,120,543 | 24,745,498 | 167,457,912 |
|  | 2020 | 14,672,481 | 16,666,426 | 15,467,537 | 4,495,495 | 47,756,295 | 41,176,626 | 1,107,626 | 24,547,218 | 165,889,704 |
|  | 2021 | 14,828,900 | 16,993,261 | 15,669,235 | 4,509,935 | 48,764,564 | 41,689,485 | 1,122,932 | 24,974,899 | 168,553,211 |
|  | 2022 | 14,612,312 | 16,893,344 | 15,476,724 | 4,411,310 | 48,549,268 | 41,153,513 | 1,109,989 | 24,774,780 | 166,981,240 |
|  | 2023 | 14,768,089 | 17,224,629 | 15,678,542 | 4,425,480 | 49,574,279 | 41,666,084 | 1,125,328 | 25,206,426 | 169,668,856 |
|  | 2024 | 14,552,388 | 17,123,351 | 15,485,917 | 4,328,702 | 49,355,407 | 41,130,414 | 1,112,356 | 25,004,452 | 168,092,989 |
|  | 2025 | 14,707,527 | 17,459,147 | 15,687,855 | 4,342,606 | 50,397,438 | 41,642,697 | 1,127,728 | 25,440,100 | 170,805,098 |

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - Reduced Load Growth (RLG) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 830,122 | 1,188,535 | 1,317,116 | 305,652 | 2,839,172 | 2,854,787 | 59,693 | 1,479,628 | 10,874,704 |
|  | 2012 | 838,971 | 1,211,842 | 1,334,291 | 306,634 | 2,899,115 | 2,890,344 | 60,517 | 1,505,407 | 11,047,122 |
|  | 2013 | 826,717 | 1,204,717 | 1,317,898 | 299,928 | 2,886,315 | 2,853,185 | 59,820 | 1,493,344 | 10,941,926 |
|  | 2014 | 835,531 | 1,228,342 | 1,335,084 | 300,892 | 2,947,253 | 2,888,722 | 60,647 | 1,519,363 | 11,115,833 |
|  | 2015 | 844,438 | 1,252,430 | 1,352,493 | 301,858 | 3,009,478 | 2,924,701 | 61,485 | 1,545,834 | 11,292,718 |
|  | 2016 | 853,440 | 1,276,991 | 1,370,130 | 302,828 | 3,073,017 | 2,961,129 | 62,334 | 1,572,767 | 11,472,636 |
|  | 2017 | 862,539 | 1,302,033 | 1,387,997 | 303,801 | 3,137,897 | 2,998,010 | 63,196 | 1,600,169 | 11,655,640 |
|  | 2018 | 849,941 | 1,294,378 | 1,370,944 | 297,157 | 3,124,043 | 2,959,467 | 62,467 | 1,587,347 | 11,545,742 |
|  | 2019 | 859,001 | 1,319,761 | 1,388,821 | 298,111 | 3,190,000 | 2,996,327 | 63,330 | 1,615,003 | 11,730,355 |
|  | 2020 | 846,455 | 1,312,001 | 1,371,758 | 291,592 | 3,175,916 | 2,957,805 | 62,600 | 1,602,062 | 11,620,191 |
|  | 2021 | 855,479 | 1,337,730 | 1,389,646 | 292,529 | 3,242,969 | 2,994,645 | 63,466 | 1,629,975 | 11,806,437 |
|  | 2022 | 842,984 | 1,329,864 | 1,372,573 | 286,132 | 3,228,651 | 2,956,145 | 62,734 | 1,616,914 | 11,695,997 |
|  | 2023 | 851,971 | 1,355,943 | 1,390,471 | 287,051 | 3,296,817 | 2,992,964 | 63,601 | 1,645,085 | 11,883,903 |
|  | 2024 | 839,527 | 1,347,971 | 1,373,388 | 280,774 | 3,282,261 | 2,954,486 | 62,868 | 1,631,904 | 11,773,178 |
|  | 2025 | 848,477 | 1,374,405 | 1,391,297 | 281,675 | 3,351,559 | 2,991,284 | 63,737 | 1,660,336 | 11,962,770 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| Climate Impact ((Consumption + Losses) X CO2)) (RLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 155,213,613 | 10,874,704 | 166,088,317 | 106,213,479 | 96.34 |
|  | 2012 | 157,677,842 | 11,047,122 | 168,724,964 | 107,899,614 | 97.86 |
|  | 2013 | 156,179,756 | 10,941,926 | 167,121,681 | 106,874,315 | 96.94 |
|  | 2014 | 158,665,600 | 11,115,833 | 169,781,432 | 108,575,226 | 98.48 |
|  | 2015 | 161,194,188 | 11,292,718 | 172,486,906 | 110,305,377 | 100.05 |
|  | 2016 | 163,766,296 | 11,472,636 | 175,238,931 | 112,065,297 | 101.64 |
|  | 2017 | 166,382,712 | 11,655,640 | 178,038,352 | 113,855,526 | 103.27 |
|  | 2018 | 164,818,136 | 11,545,742 | 176,363,878 | 112,784,700 | 102.30 |
|  | 2019 | 167,457,912 | 11,730,355 | 179,188,267 | 114,590,897 | 103.93 |
|  | 2020 | 165,889,704 | 11,620,191 | 177,509,894 | 113,517,578 | 102.96 |
|  | 2021 | 168,553,211 | 11,806,437 | 180,359,649 | 115,339,995 | 104.61 |
|  | 2022 | 166,981,240 | 11,695,997 | 178,677,237 | 114,264,093 | 103.64 |
|  | 2023 | 169,668,856 | 11,883,903 | 181,552,760 | 116,102,990 | 105.31 |
|  | 2024 | 168,092,989 | 11,773,178 | 179,866,166 | 115,024,413 | 104.33 |
|  | 2025 | 170,805,098 | 11,962,770 | 182,767,868 | 116,880,052 | 106.01 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction RLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | ZLG | BAU | Delta | ZLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 166,088,317 | 167,765,977 | 1,677,660 | 96.34 | 97.31 | 0.97 |
|  | 2012 | 168,724,964 | 170,429,257 | 1,704,293 | 97.86 | 98.85 | 0.99 |
|  | 2013 | 167,121,681 | 173,138,235 | 6,016,554 | 96.94 | 100.42 | 3.49 |
|  | 2014 | 169,781,432 | 175,893,740 | 6,112,307 | 98.48 | 102.02 | 3.55 |
|  | 2015 | 172,486,906 | 178,696,613 | 6,209,707 | 100.05 | 103.65 | 3.60 |
|  | 2016 | 175,238,931 | 181,547,714 | 6,308,783 | 101.64 | 105.30 | 3.66 |
|  | 2017 | 178,038,352 | 184,447,917 | 6,409,565 | 103.27 | 106.98 | 3.72 |
|  | 2018 | 176,363,878 | 187,398,113 | 11,034,235 | 102.30 | 108.70 | 6.40 |
|  | 2019 | 179,188,267 | 190,399,210 | 11,210,944 | 103.93 | 110.44 | 6.50 |
|  | 2020 | 177,509,894 | 193,452,134 | 15,942,239 | 102.96 | 112.21 | 9.25 |
|  | 2021 | 180,359,649 | 196,557,826 | 16,198,177 | 104.61 | 114.01 | 9.40 |
|  | 2022 | 178,677,237 | 199,717,246 | 21,040,010 | 103.64 | 115.84 | 12.20 |
|  | 2023 | 181,552,760 | 202,931,375 | 21,378,615 | 105.31 | 117.71 | 12.40 |
|  | 2024 | 179,866,166 | 206,201,208 | 26,335,042 | 104.33 | 119.60 | 15.28 |
|  | 2025 | 182,767,868 | 209,527,761 | 26,759,893 | 106.01 | 121.53 | 15.52 |

# Comments

Do you mean incandescent?