Electricity 1: Act 129 (HB 2200) Work Plan for Potential GHG Reduction Measure

Strategy Name: Act 129 of 2008 (HB 2200)

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This initiative identifies the carbon emissions benefits associated with the reduction of electricity consumption and peak load, as described in Act 129 of 2008.  Act 129 requires:

- A reduction in electricity consumption, by May 31, 2011 of 1.0% below consumption levels for the period June 1, 2009 through May 31, 2010.

- A reduction in electricity consumption, by May 31, 2013 of 3.0% below consumption levels for the period June 1, 2009 through May 31, 2010 (additional reduction of 2.0% from the June 2009 through May 2010 baseline for a net total reduction of 3.0%).

- A reduction in peak demand, by May 31, 2013 of 4.5% of the highest 100 hours of demand

Please note that the imposition of requirements of Act 129 is not inclusive of the very modest consumption and associated system losses from municipalities that are service providers or the rural electric cooperatives.

Other Involved Agencies: PUC has implementation responsibility

Possible New Measure(s):

A study must be undertaken to identify the full suite of cost-effective measures that should be given consideration.  A report from the American Council for an Energy Efficient Economy (ACEEE) is being drafted for the PUC and DEP and should serve well to inform this process.  Act 129 does not specify how these reductions are to be achieved.  Responses will be purely market-driven.

Potential GHG Reduction:  8.01 MMTCO2

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under two different scenarios (Act 129 and business as usual (BAU)).  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates of consumption were made beginning with the last year of reported data to the PUC (2006).

- A similar set of projections was made that incorporated the load curtailments as called for year 2011 via Act 129.

- Another similar set of projections was performed for 2013 but which also included an additional calculation to factor in the 4.5% reduction in peak load demand required by Act 129.

- The sum total MWh for consumption and system losses for each scenario (Act 129 and BAU) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) for electricity produced in PA.  The emissions rates were calculated from generation and emissions data reported to the EIA.

- The difference between these two scenarios yields the actual projected reduction in CO2 emissions in year 2025.

- The tables at the end provide the data used throughout this analysis.

A series of tables summarizing the estimated CO2 reductions potential of this initiative are included in this work plan immediately following “Potential Overlap.”

Economic Cost:  $793.6 million savings

The cost savings resulting from implementation of Act 129 should result in approximately $793.6 million.  Some of this will be due to peak load reductions that result in lower wholesale energy and capacity charges but not less energy used.  There is the assumption that lower wholesale charges will be passed through to customers.  Other savings will result through reducing energy consumption.

Because we only have a rough idea of where energy prices will be in 3 - 5 years, we cannot predict these results with great accuracy.  Instead, savings estimates are based on recent price trends and future price projections, while using current energy prices as the basis for calculating those savings that occur in the wholesale market.  These estimates are believed to be very conservative since the total retail price values used are expected to be lower than what will be seen after the rate caps expire.  Two tables summarizing the estimated cost savings are included in this work plan and can be found immediately following the series of emissions reductions tables.

- Cost to DEP - None

- Cost to the Commonwealth - None

- Cost to regulated community or consumer – None anticipated (see above).  Act 129 requires only modest reductions in load growth.  Consumers should realize long-term cost savings.

- Are there Federal funds available? – N/A

- Do these costs fund other programs? N/A

- Are cost savings realized from this initiative? Yes, as noted above.  Market forces will drive compliance options and the path forward.  Actual savings will likely vary widely among the EDC territories, within the various rate classes and economic sectors and also based on socio-economic factors for residential consumers.

Implementation Steps:

- Act 129 was signed into law on October 15.

- By January 15, 2009, the PUC must adopt an energy efficiency and conservation program that requires each electric distribution company (EDC) to develop and implement cost effective energy efficiency & conservation plans to reduce consumption and peak load within their service territories, as noted in the Summary section of this work plan.

- The American Council for an Energy Efficient Economy (ACEEE) is conducting a statewide assessment of cost effective energy efficiency potential.  Building on this assessment, a more ambitious plan with several, periodic, load-reduction steps could be implemented and which would actually change the projected rate of consumption instead of simply slowing the rate.

Potential Overlap:

- Transmission and Distribution Loss Work Plan

- AEPS Tier I @ 8%, 15%, 20% Work Plans

- Any additional work plans that cut electricity consumption

| HB220 Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,390,891 | 15,100,962 | 14,853,338 | 4,712,411 | 42,701,585 | 39,747,416 | 1,056,322 | 22,675,162 | 155,238,085 |
|  | 2012 | 14,544,307 | 15,397,098 | 15,047,027 | 4,727,547 | 43,603,135 | 40,242,475 | 1,070,919 | 23,070,226 | 157,702,733 |
|  | 2013 | 14,411,727 | 15,399,892 | 14,947,070 | 4,647,835 | 43,679,069 | 39,950,693 | 1,064,667 | 23,022,008 | 157,122,962 |
|  | 2014 | 14,565,366 | 15,701,891 | 15,141,982 | 4,662,764 | 44,601,257 | 40,448,283 | 1,079,379 | 23,423,115 | 159,624,037 |
|  | 2015 | 14,720,643 | 16,009,811 | 15,339,435 | 4,677,741 | 45,542,914 | 40,952,070 | 1,094,295 | 23,831,211 | 162,168,121 |
|  | 2016 | 14,877,575 | 16,323,771 | 15,539,462 | 4,692,766 | 46,504,452 | 41,462,133 | 1,109,417 | 24,246,417 | 164,755,993 |
|  | 2017 | 15,036,180 | 16,643,887 | 15,742,098 | 4,707,840 | 47,486,292 | 41,978,548 | 1,124,748 | 24,668,858 | 167,388,449 |
|  | 2018 | 15,196,476 | 16,970,280 | 15,947,377 | 4,722,962 | 48,488,860 | 42,501,395 | 1,140,290 | 25,098,658 | 170,066,298 |
|  | 2019 | 15,358,480 | 17,303,075 | 16,155,332 | 4,738,132 | 49,512,596 | 43,030,754 | 1,156,048 | 25,535,946 | 172,790,363 |
|  | 2020 | 15,522,212 | 17,642,395 | 16,365,999 | 4,753,351 | 50,557,945 | 43,566,707 | 1,172,023 | 25,980,854 | 175,561,486 |
|  | 2021 | 15,687,689 | 17,988,370 | 16,579,413 | 4,768,619 | 51,625,365 | 44,109,335 | 1,188,219 | 26,433,513 | 178,380,523 |
|  | 2022 | 15,854,931 | 18,341,129 | 16,795,611 | 4,783,936 | 52,715,321 | 44,658,721 | 1,204,639 | 26,894,058 | 181,248,346 |
|  | 2023 | 16,023,955 | 18,700,807 | 17,014,627 | 4,799,302 | 53,828,289 | 45,214,950 | 1,221,286 | 27,362,628 | 184,165,843 |
|  | 2024 | 16,194,781 | 19,067,537 | 17,236,499 | 4,814,717 | 54,964,755 | 45,778,107 | 1,238,162 | 27,839,361 | 187,133,921 |
|  | 2025 | 16,367,429 | 19,441,460 | 17,461,265 | 4,830,183 | 56,125,215 | 46,348,278 | 1,255,272 | 28,324,400 | 190,153,501 |

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - HB2200 Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 830,210 | 1,188,766 | 1,317,287 | 305,662 | 2,839,765 | 2,855,142 | 59,701 | 1,479,884 | 10,876,416 |
|  | 2012 | 839,061 | 1,212,078 | 1,334,465 | 306,644 | 2,899,720 | 2,890,703 | 60,526 | 1,505,667 | 11,048,864 |
|  | 2013 | 831,412 | 1,212,298 | 1,325,600 | 301,474 | 2,904,770 | 2,869,744 | 60,172 | 1,502,520 | 11,007,990 |
|  | 2014 | 840,276 | 1,236,071 | 1,342,886 | 302,442 | 2,966,098 | 2,905,487 | 61,004 | 1,528,698 | 11,182,962 |
|  | 2015 | 849,233 | 1,260,311 | 1,360,397 | 303,413 | 3,028,721 | 2,941,675 | 61,847 | 1,555,333 | 11,360,931 |
|  | 2016 | 858,287 | 1,285,027 | 1,378,137 | 304,388 | 3,092,665 | 2,978,314 | 62,702 | 1,582,431 | 11,541,950 |
|  | 2017 | 867,437 | 1,310,227 | 1,396,108 | 305,366 | 3,157,960 | 3,015,409 | 63,568 | 1,610,001 | 11,726,076 |
|  | 2018 | 876,684 | 1,335,921 | 1,414,313 | 306,346 | 3,224,634 | 3,052,966 | 64,447 | 1,638,052 | 11,913,363 |
|  | 2019 | 886,030 | 1,362,119 | 1,432,756 | 307,330 | 3,292,715 | 3,090,991 | 65,337 | 1,666,591 | 12,103,870 |
|  | 2020 | 895,476 | 1,388,830 | 1,451,439 | 308,318 | 3,362,233 | 3,129,490 | 66,240 | 1,695,628 | 12,297,654 |
|  | 2021 | 905,022 | 1,416,066 | 1,470,366 | 309,308 | 3,433,219 | 3,168,468 | 67,155 | 1,725,171 | 12,494,776 |
|  | 2022 | 914,670 | 1,443,835 | 1,489,540 | 310,301 | 3,505,704 | 3,207,932 | 68,083 | 1,755,228 | 12,695,295 |
|  | 2023 | 924,421 | 1,472,150 | 1,508,964 | 311,298 | 3,579,719 | 3,247,887 | 69,024 | 1,785,809 | 12,899,272 |
|  | 2024 | 934,276 | 1,501,019 | 1,528,641 | 312,298 | 3,655,297 | 3,288,340 | 69,978 | 1,816,923 | 13,106,772 |
|  | 2025 | 944,236 | 1,530,455 | 1,548,574 | 313,301 | 3,732,471 | 3,329,296 | 70,945 | 1,848,578 | 13,317,857 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| Climate Impact ((Consumption + Losses) X CO2)) HB2200 Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 155,238,085 | 10,876,416 | 166,114,501 | 106,230,224 | 96.35 |
|  | 2012 | 157,702,733 | 11,048,864 | 168,751,597 | 107,916,646 | 97.88 |
|  | 2013 | 157,122,962 | 11,007,990 | 168,130,952 | 107,519,744 | 97.52 |
|  | 2014 | 159,624,037 | 11,182,962 | 170,806,999 | 109,231,076 | 99.07 |
|  | 2015 | 162,168,121 | 11,360,931 | 173,529,051 | 110,971,828 | 100.65 |
|  | 2016 | 164,755,993 | 11,541,950 | 176,297,944 | 112,742,535 | 102.26 |
|  | 2017 | 167,388,449 | 11,726,076 | 179,114,525 | 114,543,739 | 103.89 |
|  | 2018 | 170,066,298 | 11,913,363 | 181,979,661 | 116,375,993 | 105.55 |
|  | 2019 | 172,790,363 | 12,103,870 | 184,894,233 | 118,239,862 | 107.24 |
|  | 2020 | 175,561,486 | 12,297,654 | 187,859,141 | 120,135,921 | 108.96 |
|  | 2021 | 178,380,523 | 12,494,776 | 190,875,299 | 122,064,754 | 110.71 |
|  | 2022 | 181,248,346 | 12,695,295 | 193,943,640 | 124,026,958 | 112.49 |
|  | 2023 | 184,165,843 | 12,899,272 | 197,065,115 | 126,023,141 | 114.30 |
|  | 2024 | 187,133,921 | 13,106,772 | 200,240,693 | 128,053,923 | 116.14 |
|  | 2025 | 190,153,501 | 13,317,857 | 203,471,359 | 130,119,934 | 118.02 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction HB2200 vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | HB2200 | BAU | Delta | HB2200 | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 166,114,501 | 167,765,977 | 1,651,476 | 96.35 | 97.31 | 0.96 |
|  | 2012 | 168,751,597 | 170,429,257 | 1,677,660 | 97.88 | 98.85 | 0.97 |
|  | 2013 | 168,130,952 | 173,138,235 | 5,007,283 | 97.52 | 100.42 | 2.90 |
|  | 2014 | 170,806,999 | 173,138,235 | 2,331,236 | 99.07 | 100.42 | 1.35 |
|  | 2015 | 173,529,051 | 178,696,613 | 5,167,562 | 100.65 | 103.65 | 3.00 |
|  | 2016 | 176,297,944 | 181,547,714 | 5,249,771 | 102.26 | 105.30 | 3.05 |
|  | 2017 | 179,114,525 | 184,447,917 | 5,333,393 | 103.89 | 106.98 | 3.09 |
|  | 2018 | 181,979,661 | 187,398,113 | 5,418,453 | 105.55 | 108.70 | 3.14 |
|  | 2019 | 184,894,233 | 190,399,210 | 5,504,977 | 107.24 | 110.44 | 3.19 |
|  | 2020 | 187,859,141 | 193,452,134 | 5,592,993 | 108.96 | 112.21 | 3.24 |
|  | 2021 | 190,875,299 | 196,557,826 | 5,682,527 | 110.71 | 114.01 | 3.30 |
|  | 2022 | 193,943,640 | 199,717,246 | 5,773,606 | 112.49 | 115.84 | 3.35 |
|  | 2023 | 197,065,115 | 202,931,375 | 5,866,259 | 114.30 | 117.71 | 3.40 |
|  | 2024 | 200,240,693 | 206,201,208 | 5,960,515 | 116.14 | 119.60 | 3.46 |
|  | 2025 | 203,471,359 | 209,527,761 | 6,056,403 | 118.02 | 121.53 | 3.51 |

Estimated Cost Savings Associated with Reductions in Consumption and Peak Demand

|  | 2010 Electricity Consumption (kwh)** |  | Price (per kwh) |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| EDC | Residential | Commercial | Industrial | Total | Peak Load | Residential | Commercial | Industrial |  |  |  |
| Duquesne | 4,252,636,310 | 6,782,533,800 | 3,176,632,810 | 14,211,802,920 | 2,890 | $ 0.125 | $ 0.120 | $ 0.105 |  |  |  |
| Met-Ed | 5,651,232,800 | 4,762,128,790 | 4,032,205,830 | 14,445,567,420 | 2,825 | $ 0.145 | $ 0.140 | $ 0.125 |  |  |  |
| Penelec | 4,541,799,310 | 5,190,247,590 | 4,655,657,620 | 14,387,704,520 | 2,524 | $ 0.140 | $ 0.135 | $ 0.115 |  |  |  |
| Penn Power | 1,706,494,990 | 1,427,734,990 | 1,643,389,180 | 4,777,619,160 | 1,042 | $ 0.140 | $ 0.135 | $ 0.115 |  |  |  |
| PECO | 13,622,155,830 | 8,980,529,130 | 16,748,003,820 | 39,350,688,780 | 8,549 | $ 0.160 | $ 0.155 | $ 0.115 |  |  |  |
| PPL | 14,554,732,260 | 13,893,139,840 | 9,576,452,360 | 38,024,324,460 | 7,141 | $ 0.140 | $ 0.135 | $ 0.125 |  |  |  |
| West Penn | 7,338,168,130 | 5,047,907,280 | 8,241,191,960 | 20,627,267,370 | 3,838 | $ 0.123 | $ 0.118 | $ 0.095 |  |  |  |
|  | Energy Cost Savings | Capacity Cost Savings | Market Price Impact of Efficiency* | Market Impact of Peak Load* | Overall Savings |
| EDC | In 2011 and 2012 | Additional in 2013 | Total in 2013 and after | In 2013 and after | In 2011 and 2012 | Additional in 2013 | Total in 2013 and after | In 2013 and after | In 2011 and 2012 | Additional in 2013 | Total for 2013 and after |
| Duquesne | $ 16,790,300 | $ 33,580,601 | $ 50,370,901 | $ 1,364,712 | $ 7,034,842 | $6,892,724 | $ 13,927,567 | $ 79,349 | $ 23,825,143 | $ 41,917,386 | $ 65,742,529 |
| Met-Ed | $ 19,901,525 | $ 39,803,050 | $ 59,704,575 | $ 8,004,108 | $ 7,150,556 | $7,006,100 | $ 14,156,656 | $ 465,383 | $ 27,052,081 | $ 55,278,642 | $ 82,330,723 |
| Penelec | $ 18,719,360 | $ 37,438,719 | $ 56,158,079 | $ 7,151,281 | $ 7,121,914 | $6,978,037 | $ 14,099,950 | $ 415,797 | $ 25,841,273 | $ 51,983,834 | $ 77,825,107 |
| Penn Power | $ 6,206,433 | $ 12,412,866 | $ 18,619,298 | $ 2,952,312 | $ 2,364,921 | $2,317,145 | $ 4,682,067 | $ 171,656 | $ 8,571,354 | $ 17,853,979 | $ 26,425,333 |
| PECO | $ 54,975,474 | $ 109,950,948 | $ 164,926,422 | $ 24,221,989 | $19,478,591 | $19,085,084 | $ 38,563,675 | $ 1,408,341 | $ 74,454,065 | $ 154,666,361 | $ 229,120,426 |
| PPL | $ 51,102,929 | $ 102,205,859 | $ 153,308,788 | $ 20,232,685 | $18,822,041 | $18,441,797 | $ 37,263,838 | $ 1,176,390 | $ 69,924,970 | $ 142,056,731 | $ 211,981,701 |
| West Penn | $ 22,811,610 | $ 45,623,220 | $ 68,434,829 | $ 10,874,253 | $10,210,497 | $10,004,225 | $ 20,214,722 | $ 632,263 | $ 33,022,107 | $ 67,133,960 | $ 100,156,067 |
| Total | $190,507,631 | $ 381,015,262 | $ 571,522,893 | $ 74,801,339 | $72,183,362 | $70,725,113 | $142,908,475 | $ 4,349,180 | $262,690,993 | $ 530,890,893 | $ 793,581,887 |
| * Market impacts of $.0005/kwh and $.005/kw for all energy consumed |
| Note: Data is not inclusive of UGI. UGI was exempted from Act 129 requirements. |
| ** Electricity consumption in 2010 is 2007 actual plus 1%/year increase through 2010. |
| Electricity consumption in 2012 is the same as in 2010: 1% reduction plus 1% growth. |

Electricity 2 : Reduced Load Growth Work Plan for Potential GHG Reduction Measure

Strategy Name: Reduced Load Growth

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This initiative identifies the carbon emissions benefits associated with curbing the rate of growth in electricity consumption in PA.  This strategy builds upon the conservation requirements of Act 129 of 2008, which requires 1.0% and 2.0% reductions in electricity consumption from 2010, by 2011 and 2013, respectively.  Act 129 also requires the PUC to assess the potential for additional cost-effective reductions.  The scenario developed in this work plan builds upon Act 129 by requiring biennial reductions in electricity consumption equal to 1.5% per  period (.75% per year), beginning in 2015 and carrying through 2025.  These reductions are calculated from the previous years estimated consumption.  The result is a net reduction in greenhouse gas emissions of approximately 29.22 MMTCO2 (92.31 MMTCO2 from the combination of Act 129 and this work plan).

Please note that this analysis does not include the very modest consumption and associated system losses from municipalities that are service providers or the rural electric cooperatives.

Other Involved Agencies: PUC

Possible New Measure(s): As required in Act 129, a study must be undertaken to identify the full suite of cost-effective measures that should be given consideration.  A report from the American Council for an Energy Efficient Economy (ACEEE) is being drafted for the PUC and DEP and should serve well to inform this process.

Potential GHG Reduction: 29.22 MMTCO2 additional beyond Act 129 reductions (92.31 MMTCO2 total)

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under two different scenarios; Reduced Load Growth (RLG) and business as usual (BAU).  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates of consumption were made beginning with the last year of reported data to the PUC (2006).

- A similar set of projections was made that incorporated the load curtailments as required for in Act 129 coupled with a series of 1.50% reductions occurring in even odd years from 2015 through 2025.  1.5% is approximately equal to (slightly less than) the five-year average rate of growth for all of the EDCs.

- The sum total MWh for consumption and system losses for each scenario (RLG and BAU) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) for electricity produced in PA.  The emissions rates were calculated from generation and emissions data reported to the EIA.

- The difference between these two scenarios yields the actual projected reduction in CO2 emissions in year 2025.

  - The result is a cumulative effect curtailing load growth to less than would be the case under the projected BAU scenario in 2016.

  - This scenario facilitates reductions in electricity consumption while still realizing growth in electricity demand.  The projected emissions reductions from this work plan yield an additional 12.71 MMTCO2 beyond that which is anticipated via Act 129.

A series of tables summarizing the estimated CO2 reductions potential of this initiative are included in this work plan immediately following “Potential Overlap.”

Assumptions:

- Adequate cost-effective reductions exist or will exist, through year 2025, to provide the estimated 25 million MWh of curtailment as compared to the unchecked, projected rate of growth in electricity consumption.

- No reductions would be required if not supported through an analysis of cost-effective measures.

Economic Cost:

- Cost to DEP - None

- Cost to the Commonwealth – Act 129 requires the PUC to hire a program administrator to oversee this process and to provide assessments as to the cost-effectiveness and level of additional reductions that may be possible within PA.  The cost for this service is unknown.

- Cost to regulated community or consumer – Not quantified, as of yet.  Short-term capital costs may be experienced, depending on a host of issues but short and long-term savings are anticipated.  Requires detailed analysis.

- Are there Federal funds available? – Federal funding is not required nor is it available at this time.  Limited assistance may be available through the U.S. DOE State Energy Plan but this would most likely be limited to policy analysis and possibly technical support.

- Do these costs fund other programs? No.  Any costs are expected to result in changes to consumer behavior.

- Are cost savings realized from this initiative? Cost savings are expected but this does require a detailed analysis.  The assumption is that reductions will only be required such that can be sustained through cost-effective measures.

Implementation Steps:  The following, and other, considerations should be examined as policy tools to support this measure:

- Act 129 provides the PUC with the necessary authority to require additional cost-effective reductions in electricity consumption.

- An assessment of electricity consumption reduction potential is necessary to determine if the requirements suggested within this work plan conform to Act 129 requisites.  Such a study is underway by ACEEE.

- A legislative amendment to the AEPS establishing a dedicated market share for energy efficiency credits (new tier or carve out) might facilitate achieving this reduction measure by rewarding over-compliance and providing a cost-effective manner to achieve greater reductions.

- Require electric distribution companies to invest in demand side response initiatives, including rebates to consumers.

- Require that all cost-effective supply side and demand side response initiatives have been identified and acted upon before approvals for new generation are granted.  In a February 5, 2007 press release http://www.aceee.org/press/e072pr.htm ACEEE reported that, “States from Texas to Vermont are finding energy efficiency resources available at less than 4 cents per kilowatt-hour, compared to the expected cost of power from new plants of 5 to 10 cents.”

- Implementing advanced building standards for the commercial, institutional, state and municipal government sectors that establish minimum green building practices and energy efficiency standards.

- Coupled with the advanced building standard, consider a requirement that all commercial, institutional, state and municipal government buildings perform annual benchmarking, similar to that established by the U.S. EPA that documents the gains or losses in energy consumption on a per square foot basis, based on the type of activity occurring.  This information is publicly accessible.  It educates and encourages building owners and operators to achieve higher performance.

- Work with neighboring states on establishing regional efficiency standards for appliances and electronics where none currently exist or where minimum standards are less than optimal.

- Establish an aggressive phase-out of incandescent lights and/or establish a pricing/tax structure that preferentially treats lighting with a higher lumens to watts ratio.

- Rate decoupling

Potential Overlap:

- Act 129 Work Plan

- Stabilized Load Growth Work Plan

| Reduced Load Growth (RLG) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,390,891 | 15,100,962 | 14,853,338 | 4,712,411 | 42,701,585 | 39,747,416 | 1,056,322 | 22,675,162 | 155,238,085 |
|  | 2012 | 14,544,307 | 15,397,098 | 15,047,027 | 4,727,547 | 43,603,135 | 40,242,475 | 1,070,919 | 23,070,226 | 157,702,733 |
|  | 2013 | 14,411,732 | 15,399,897 | 14,947,075 | 4,647,840 | 43,679,074 | 39,950,697 | 1,064,671 | 23,022,012 | 157,122,998 |
|  | 2014 | 14,565,371 | 15,701,895 | 15,141,986 | 4,662,769 | 44,601,261 | 40,448,287 | 1,079,384 | 23,423,120 | 159,624,073 |
|  | 2015 | 14,504,926 | 15,785,458 | 15,117,314 | 4,606,577 | 44,909,435 | 40,357,324 | 1,078,515 | 23,493,594 | 157,309,059 |
|  | 2016 | 14,659,559 | 16,095,017 | 15,314,446 | 4,621,373 | 45,857,599 | 40,859,979 | 1,093,419 | 23,902,918 | 162,404,309 |
|  | 2017 | 14,600,119 | 16,050,880 | 15,261,987 | 4,454,919 | 46,130,751 | 41,079,853 | 889,355 | 23,942,019 | 163,919,929 |
|  | 2018 | 14,755,766 | 16,221,994 | 15,424,690 | 4,502,412 | 46,622,536 | 41,517,792 | 898,836 | 24,197,257 | 164,141,283 |
|  | 2019 | 14,697,352 | 16,179,210 | 15,373,407 | 4,334,690 | 46,903,843 | 41,744,679 | 692,697 | 24,239,495 | 164,165,373 |
|  | 2020 | 14,854,035 | 16,351,692 | 15,537,298 | 4,380,900 | 47,403,870 | 42,189,706 | 700,082 | 24,497,905 | 165,915,488 |
|  | 2021 | 14,796,669 | 16,310,291 | 15,487,215 | 4,211,883 | 47,693,506 | 42,423,756 | 491,824 | 24,543,348 | 165,958,493 |
|  | 2022 | 14,954,411 | 16,484,170 | 15,652,320 | 4,256,784 | 48,201,952 | 42,876,022 | 497,068 | 24,804,997 | 167,727,723 |
|  | 2023 | 14,898,114 | 16,444,181 | 15,603,463 | 4,086,444 | 48,500,096 | 43,117,388 | 286,646 | 24,853,714 | 167,790,048 |
|  | 2024 | 15,056,938 | 16,619,487 | 15,769,807 | 4,130,008 | 49,017,140 | 43,577,049 | 289,702 | 25,118,672 | 169,578,803 |
|  | 2025 | 15,001,735 | 16,580,942 | 15,722,203 | 3,958,316 | 49,323,975 | 43,825,889 | 77,069 | 25,170,733 | 169,660,862 |

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - Reduced Load Growth (RLG) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | ,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 830,210 | 1,188,766 | 1,317,287 | 305,662 | 2,839,765 | 2,855,142 | 59,701 | 1,479,884 | 10,876,416 |
|  | 2012 | 839,061 | 1,212,078 | 1,334,465 | 306,644 | 2,899,720 | 2,890,703 | 60,526 | 1,505,667 | 11,048,864 |
|  | 2013 | 831,412 | 1,212,298 | 1,325,600 | 301,474 | 2,904,770 | 2,869,744 | 60,173 | 1,502,521 | 11,007,993 |
|  | 2014 | 840,276 | 1,236,072 | 1,342,886 | 302,442 | 2,966,098 | 2,905,487 | 61,004 | 1,528,699 | 11,182,965 |
|  | 2015 | 836,789 | 1,242,650 | 1,340,698 | 298,797 | 2,986,593 | 2,898,953 | 60,955 | 1,533,298 | 11,198,734 |
|  | 2016 | 845,710 | 1,267,019 | 1,358,181 | 299,757 | 3,049,648 | 2,935,060 | 61,797 | 1,560,013 | 11,377,184 |
|  | 2017 | 842,280 | 1,263,544 | 1,353,529 | 288,960 | 3,067,813 | 2,950,854 | 50,264 | 1,562,564 | 11,379,810 |
|  | 2018 | 851,260 | 1,277,015 | 1,367,958 | 292,041 | 3,100,518 | 2,982,312 | 50,800 | 1,579,222 | 11,501,126 |
|  | 2019 | 847,890 | 1,273,647 | 1,363,410 | 281,162 | 3,119,226 | 2,998,610 | 39,150 | 1,581,979 | 11,505,073 |
|  | 2020 | 856,929 | 1,287,225 | 1,377,945 | 284,159 | 3,152,479 | 3,030,577 | 39,567 | 1,598,844 | 11,627,725 |
|  | 2021 | 853,619 | 1,283,965 | 1,373,503 | 273,196 | 3,171,741 | 3,047,389 | 27,797 | 1,601,810 | 11,633,021 |
|  | 2022 | 862,720 | 1,297,653 | 1,388,146 | 276,109 | 3,205,553 | 3,079,877 | 28,093 | 1,618,886 | 11,757,037 |
|  | 2023 | 859,472 | 1,294,505 | 1,383,813 | 265,060 | 3,225,381 | 3,097,215 | 16,201 | 1,622,066 | 11,763,712 |
|  | 2024 | 868,634 | 1,308,306 | 1,398,565 | 267,886 | 3,259,766 | 3,130,233 | 16,373 | 1,639,358 | 11,889,121 |
|  | 2025 | 865,450 | 1,305,271 | 1,394,343 | 256,749 | 3,280,171 | 3,148,108 | 4,356 | 1,642,756 | 11,897,204 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| Climate Impact ((Consumption + Losses) X CO2)) (RLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 155,238,085 | 10,876,416 | 166,114,501 | 106,230,224 | 96.35 |
|  | 2012 | 157,702,733 | 11,048,864 | 168,751,597 | 107,916,646 | 97.88 |
|  | 2013 | 157,122,998 | 11,007,993 | 168,130,991 | 107,519,769 | 97.52 |
|  | 2014 | 159,624,073 | 11,182,965 | 170,807,038 | 109,231,101 | 99.07 |
|  | 2015 | 157,309,059 | 11,198,734 | 168,507,793 | 107,760,733 | 97.74 |
|  | 2016 | 162,404,309 | 11,377,184 | 173,781,494 | 111,133,265 | 100.80 |
|  | 2017 | 163,919,929 | 11,379,810 | 175,299,739 | 112,104,183 | 101.68 |
|  | 2018 | 164,141,283 | 11,501,126 | 175,642,409 | 112,323,320 | 101.88 |
|  | 2019 | 164,165,373 | 11,505,073 | 175,670,446 | 112,341,250 | 101.89 |
|  | 2020 | 165,915,488 | 11,627,725 | 177,543,212 | 113,538,884 | 102.98 |
|  | 2021 | 165,958,493 | 11,633,021 | 177,591,514 | 113,569,773 | 103.01 |
|  | 2022 | 167,727,723 | 11,757,037 | 179,484,760 | 114,780,504 | 104.11 |
|  | 2023 | 167,790,048 | 11,763,712 | 179,553,759 | 114,824,629 | 104.15 |
|  | 2024 | 169,578,803 | 11,889,121 | 181,467,924 | 116,048,738 | 105.26 |
|  | 2025 | 169,660,862 | 11,897,204 | 181,558,066 | 116,106,383 | 105.31 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction RLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | RLG | BAU | Delta | RLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 166,114,501 | 167,765,977 | 1,651,476 | 96.35 | 97.31 | 0.96 |
|  | 2012 | 168,751,597 | 170,429,257 | 1,677,660 | 97.88 | 98.85 | 0.97 |
|  | 2013 | 168,130,991 | 173,138,235 | 5,007,244 | 97.52 | 100.42 | 2.90 |
|  | 2014 | 170,807,038 | 175,893,740 | 5,086,702 | 99.07 | 102.02 | 2.95 |
|  | 2015 | 168,507,793 | 178,696,613 | 10,188,821 | 97.74 | 103.65 | 5.91 |
|  | 2016 | 173,781,494 | 181,547,714 | 7,766,220 | 100.80 | 105.30 | 4.50 |
|  | 2017 | 175,299,739 | 184,447,917 | 9,148,179 | 101.68 | 106.98 | 5.31 |
|  | 2018 | 175,642,409 | 187,398,113 | 11,755,705 | 101.88 | 108.70 | 6.82 |
|  | 2019 | 175,670,446 | 190,399,210 | 14,728,764 | 101.89 | 110.44 | 8.54 |
|  | 2020 | 177,543,212 | 193,452,134 | 15,908,921 | 102.98 | 112.21 | 9.23 |
|  | 2021 | 177,591,514 | 196,557,826 | 18,966,312 | 103.01 | 114.01 | 11.00 |
|  | 2022 | 179,484,760 | 199,717,246 | 20,232,487 | 104.11 | 115.84 | 11.74 |
|  | 2023 | 179,553,759 | 202,931,375 | 23,377,615 | 104.15 | 117.71 | 13.56 |
|  | 2024 | 181,467,924 | 206,201,208 | 24,733,283 | 105.26 | 119.60 | 14.35 |
|  | 2025 | 181,558,066 | 209,527,761 | 27,969,696 | 105.31 | 121.53 | 16.22 |

Electricity 3: Stabilized Load Growth Work Plan for Potential GHG Reduction Measure

Strategy Name: Stabilized Load Growth

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  This measure builds upon the very modest reductions required via Act 129 of 2008.  Act 129 requires reductions in consumption of 1.0% by 2011 and 2.0% by 2013, measured against 2010 consumption.  The Stabilized Load Growth (SLG) scenario further investigates the potential impact of annual consumption reductions of .75% per year in the period 2014 through the end of 2017 followed by a rate of consumption that is held static from 2018 through 2025.  The annual reductions in subsequent years would be based on the previous year’s consumption figures and would allow a subsequent one year “true-up” for electricity distribution companies to achieve stabilized consumption levels. These reductions are less than what would be achieved as compared to the Reduced Load work plan in that the Reduced Load work plan scenario continues to require additional reductions in consumption through 2025.  It is estimated that the Stabilized Load Growth work plan realizes a reduction in gross-level GHG emissions of 26.05 MMTCO2.  The net total, subtracting out the impact of Act 129 reductions (8.01 MMTCO2) is 18.04 MMTCO2.

Please note that this analysis does not include the very modest consumption and associated system losses from municipalities that are service providers or the rural electric cooperatives.

Other Involved Agencies: PUC

Possible New Measure(s): As required in Act 129, a study must be undertaken to identify the full suite of cost-effective measures that should be given consideration.  A report from the American Council for an Energy Efficient Economy (ACEEE) is being drafted for the PUC and DEP and should serve well to inform this process.

Potential GHG Reduction: 18.04 MMTCO2 additional to Act 129 reductions (26.05 MMTCO2 total for this measure)

The following steps were used in calculating the emissions reduction:

- Consumption and system loss data was obtained for each of the eight electric distribution companies (EDCs) in PA for years 2001 through 2006.  This data was obtained from the PUC’s Electric Power Annual Outlook reports.

- Average rates of consumption and system losses were calculated for each EDC under two different scenarios; Stabilized Load Growth (SLG) that includes Act 129 reductions and business as usual (BAU) that assumes no reductions are realized.  Average growth rates in consumption ranged from 0.32% to 2.11%.  Average rates for systems losses, by EDC, ranged from 5.65% to 8.87%.

- Projections for BAU rates of consumption were made beginning with the last year of reported data to the PUC (2006).

- Under the Stabilized Load Growth scenario, consumption in years 2019 through 2025 is held equal to that in 2018 which represents a forecasted sustained, annual reduction of approximately 1.55%, as compared to the BAU scenario.

- The sum total MWh for consumption and system losses for each scenario (SLG and BAU) was then multiplied by a five-year (2000 through 2004) statewide average CO2 emission factor (1,279 pounds of CO2 per MWh) for electricity produced in PA.  The emissions rates were calculated from generation and emissions data reported to the EIA.

- The difference between these two scenarios yields the anticipated reduction in CO2 emissions in year 2025 of 12.47 MMTCO2 (incremental) beyond those provided solely by Act 129 or a total of 15.98 MMTCO2 in association with Act 129 implementation.

A series of tables summarizing the estimated CO2 reductions potential of this initiative are included in this work plan immediately following “Potential Overlap.”

Assumptions:

- Adequate cost-effective reductions exist or will exist, through year 2025, to provide the approximate 25 million MWh of curtailment, as compared to the unchecked, projected rate of growth in electricity consumption.

- No reductions would be required if not supported through an analysis of cost-effective measures.

Economic Cost:

- Cost to DEP - None

- Cost to the Commonwealth – Act 129 requires the PUC to hire a program administrator to oversee this process and to provide assessments as to the cost-effectiveness and level of additional reductions that may be possible within PA.  The cost for this service is unknown.  It is further assumed that the PUC would perform similar services to oversee the reductions that may be required if such a Stabilized Load Growth initiative were to be implemented.

- Cost to regulated community or consumer – Not quantified, as of yet.  Short-term capital costs may be experienced, depending on a host of issues but short and long-term savings are anticipated.  Requires detailed analysis.

- Are there Federal funds available? – Federal funding is not required nor is it available at this time.  Limited assistance may be available through the U.S. DOE State Energy Plan but this would most likely be limited to policy analysis and possibly technical support.

- Do these costs fund other programs? No.  Any costs are expected to result in changes to consumer behavior.

- Are cost savings realized from this initiative? Cost savings are expected but this does require a detailed analysis.  The assumption is that reductions will only be required such that can be sustained through cost-effective measures.

Implementation Steps:  The following, and other, considerations should be examined as policy tools to support this measure:

- Act 129 provides the PUC with the necessary authority to require additional cost-effective reductions in electricity consumption.

- An assessment of electricity consumption reduction potential is necessary to determine if the requirements suggested within this work plan conform to Act 129 requisites.  Such a study is underway by the ACEEE.

- The PUC may have the authority within Act 129 of 2008 that would facilitate realization of this reduction measure.

- A legislative amendment to the AEPS establishing a dedicated market share for energy efficiency credits (new tier or carve out) might facilitate achieving this reduction measure by rewarding over-compliance and providing a cost-effective manner to achieve greater reductions.

- Require electric distribution companies to invest in demand side response initiatives, including rebates to consumers.

- Require that all cost-effective supply side and demand side measures have been identified and acted upon before approvals for new generation are granted.  In a February 5, 2007 press release http://www.aceee.org/press/e072pr.htm ACEEE reported that, “States from Texas to Vermont are finding energy efficiency resources available at less than 4 cents per kilowatt-hour, compared to the expected cost of power from new plants of 5 to 10 cents.”

- Implementing advanced building standards for the commercial, institutional, state and municipal government sectors that establish minimum green building practices and energy efficiency standards.

- Coupled with the advanced building standard, consider a requirement that all commercial, institutional, state and municipal government buildings perform annual benchmarking, similar to that established by the U.S. EPA that documents the gains or losses in energy consumption on a per square foot basis, based on the type of activity occurring.  This information is publicly accessible.  It educates and encourages building owners and operators to achieve higher performance.

- Work with neighboring states on establishing regional efficiency standards for appliances and electronics where none currently exist or where minimum standards are less than optimal.

- Establish an aggressive phase-out of incandescent lights and/or establish a pricing/tax structure that preferentially treats lighting with a higher lumens to watts ratio.

- Rate decoupling

Potential Overlap:

- Act 129 Work Plan

- Reduced Load Growth Work Plan

| Stabilized Load Growth (SLG) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,237,575 | 14,807,644 | 14,660,236 | 4,697,171 | 41,809,943 | 39,253,571 | 1,041,780 | 22,283,008 | 152,790,928 |
|  | 2012 | 14,389,357 | 15,098,028 | 14,851,407 | 4,712,258 | 42,692,668 | 39,742,478 | 1,056,176 | 22,671,240 | 155,213,613 |
|  | 2013 | 14,093,757 | 14,658,068 | 14,512,148 | 4,649,720 | 41,387,616 | 38,857,065 | 1,031,252 | 22,057,923 | 151,247,549 |
|  | 2014 | 14,244,006 | 14,945,518 | 14,701,388 | 4,664,655 | 42,261,425 | 39,341,034 | 1,045,503 | 22,442,233 | 153,645,763 |
|  | 2015 | 14,030,346 | 14,721,336 | 14,480,867 | 4,594,686 | 41,627,503 | 38,750,919 | 1,029,821 | 22,105,600 | 151,330,748 |
|  | 2016 | 14,179,919 | 15,010,027 | 14,669,699 | 4,609,444 | 42,506,376 | 39,233,565 | 1,044,052 | 22,490,741 | 153,743,823 |
|  | 2017 | 13,967,220 | 14,784,877 | 14,449,654 | 4,540,302 | 41,868,781 | 38,645,062 | 1,028,391 | 22,153,380 | 151,437,665 |
|  | 2018 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2019 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2020 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2021 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2022 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2023 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2024 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |
|  | 2025 | 14,116,120 | 15,074,814 | 14,638,078 | 4,554,886 | 42,752,748 | 39,126,390 | 1,042,602 | 22,539,353 | 153,844,992 |

| Consumption - Business as Usual (BAU) Scenario |
| --- |
|  | Average Growth Rate per EDC |  |
|  | 1.07% | 1.96% | 1.30% | 0.32% | 2.11% | 1.25% | 1.38% | 1.74% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| Consumption (MWh) by Compliance Year | 2007 | 13,931,078 | 14,110,681 | 14,243,800 | 4,699,190 | 39,666,440 | 38,204,688 | 1,009,857 | 21,371,462 | 147,237,195 |
|  | 2008 | 14,079,593 | 14,387,398 | 14,429,540 | 4,714,284 | 40,503,909 | 38,680,531 | 1,023,812 | 21,743,813 | 149,562,879 |
|  | 2009 | 14,229,691 | 14,669,541 | 14,617,703 | 4,729,426 | 41,359,060 | 39,162,301 | 1,037,960 | 22,122,651 | 151,928,332 |
|  | 2010 | 14,381,389 | 14,957,216 | 14,808,319 | 4,744,617 | 42,232,266 | 39,650,071 | 1,052,303 | 22,508,089 | 154,334,271 |
|  | 2011 | 14,534,704 | 15,250,534 | 15,001,421 | 4,759,857 | 43,123,907 | 40,143,917 | 1,066,845 | 22,900,242 | 156,781,428 |
|  | 2012 | 14,689,654 | 15,549,603 | 15,197,041 | 4,775,146 | 44,034,374 | 40,643,914 | 1,081,587 | 23,299,229 | 159,270,547 |
|  | 2013 | 14,846,256 | 15,854,537 | 15,395,212 | 4,790,484 | 44,964,063 | 41,150,138 | 1,096,533 | 23,705,166 | 161,802,389 |
|  | 2014 | 15,004,527 | 16,165,451 | 15,595,967 | 4,805,871 | 45,913,380 | 41,662,667 | 1,111,686 | 24,118,176 | 164,377,726 |
|  | 2015 | 15,164,486 | 16,482,463 | 15,799,340 | 4,821,308 | 46,882,740 | 42,181,580 | 1,127,048 | 24,538,382 | 166,997,346 |
|  | 2016 | 15,326,149 | 16,805,691 | 16,005,365 | 4,836,794 | 47,872,566 | 42,706,956 | 1,142,623 | 24,965,909 | 169,662,052 |
|  | 2017 | 15,489,536 | 17,135,257 | 16,214,076 | 4,852,330 | 48,883,290 | 43,238,875 | 1,158,412 | 25,400,885 | 172,372,662 |
|  | 2018 | 15,654,665 | 17,471,287 | 16,425,509 | 4,867,916 | 49,915,353 | 43,777,420 | 1,174,420 | 25,843,439 | 175,130,010 |
|  | 2019 | 15,821,555 | 17,813,906 | 16,639,699 | 4,883,551 | 50,969,206 | 44,322,672 | 1,190,649 | 26,293,704 | 177,934,944 |
|  | 2020 | 15,990,223 | 18,163,244 | 16,856,683 | 4,899,238 | 52,045,308 | 44,874,716 | 1,207,103 | 26,751,814 | 180,788,329 |
|  | 2021 | 16,160,690 | 18,519,433 | 17,076,495 | 4,914,974 | 53,144,130 | 45,433,635 | 1,223,784 | 27,217,905 | 183,691,047 |
|  | 2022 | 16,332,974 | 18,882,607 | 17,299,175 | 4,930,761 | 54,266,152 | 45,999,516 | 1,240,695 | 27,692,117 | 186,643,996 |
|  | 2023 | 16,507,094 | 19,252,903 | 17,524,758 | 4,946,599 | 55,411,862 | 46,572,444 | 1,257,840 | 28,174,591 | 189,648,091 |
|  | 2024 | 16,683,071 | 19,630,461 | 17,753,282 | 4,962,488 | 56,581,762 | 47,152,509 | 1,275,222 | 28,665,471 | 192,704,264 |
|  | 2025 | 16,860,924 | 20,015,422 | 17,984,787 | 4,978,427 | 57,776,361 | 47,739,798 | 1,292,844 | 29,164,903 | 195,813,466 |

| System Losses - Stabilized Load Growth (SLG) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 821,365 | 1,165,675 | 1,300,162 | 304,674 | 2,780,469 | 2,819,668 | 58,879 | 1,454,290 | 10,705,181 |
|  | 2012 | 830,122 | 1,188,535 | 1,317,116 | 305,652 | 2,839,172 | 2,854,787 | 59,693 | 1,479,628 | 10,874,704 |
|  | 2013 | 813,068 | 1,153,900 | 1,287,028 | 301,596 | 2,752,383 | 2,791,186 | 58,284 | 1,439,600 | 10,597,046 |
|  | 2014 | 821,736 | 1,176,529 | 1,303,811 | 302,565 | 2,810,493 | 2,825,951 | 59,089 | 1,464,682 | 10,764,856 |
|  | 2015 | 809,410 | 1,158,881 | 1,284,254 | 298,026 | 2,768,336 | 2,783,562 | 58,203 | 1,442,711 | 10,603,383 |
|  | 2016 | 818,039 | 1,181,607 | 1,301,001 | 298,983 | 2,826,783 | 2,818,231 | 59,007 | 1,467,847 | 10,771,500 |
|  | 2017 | 805,768 | 1,163,883 | 1,281,486 | 294,499 | 2,784,381 | 2,775,958 | 58,122 | 1,445,830 | 10,609,927 |
|  | 2018 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2019 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2020 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2021 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2022 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2023 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2024 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |
|  | 2025 | 814,359 | 1,186,707 | 1,298,197 | 295,445 | 2,843,167 | 2,810,533 | 58,925 | 1,471,020 | 10,778,352 |

| System Losses - Business as Usual (BAU) Scenario |
| --- |
|  | Average System Loss Rate per EDC |  |
|  | 5.77% | 7.87% | 8.87% | 6.49% | 6.65% | 7.18% | 5.65% | 6.53% |  |
|  | Duquesne | MetEd | Penelec | PennPower | PECO | PPL | UGI | West Penn | Total MWh |
| System Losses (MWh) by Compliance Year | 2007 | 803,683 | 1,110,810 | 1,263,229 | 304,805 | 2,637,920 | 2,744,325 | 57,075 | 1,394,798 | 10,316,645 |
|  | 2008 | 812,251 | 1,132,593 | 1,279,702 | 305,784 | 2,693,614 | 2,778,506 | 57,863 | 1,419,100 | 10,479,412 |
|  | 2009 | 820,910 | 1,154,804 | 1,296,390 | 306,766 | 2,750,484 | 2,813,112 | 58,663 | 1,443,824 | 10,644,952 |
|  | 2010 | 829,662 | 1,177,450 | 1,313,295 | 307,751 | 2,808,554 | 2,848,150 | 59,474 | 1,468,980 | 10,813,315 |
|  | 2011 | 838,507 | 1,200,540 | 1,330,420 | 308,740 | 2,867,850 | 2,883,624 | 60,296 | 1,494,573 | 10,984,550 |
|  | 2012 | 847,446 | 1,224,083 | 1,347,769 | 309,731 | 2,928,399 | 2,919,540 | 61,129 | 1,520,613 | 11,158,709 |
|  | 2013 | 856,480 | 1,248,088 | 1,365,344 | 310,726 | 2,990,226 | 2,955,903 | 61,973 | 1,547,106 | 11,335,846 |
|  | 2014 | 865,611 | 1,272,564 | 1,383,148 | 311,724 | 3,053,358 | 2,992,719 | 62,830 | 1,574,061 | 11,516,014 |
|  | 2015 | 874,839 | 1,297,519 | 1,401,184 | 312,726 | 3,117,822 | 3,029,993 | 63,698 | 1,601,486 | 11,699,268 |
|  | 2016 | 884,165 | 1,322,964 | 1,419,456 | 313,730 | 3,183,648 | 3,067,732 | 64,578 | 1,629,388 | 11,885,662 |
|  | 2017 | 893,591 | 1,348,908 | 1,437,966 | 314,738 | 3,250,864 | 3,105,941 | 65,471 | 1,657,777 | 12,075,255 |
|  | 2018 | 903,117 | 1,375,360 | 1,456,717 | 315,749 | 3,319,499 | 3,144,626 | 66,375 | 1,686,660 | 12,268,104 |
|  | 2019 | 912,745 | 1,402,332 | 1,475,713 | 316,763 | 3,389,583 | 3,183,793 | 67,293 | 1,716,046 | 12,464,267 |
|  | 2020 | 922,475 | 1,429,832 | 1,494,956 | 317,780 | 3,461,147 | 3,223,447 | 68,223 | 1,745,944 | 12,663,805 |
|  | 2021 | 932,310 | 1,457,872 | 1,514,451 | 318,801 | 3,534,221 | 3,263,595 | 69,165 | 1,776,364 | 12,866,779 |
|  | 2022 | 942,249 | 1,486,461 | 1,534,199 | 319,825 | 3,608,838 | 3,304,244 | 70,121 | 1,807,313 | 13,073,250 |
|  | 2023 | 952,294 | 1,515,611 | 1,554,205 | 320,852 | 3,685,031 | 3,345,399 | 71,090 | 1,838,801 | 13,283,284 |
|  | 2024 | 962,446 | 1,545,333 | 1,574,472 | 321,883 | 3,762,832 | 3,387,066 | 72,073 | 1,870,838 | 13,496,943 |
|  | 2025 | 972,706 | 1,575,638 | 1,595,004 | 322,917 | 3,842,276 | 3,429,252 | 73,068 | 1,903,433 | 13,714,295 |

| Climate Impact ((Consumption + Losses) X CO2)) (SLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 152,790,928 | 10,705,181 | 163,496,109 | 104,555,762 | 94.83 |
|  | 2012 | 155,213,613 | 10,874,704 | 166,088,317 | 106,213,479 | 96.34 |
|  | 2013 | 151,247,549 | 10,597,046 | 161,844,595 | 103,499,619 | 93.87 |
|  | 2014 | 153,645,763 | 10,764,856 | 164,410,619 | 105,140,591 | 95.36 |
|  | 2015 | 151,330,748 | 10,603,383 | 161,934,132 | 103,556,877 | 93.93 |
|  | 2016 | 153,743,823 | 10,771,500 | 164,515,322 | 105,207,549 | 95.42 |
|  | 2017 | 151,437,665 | 10,609,927 | 162,047,593 | 103,629,435 | 93.99 |
|  | 2018 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2019 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2020 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2021 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2022 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2023 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2024 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |
|  | 2025 | 153,844,992 | 10,778,352 | 164,623,344 | 105,276,629 | 95.49 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction SLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | SLG | BAU | Delta | SLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 163,496,109 | 167,765,977 | 4,269,868 | 94.83 | 97.31 | 2.48 |
|  | 2012 | 166,088,317 | 170,429,257 | 4,340,939 | 96.34 | 98.85 | 2.52 |
|  | 2013 | 161,844,595 | 173,138,235 | 11,293,640 | 93.87 | 100.42 | 6.55 |
|  | 2014 | 164,410,619 | 175,893,740 | 11,483,121 | 95.36 | 102.02 | 6.66 |
|  | 2015 | 161,934,132 | 178,696,613 | 16,762,482 | 93.93 | 103.65 | 9.72 |
|  | 2016 | 164,515,322 | 181,547,714 | 17,032,392 | 95.42 | 105.30 | 9.88 |
|  | 2017 | 162,047,593 | 184,447,917 | 22,400,325 | 93.99 | 106.98 | 12.99 |
|  | 2018 | 164,623,344 | 187,398,113 | 22,774,769 | 95.49 | 108.70 | 13.21 |
|  | 2019 | 164,623,344 | 190,399,210 | 25,775,866 | 95.49 | 110.44 | 14.95 |
|  | 2020 | 164,623,344 | 193,452,134 | 28,828,789 | 95.49 | 112.21 | 16.72 |
|  | 2021 | 164,623,344 | 196,557,826 | 31,934,481 | 95.49 | 114.01 | 18.52 |
|  | 2022 | 164,623,344 | 199,717,246 | 35,093,902 | 95.49 | 115.84 | 20.36 |
|  | 2023 | 164,623,344 | 202,931,375 | 38,308,030 | 95.49 | 117.71 | 22.22 |
|  | 2024 | 164,623,344 | 206,201,208 | 41,577,863 | 95.49 | 119.60 | 24.12 |
|  | 2025 | 164,623,344 | 209,527,761 | 44,904,417 | 95.49 | 121.53 | 26.05 |

| Climate Impact ((Consumption + Losses) X CO2)) (SLG) Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 155,238,085 | 10,876,416 | 166,114,501 | 106,230,224 | 96.35 |
|  | 2012 | 157,702,733 | 11,048,864 | 168,751,597 | 107,916,646 | 97.88 |
|  | 2013 | 157,122,998 | 11,007,993 | 168,130,991 | 107,519,769 | 97.52 |
|  | 2014 | 159,624,073 | 11,182,965 | 170,807,038 | 109,231,101 | 99.07 |
|  | 2015 | 162,168,158 | 11,360,933 | 173,529,091 | 110,971,854 | 100.65 |
|  | 2016 | 164,756,031 | 11,541,953 | 176,297,984 | 112,742,561 | 102.26 |
|  | 2017 | 167,388,487 | 11,726,078 | 179,114,565 | 114,543,765 | 103.89 |
|  | 2018 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2019 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2020 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2021 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2022 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2023 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2024 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |
|  | 2025 | 170,066,336 | 11,913,366 | 181,979,702 | 116,376,019 | 105.55 |

| Climate Impact ((Consumption + Losses) X CO2)) BAU Scenario |
| --- |
|  | Consumption | Losses | Total MWh | CO2 Tons | MMTCO2 |
| Consumption (MWh) by Compliance Year | 2007 | 147,237,195 | 10,316,645 | 157,553,840 | 100,755,681 | 91.39 |
|  | 2008 | 149,562,879 | 10,479,412 | 160,042,292 | 102,347,045 | 92.83 |
|  | 2009 | 151,928,332 | 10,644,952 | 162,573,284 | 103,965,615 | 94.30 |
|  | 2010 | 154,334,271 | 10,813,315 | 165,147,585 | 105,611,881 | 95.79 |
|  | 2011 | 156,781,428 | 10,984,550 | 167,765,977 | 107,286,342 | 97.31 |
|  | 2012 | 159,270,547 | 11,158,709 | 170,429,257 | 108,989,510 | 98.85 |
|  | 2013 | 161,802,389 | 11,335,846 | 173,138,235 | 110,721,901 | 100.42 |
|  | 2014 | 164,377,726 | 11,516,014 | 175,893,740 | 112,484,047 | 102.02 |
|  | 2015 | 166,997,346 | 11,699,268 | 178,696,613 | 114,276,484 | 103.65 |
|  | 2016 | 169,662,052 | 11,885,662 | 181,547,714 | 116,099,763 | 105.30 |
|  | 2017 | 172,372,662 | 12,075,255 | 184,447,917 | 117,954,443 | 106.98 |
|  | 2018 | 175,130,010 | 12,268,104 | 187,398,113 | 119,841,094 | 108.70 |
|  | 2019 | 177,934,944 | 12,464,267 | 190,399,210 | 121,760,295 | 110.44 |
|  | 2020 | 180,788,329 | 12,663,805 | 193,452,134 | 123,712,639 | 112.21 |
|  | 2021 | 183,691,047 | 12,866,779 | 196,557,826 | 125,698,729 | 114.01 |
|  | 2022 | 186,643,996 | 13,073,250 | 199,717,246 | 127,719,179 | 115.84 |
|  | 2023 | 189,648,091 | 13,283,284 | 202,931,375 | 129,774,614 | 117.71 |
|  | 2024 | 192,704,264 | 13,496,943 | 206,201,208 | 131,865,672 | 119.60 |
|  | 2025 | 195,813,466 | 13,714,295 | 209,527,761 | 133,993,003 | 121.53 |

| CO2 Reduction SLG vs. BAU |
| --- |
|  | Total MWh | MMTCO2 |
|  | SLG | BAU | Delta | SLG | BAU | Delta |
| Consumption (MWh) by Compliance Year | 2007 | 157,553,840 | 157,553,840 | 0 | 91.39 | 91.39 | 0.00 |
|  | 2008 | 160,042,292 | 160,042,292 | 0 | 92.83 | 92.83 | 0.00 |
|  | 2009 | 162,573,284 | 162,573,284 | 0 | 94.30 | 94.30 | 0.00 |
|  | 2010 | 165,147,585 | 165,147,585 | 0 | 95.79 | 95.79 | 0.00 |
|  | 2011 | 166,114,501 | 167,765,977 | 1,651,476 | 96.35 | 97.31 | 0.96 |
|  | 2012 | 168,751,597 | 170,429,257 | 1,677,660 | 97.88 | 98.85 | 0.97 |
|  | 2013 | 168,130,991 | 173,138,235 | 5,007,244 | 97.52 | 100.42 | 2.90 |
|  | 2014 | 170,807,038 | 175,893,740 | 5,086,702 | 99.07 | 102.02 | 2.95 |
|  | 2015 | 173,529,091 | 178,696,613 | 5,167,523 | 100.65 | 103.65 | 3.00 |
|  | 2016 | 176,297,984 | 181,547,714 | 5,249,731 | 102.26 | 105.30 | 3.04 |
|  | 2017 | 179,114,565 | 184,447,917 | 5,333,352 | 103.89 | 106.98 | 3.09 |
|  | 2018 | 181,979,702 | 187,398,113 | 5,418,411 | 105.55 | 108.70 | 3.14 |
|  | 2019 | 181,979,702 | 190,399,210 | 8,419,509 | 105.55 | 110.44 | 4.88 |
|  | 2020 | 181,979,702 | 193,452,134 | 11,472,432 | 105.55 | 112.21 | 6.65 |
|  | 2021 | 181,979,702 | 196,557,826 | 14,578,124 | 105.55 | 114.01 | 8.46 |
|  | 2022 | 181,979,702 | 199,717,246 | 17,737,544 | 105.55 | 115.84 | 10.29 |
|  | 2023 | 181,979,702 | 202,931,375 | 20,951,673 | 105.55 | 117.71 | 12.15 |
|  | 2024 | 181,979,702 | 206,201,208 | 24,221,506 | 105.55 | 119.60 | 14.05 |
|  | 2025 | 181,979,702 | 209,527,761 | 27,548,059 | 105.55 | 121.53 | 15.98 |

Electricity 4 : Alternative Energy Portfolio (Act 213 of 2004) Tier I Standard: Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Joe Sherrick (717-772-8944)

Summary:  Identifies GHG reductions associated with the existing AEPS Tier I requirement at 8%.

Other Involved Agencies:  PUC and DEP have shared roles in administering the AEPS

Existing Measure: The AEPS requires that all electricity consumed within PA by 2021 be comprised of at least 0.5% solar PV, 8% from other renewable (Tier I) sources and 10% from other alternative energy (Tier II) sources.  The AEPS matures in 2021 after which, no further increase in renewable generation is required but the standards from 2021 remain in effect.

Projected GHG Reduction:  9.65 MMTCO2

The CO2 emissions reductions associated with this AEPS structure was calculated by first establishing a consumption-based load growth projection for each electric distribution company (EDC) and applying that factor to the 2006 actual consumption for each EDC, projecting out to 2025.  The total estimated electricity consumption was multiplied by a five-year (2000 through 2004) statewide, grid average, CO2 emissions factor of 1,279 pounds per MWH.  This was then converted to million metric tons of carbon dioxide (MMTCO2).

There will be some additional reductions through Tier II from sources such as large hydro and energy efficiency.  The contribution of these resources to meeting the Tier II obligation is somewhat uncertain because we already know that sufficient credits from waste coal have been generated to meet the entire Tier II requirements through at least 2021.   The impact is that little incentive exists for the generation of electricity from new, zero carbon emitting sources due to the over-supply created by waste coal.  It also needs to be noted that any energy efficiency work plans that reduce the overall consumption of electricity within PA will result in a direct reduction of the emissions associated with the AEPS.

Economic Cost:

- Cost to DEP – Administration of programs for the continued support of energy efficiency and renewables, particularly solar PV (ex. Energy Harvest, PEDA, Alternative Energy Investment Act, etc.)

- Cost to the Commonwealth – Continued support of renewables, particularly solar

- Cost to regulated community or consumer – Distribution companies pass compliance costs on to the rate-payers.  Until all of the EDC rate caps are removed the impact will remain uncertain.  The removal of the rate caps will have a far more pronounced impact on electricity rates than will the requirements of the AEPS.

- Are there Federal funds available? USDA Farm Bill appropriations can and have provided limited support.  Moreover, as the total appropriations are increasing, the amount available via grant funding is being significantly scaled back in favor of loans.

- Do these costs fund other programs? No.

- Are cost savings realized from this initiative? Not directly.  Indirect savings to the Commonwealth will accrue subject to in-state renewables development (manufacturing, installation, sales and service, etc.)

Implementation Steps:

- Already being implemented.

- Legislation continues to be drafted that would require additional increases in the amount of alternative energy.  Pennsylvania has the lowest percentage requirements of any surrounding state renewable portfolio standards.  Because the geographic scope from which projects may be considered eligible (Illinois to North Carolina) for Act 213 compliance is much broader than was originally intended and in order to ensure that more renewable energy and associated new jobs are created in PA, the requirements of the AEPS could be increased.

- Act 1 incentives for renewable resources

- Federal production tax credit

Potential Overlap:

- HB 2200

- Reduced Load Growth

- Al Electricity Efficiency Initiatives

- Transmission and Distribution Loss Reductions

- High Performance Building Standards

- Energy Audits

- Others

| AEPS Requirements |  | AEPS CO2 Reductions |
| --- | --- | --- |
| Compliance Year | Tier I | PV | Tier II | Projected PA Consumption (MWH) | Tier I MWH | PV MWH | Tier II MWH | Total AEPS MWH |  | Total Tier I + PV MWH | Total MMTCO2 |
| 2007 | 1.50% | 0.0013% | 4.2% | 147,237,195 | 2,208,558 | 1,914 | 6,183,962 | 8,394,434 |  | 2,210,472 | 1.28 |
| 2008 | 1.50% | 0.0030% | 4.2% | 149,562,879 | 2,243,443 | 4,487 | 6,281,641 | 8,529,571 |  | 2,247,930 | 1.30 |
| 2009 | 2.00% | 0.0063% | 4.2% | 151,928,332 | 3,038,567 | 9,571 | 6,380,990 | 9,429,128 |  | 3,048,138 | 1.77 |
| 2010 | 2.50% | 0.0120% | 4.2% | 154,334,271 | 3,858,357 | 18,520 | 6,482,039 | 10,358,916 |  | 3,876,877 | 2.25 |
| 2011 | 3.00% | 0.0203% | 6.2% | 156,781,428 | 4,703,443 | 31,827 | 9,720,449 | 14,455,718 |  | 4,735,269 | 2.75 |
| 2012 | 3.50% | 0.0325% | 6.2% | 159,270,547 | 5,574,469 | 51,763 | 9,874,774 | 15,501,006 |  | 5,626,232 | 3.26 |
| 2013 | 4.00% | 0.0510% | 6.2% | 161,802,389 | 6,472,096 | 82,519 | 10,031,748 | 16,586,363 |  | 6,554,615 | 3.80 |
| 2014 | 4.50% | 0.0840% | 6.2% | 164,377,726 | 7,396,998 | 138,077 | 10,191,419 | 17,726,494 |  | 7,535,075 | 4.37 |
| 2015 | 5.00% | 0.1440% | 6.2% | 166,997,346 | 8,349,867 | 240,476 | 10,353,835 | 18,944,179 |  | 8,590,343 | 4.98 |
| 2016 | 5.50% | 0.2500% | 8.2% | 169,662,052 | 9,331,413 | 424,155 | 13,912,288 | 23,667,856 |  | 9,755,568 | 5.66 |
| 2017 | 6.00% | 0.2933% | 8.2% | 172,372,662 | 10,342,360 | 505,569 | 14,134,558 | 24,982,487 |  | 10,847,929 | 6.29 |
| 2018 | 6.50% | 0.3400% | 8.2% | 175,130,010 | 11,383,451 | 595,442 | 14,360,661 | 26,339,553 |  | 11,978,893 | 6.95 |
| 2019 | 7.00% | 0.3900% | 8.2% | 177,934,944 | 12,455,446 | 693,946 | 14,590,665 | 27,740,058 |  | 13,149,392 | 7.63 |
| 2020 | 7.50% | 0.4433% | 8.2% | 180,788,329 | 13,559,125 | 801,435 | 14,824,643 | 29,185,202 |  | 14,360,559 | 8.33 |
| 2021 | 8.00% | 0.5000% | 10.0% | 183,691,047 | 14,695,284 | 918,455 | 18,369,105 | 33,982,844 |  | 15,613,739 | 9.06 |
| 2022 | 8.00% | 0.5000% | 10.0% | 186,643,996 | 14,931,520 | 933,220 | 18,664,400 | 34,529,139 |  | 15,864,740 | 9.20 |
| 2023 | 8.00% | 0.5000% | 10.0% | 189,648,091 | 15,171,847 | 948,240 | 18,964,809 | 35,084,897 |  | 16,120,088 | 9.35 |
| 2024 | 8.00% | 0.5000% | 10.0% | 192,704,264 | 15,416,341 | 963,521 | 19,270,426 | 35,650,289 |  | 16,379,862 | 9.50 |
| 2025 | 8.00% | 0.5000% | 10.0% | 195,813,466 | 15,665,077 | 979,067 | 19,581,347 | 36,225,491 |  | 16,644,145 | 9.65 |

Electricity 5: Work Plan for House Bill 80

TBD

Note: Replaces Tier 1 at 15%, Tier 1 at 20%, Carbon Capture and Sequestration Work plans

Electricity 6: Improve Coal-Fired Power Plant Efficiency by 5% Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Krish Ramamurthy (717-772-3369)

Summary: Require a 5% increase in energy efficiency at coal-fired power plants.  Each facility would have the flexibility to meet this efficiency requirement at the least cost method available to them.  Goals and timing of  measure are:

Other Involved Agencies:  Workplan measures would need to be designed so as not to trigger “Major Modification” clause in US EPA New Source Review program for major stationary sources in attainment areas.  This eliminates the option of repowering existing resources in the quantification.  The typical methods that could be utilized for compliance with this measure are listed in the table from the Australian Greenhouse Gas Office publication below.

Possible New Measure(s): An affected Electricity Generating Unit (EGU) may improve efficiency to minimize system losses as a means to reduce CO2 emissions.  For instance, a 15 percent increase in efficiency at an EGU would result in a 13 percent decrease in CO2 emissions.  Upgrades can include improvements to the boiler, turbine, and control systems.  Examples of turbine improvements include installing high efficiency turbine blades, which allow for increased power generation and an efficiency improvement of 0.98 percent.  Fuel consumption reduction can occur with improvements to feed water heater material within a turbine system, leading to an increase in efficiency of between 1 percent and 5 percent.  Upgrading the software of the control system that monitors and fine-tunes combustion can improve efficiency between 0.3 percent to 3 percent.

Additionally, the average U.S. pulverized coal-fired plant operates at a heat rate of about 10,500 Btu/kWh. Yet a sub-critical (2,400 psi/1,000F/1,000F) unit is capable of operating at least 10 percent more efficiently, at a heat rate of 9,500 Btu/kWh.  Using a minimum of 5 percent efficiency expectation, a total of 5.9 million tons of CO2 could be reduced while producing existing levels of electricity.

Potential GHG Reduction: 5.8 MMT CO2e

Economic Cost:

- Cost to DEP – The cost to DEP will be in terms of staff man hours invested in developing any new regulation, or guidance document, that will be required for this effort.  Also, if additional conditions need to be added to permits this will require additional staff time invested by regional office personnel.

- Cost to regulated community or consumer – A study conducted by the Australian Greenhouse Office (January 2000) evaluated the costs and benefits of efficiency improvements to electric generating units.  This paper can be found at http://www.greenhouse.gov.au/ges/publications/pubs/skmreport.pdf

They found that based on a range of efficiency improvement measures for bituminous and sub-bituminous coal plants, the cost effectiveness for those improvements ranged from a savings of $11/ton to a cost of $9/ton.  This is based on an average of all plants in the study.  As indicated not all plants achieved a net cost savings.

- The net present value (NPV) after fuel savings was found to be $5/ton of greenhouse gas saved for the bituminous and sub-bituminous coal plants.  At the NPV of $5/ton it was found that the Average Simple Payback period was five years.  This study found that the fuel savings due to these efficiency improvements ranged from $21 to $30 per ton depending on the plant.

- These improvements were found to result in an expected reduction in the cost of electricity generated for bituminous and sub-bituminous coal.  A 0.3% reduction in the price of electricity generated from bituminous and sub-bituminous coal is expected.

This means that, on average, it was found that efficiency improvements, when applied to an existing coal fired power plant, will pay for themselves over the lifetime of operation of the facility.  Since the cost of coal has increased since 2000, and is projected to increase further, the projected savings from efficiency increases will be greater.

- The availability of federal funds for such improvement projects is unknown.

- The cost to other programs at the federal level is not known.

- Cost savings will be realized by coal fired power plants, according to the Australian study, over the lifetime of the efficiency improvement project.

The table below, from the Australian Greenhouse Office (January 2000)

Report, Integrating Consultancy Efficiency Standards for Power Generation, illustrates the cost in terms of tons of CO2 reduced for a variety of power plant efficiency improvement steps.  For each efficiency improvement action the cost can be determined based on the expected reduction of carbon dioxide in terms of tons of CO2 reduced.  All data in this table is in terms of Australian dollars and metric tones.

Potential Overlap:

- HB 2200, AEPS Tier I (@ 8%, 15%, 20%), Alternative Energy Investment Act, Reduced Load Growth, Reduced Transmission and Distribution Losses

Electricity 6: Greenhouse Gas Performance Standard for New Power Plants Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Krish Ramamurthy (717-772-3369)

Summary:  In order to facilitate maintaining or decreasing the emissions of greenhouse gases (GHG), all new power plants must meet a GHG emissions performance standard of 1320 pounds of CO2 per megawatt hour sent out (equivalent)1 at the time of siting. New power plants must be CO2 neutral: a) within 10 years, or b) by December 31, 2024. The measure allow compliance flexibility as operators can meet the zero emissions requirement by the use of offsets, carbon capture and sequestration, or other methods.  The performance standard applies to all plants beginning operation starting in the year_XXXX.  Interim targets for GHG reductions are XXXX% by 2015 and XXXX% by 2020?

Other Involved Agencies:  None

Proposed New Measures: A new facility must comply with the Best Available Technology (BAT) requirements set forth in 25 Pa. Code Chapter 127.  If the Department determines that the performance standard is either technically or economically infeasible for a proposed project, a facility could meet the performance standard by providing an equivalent offset from the Department approved GHG emission registry prior to the commencement of operation of the project.  At a minimum, the new power plant must be carbon capture ready.

- Alternate GHG performance standard is 1760 pounds of CO2 per megawatt hour sent out (equivalent)1  based on the level that could be achieved by an Integrated Gasification Combined Cycle (IGCC) plant without any of its GHG emissions captured and sequestered.

These new plants shall achieve zero net emission of greenhouse gas emissions within 10 years of their start date of operation but no later than December 31, 2024. These facilities may meet the requirement either by carbon capture and sequestration or by providing an equivalent offset from the Department approved GHG emission registry.   Preference shall be given to offsets from Pennsylvania projects.

Alternate Offset Period – 5 years of the start date of operation but no later than December 31, 2024.

Potential GHG Reduction: The rate of coal-fired power plant retirements by 2025 is uncertain due to technology changes, market factors and facility-specific economics.  The appropriate level of GHG emission reductions to attribute to this initiative is extremely speculative.  The only available data concerns the retirement of Martin’s Creek power plant on September 14th, 2007.  In 2004, this plant created 1,590,999 mwh of coal-fired generation.  This generation going offline will result in a 1.5 MMT CO2e reduction.

Economic Cost:  See note2

Implementation Steps: Limitations are to be implemented through the established Plan Approval Application process for new stationary air contamination sources, administered by the Department’s Field Operations, Regional Air Quality Programs.

Establishment of a GHG emission registry and offset allocation process would require development of new regulatory provisions.

Foot Note 1: The greenhouse gas emissions performance standard of 1320 pounds of CO2 equivalent (CO2e)1 is based on the level that could be achieved by an Integrated Gasification Combined Cycle (IGCC) plant with 25% of GHG emissions are captured and sequestered.

Foot Note 2: Based on National Energy Technology Laboratory (NETL) analysis, dated May 15, 2007, the total plant costs of an IGCC plant with CO2 capture are estimated at $2,390/kWe with total capital and operating costs at $0.1029/kwh. The total plant costs of an IGCC plant without any CO2 capture are estimated at $1,813/kWe and total capital and operating costs at $0.078/kwh.  On the other hand, the total plant costs of a pulverized coal fired supercritical plant without any CO2 capture are estimated at $1,575/kWe and total capital and operating costs at $0.0633/kwh.

Definitions: (as per Title 25 PA Code, Chapter 121)

Best available technology—Equipment, devices, methods or techniques as determined by the Department which will prevent, reduce or control emissions of air contaminants to the maximum degree possible and which are available or may be made available.

Potential Overlap:

- HB 2200, AEPS Tier I (@ 8%, 15%, 20%), Alternative Energy Investment Act, Reduced Load Growth, Reduced Transmission and Distribution Losses

Electricity 7: Nuclear and Hydro Capacity Uprates Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Dan Griffiths (717-773-0542)

Summary:  Capacity uprates at existing nuclear and hydroelectric plants in PA. The uprate schedule for the PA is assumed to be: XXXX.  The targets for hydro uprates begin in year XXXX through XXXX when XXXX% of PA’s existing hydro capacity is assumed to be retrofitted.  Baseline hyrdro uprates under Tier 1 of the AEPS are assumed to be XXXX%

Other Involved Agencies: N/A

Possible New Measure(s):

Nuclear Uprates - To increase the power output of a reactor, typically a more highly enriched uranium fuel is added. This enables the reactor to produce more thermal energy and therefore more steam, driving a turbine generator to produce electricity. In order to accomplish this, components such as pipes, valves, pumps, heat exchangers, electrical transformers and generators, must be able to accommodate the conditions that would exist at the higher power level. For example, a higher power level usually involves higher steam and water flow through the systems used in converting the thermal power into electric power. These systems must be capable of accommodating the higher flows.

In some instances, facilities will modify and/or replace components in order to accommodate a higher power level. Depending on the desired increase in power level and original equipment design, this can involve major and costly modifications to the plant such as the replacement of main turbines. All of these factors must be analyzed by the facility as part of a request for a power uprate, which is accomplished by amending the plant's operating license. The analyses must demonstrate that the proposed new configuration remains safe and that measures continue to be in place to protect the health and safety of the public. Before a request for a power uprate is approved, the Nuclear Regulatory Commission must review these analyses.

Hydroelectric – Uprates or upgrades to hydroelectric power generation can come from the addition of incremental (new) generation at existing plants or simply by making improvements in efficiency to things such as turbine design or improvements to the electrical generators.  With the enactment of the Alternative Energy Portfolio Standard (AEPS), such improvements are being given serious consideration by generating companies.  Therefore, it is important to note that if these improvements are made or incremental generation is brought online, the resultant emissions reduction that might accrue will be accounted for under Tier I of the AEPS, provided that these hydroelectric plants obtain certification from the Low Impact Hydro Institute (LIHI), as required under the AEPS.  Any improvements or incremental generation from a hydroelectric plant that does not or can not obtain LIHI certification will earn Tier II credits under the AEPS but the emissions reductions would not count against our total reductions from the AEPS.  Upgrading older hydropower generating systems is common practice in North America.  Through rehabilitation, hydroelectric producers are increasing capacity and efficiency at existing facilities that are several decades old.  Rewinding a generator or replacing a turbine runner can result in performance that not only equals, but also surpasses the capabilities of the equipment when it was new. Rehabilitating existing plants is often a more economical way of adding capacity, when compared to building new facilities.

Potential GHG Reduction: 		1.57 MMTCO2e

Avoided emissions are calculated on the basis of known potential uprates displacing gas at 1,137.75 lb/MWh (four year average 2002-2005). Exelon was not included in the total since no information was available.

| Planned Nuclear and Hydro Uprates in Pennsylvania |
| --- |
| Owner | Unit | Potential Upgrade & Upgrades Post 2000 (MW) | Capacity Factor | MWH | Avoided CO2 (Tons) - assuming displaces gas at 1,137.75 lb/mwh | CO2 - MM Tons |
| PPL | Susquehanna I | 74 | 0.9 | 583,416 | 331,891 | 0.30 |
| PPL | Susquehanna II | 69 | 0.9 | 543996 | 309,466 | 0.28 |
| PPL | Holtwood | 125 | 0.3 | 328,500 | 186,875 | 0.17 |
| PPL | Safe Harbor | none planned | 0 | 0 | 0 | 0.00 |
| PPL | Wallenpaupack | none planned | 0 | 0 | 0 | 0.00 |
| FE | Beaver Valley I | 81 | 0.9 | 638,604 | 363,286 | 0.33 |
| FE | Beaver Valley II* | 73 | 0.9 | 575,532 | 233,090 | 0.21 |
| Exelon | Peach Bottom II | 70 | 0.9 | 551,880 | 313,951 | 0.28 |
| Exelon | Peach Bottom III | n/a | 0.9 | 0 | 0 | 0.00 |
| Exelon | Limerick I | n/a | 0.9 | 0 | 0 | 0.00 |
| Exelon | Limerick II | n/a | 0.9 | 0 | 0 | 0.00 |
| Exelon | TMI I | n/a | 0.9 | 0 | 0 | 0.00 |
|  |  |  |  |  | 1,738,559 | 1.57 |

Economic Cost: Market forces will drive Investments into infrastructure, to uprate capacity.  These upfront costs will yield greater energy generation capacity and efficiency, leading to increased sales and eventually, increased profits.

Implementation Steps:

- These actions are currently being implemented

- Market-driven initiative

Potential Overlap:

- HB 2200, AEPS Tier I (@ 8%, 15%, 20%), Alternative Energy Investment Act, Reduced Load Growth, Reduced Transmission and Distribution Losses

Electricity 8: Sulfur Hexafluoride (SF6) Emission Reductions from the Electric Power IndustryWork Plan for Potential GHG Reduction Measure

Lead Staff Contact: Krish Ramamurthy (717-783-9476)

Summary:  This initiative uses a pollution prevention approach, including a best management practices manual and recordkeeping and reporting requirements, to ensure that all SF6 emission reductions are quantified and permanent.

Other Involved Agencies: United States Environmental Protection Agency

Possible New Measure(s): SF6 is identified as the most potent non-CO2 greenhouse gas with the ability to trap heat in the atmosphere 23,900 times more effectively than CO2. Approximately 80 percent of SF6 gas produced is used by the electric power industry in high voltage electrical equipment as an insulator or arc quenching medium. SF6 is emitted to the atmosphere during various stages of the equipment’s life cycle. Leaks increase as equipment ages. The gas can also be accidentally released at the time of equipment installation and during servicing.

U.S. EPA has established a voluntary reduction program entitled “SF6 Emission Reduction Partnership for Electric Power Systems.” Under this program the collective SF6 emission rate has been reduced from 17 percent in 1999 to 8.3 percent in 2005 or a reduction of 6.88 MMTCO2e. Avoided purchases to replace gas losses to the atmosphere from this reduction are approximately $3.8 to $5.7 million.  Emissions estimates for Pennsylvania include:

| Basis | Year | SF6 Emissions | (MMTCO2e) |
| --- | --- | --- | --- |
| CIRA-2003 | 1990 | SF6 from Electric Utilities | 0.8 | 87% |
| CIRA-2003 | 1990 | SF6 from Magnesium | 0.1 | 13% |
|  |  | Total | 0.9 | 100% |
| CIRA-2003 | 1999 | SF6 from Electric Utilities | 0.9 | 76% |
| CIRA-2003 | 1999 | SF6 from Magnesium | 0.3 | 24% |
|  |  | Total | 1.2 | 100% |
| PEC-2007 | 1990 | SF6 from Electric Utilities | 1.2 |  |
| PEC-2007 | 2000 | SF6 from Electric Utilities | 0.6 |  |
| PEC-2007 | 2020 | SF6 from Electric Utilities | 0.3 |  |

A regulatory program could be developed in Pennsylvania that uses pollution prevention approach including a best management practices manual and recordkeeping and reporting requirements to ensure that all SF6 emission reductions are quantified and permanent. The reduction of SF6 emissions from the electric power industry is available as one of the offset opportunities for any Cap and Trade Program established for large emitters.

As part of this regulatory program, a manual could be developed that would identify best management practices that would be required of all owners and operators of electric power systems. Best management practices could include proper handling techniques, identification and elimination of leaks, and the replacement of equipment that do not meet specific leak rate thresholds. An example of best management practices would be the recent Duquesne Light Company decommissioning of an old substation to recover the SF6 gas and reclaim it to ASTM standards. The project resulted in the removal of approximately 7,300 lbs of SF6 that otherwise would have been emitted to the atmosphere. As a part of SF6 Emission Reduction Partnership for Electric Power Systems, Exelon’s PECO subsidiaries set a SF6 goal in March 2006, commit a leak rate for SF6 of no more than 10% for 2006. To help achieve the companies provided additional training to substation personnel to minimize SF6 gas leaks and revised the gas handling procedures.   Annual recordkeeping and reporting requirements would be required to ensure the quantification and reduction of SF6 emissions.

Potential GHG Reduction: 0.1 MMT CO2e

This program might reduce SF6 emissions from electric utilities in 2025 from 0.3 to 0.2 MMT CO2e, for an overall reduction of 0.1 MMT CO2e.

Economic Cost:

Industry:  Savings by avoiding purchases to replace gas losses to the atmosphere, are approximately $3.8 to $5.7 million.

Department: No cost authorized or anticipated.  Development of any regulatory program would then be required to be accomplished through existing resources and budget.

Funding Sources: US EPA voluntary cooperative program is implemented under Federal funding independent of Pennsylvania’s budget process.

Implementation Steps: US EPA voluntary cooperative program is implemented and summarized at http://www.epa.gov/electricpower-sf6/   Pennsylvania’s major power producers are participants.

Potential Overlap:

- N/A

Electricity 9: Join Regional Greenhouse Gas Initiative Work Plan for Potential GHG Reduction Measure

Lead Staff Contact:  PUC and DEP

Initiative Summary: Examine the potential CO2 emissions reductions associated with joining the Regional Greenhouse Gas Initiative.

Other Involved Agencies: PUC and DEP

Possible New Measure(s):

RGGI is composed of individual CO2 Budget Trading Programs in each participating state. These programs are implemented through state regulations, based on a RGGI Model Rule, and are linked through CO2 allowance reciprocity. Regulated power plants are able to use a CO2 allowance issued by any of the participating states to demonstrate compliance with the state program governing their facility. Taken together, the individual state programs function as a single regional compliance market for carbon emissions.

To reduce emissions of greenhouse gases, the RGGI participating states are using a market-based cap-and-trade approach that includes:

- Establishing a multi-state CO2 emissions budget (cap) that will decrease gradually until it is 10 percent lower than at the start

- Requiring electric power generator to hold allowances covering their emissions of CO2

- Providing a market-based emissions auction and trading system where electric power generators can buy, sell and trade CO2 emissions allowances

- Using the proceeds of allowance auctions to support low-carbon-intensity solutions, including energy efficiency and clean renewable energy, such as solar and wind power

- Employing offsets (greenhouse gas emissions reduction or sequestration projects at sources beyond the electricity sector) to help companies meet their compliance obligations

RGGI's phased approach means that reductions in the CO2 cap will initially be modest, providing predictable market signals and regulatory certainty. Electricity generators will be able to plan for and invest in lower-carbon alternatives and avoid dramatic electricity price impacts.

The RGGI Model Rule may be found at http://www.rggi.org/docs/Model%20Rule%20Revised%2012.31.08.pdf

Potential GHG Reduction (Million Metric Tons of CO2 Equivalents):

RGGI is set up to reduce CO2 emissions 10% below 2005 by 2018.  According to EIA data, CO2 emissions from the PA electric sector in 2005 were 215 million tons, therefore, a 10% reduction would be 12.5 million tons.

Economic Cost: [Identify the costs associated with this initiative.  Some things to consider and identify could include:

- Cost to DEP & PUC – The cost will be in terms of staff man hours invested in developing any new regulation, or guidance document, that will be required for this effort.  Also, additional staff time invested by regional office personnel necessary to update permits.

- Cost to Commonwealth – A study conducted by the University of Maryland (January 2007) evaluated the costs and benefits of participating in the Regional Greenhouse Gas Initiative.  This study can be found at http://www.cier.umd.edu/RGGI/documents/UMD_RGGI_STUDY_Jan07.pdf

The main conclusions of this study indicate that, overall, joining RGGI would only have a limited impact on the economy and electric power markets in Maryland.  Similar conclusions hold for the current RGGI region and affected areas outside this region.

Electricity Bill Impacts:  Overall, electricity bills are forecast to decrease over $100 million in 2010 and more than $200 million by 2025.  This is a result of energy efficiencies, which will lower customers’ demands.  Since the heaviest users will save the most, more than half the savings (between 53 percent and 63 percent) will go to industrial and commercial customers.  On average, a residential ratepayer will see a modest reduction – about $22 savings in 2010 per household.

Overall Economic Impacts:  Will have little net impact on the Maryland economy.  The positive economic impacts from reduced electricity costs and energy efficiency investments are partially offset by reduced investment and profits in the electricity generating sector.  Overall RGGI is predicted to have a positive economic impact on Gross State Product of approximately $100 million in 2010, increasing to about $200 million in 2015 and subsequent years.  This impact is expected to create approximately 1200 jobs across the state by 2010, increasing to 2800 jobs by 2025.  Such positive impacts are less than 0.1 percent of overall Maryland gross state product and employment in all years.

Implementation Steps: New legislation and new regulation based on RGGI Model Rule is required.

Potential Overlap: Reduced load growth, efficiency at coal plants, and new plant plans

Electricity 10: Promote Combined Heat and Power Work Plan for Potential GHG Reduction Measure

Strategy Name: Promote combined heat and power (CHP)

Lead Staff Contact: Maureen Guttman (717-783-8411)

Summary:  This initiative encourages CHP systems to reduce fossil fuel use and GHG emissions.  Reductions are achieved through the improved efficiency of CHP systems, relative to separate heat and power technologies, and by avoiding transmission and distribution losses associated with moving power from central generation stations to distant locations where electricity is used.

Other Involved Agencies:

Possible New Measure(s):

- Promote use of natural gas-fired CHP.

- Promote use of biomass-fired CHP.

- Create or expand markets for CHP units by incentives designed to promote implementation for residential, commercial and industrial users.

- Promote CHP technologies through provisions for tax benefits, attractive financing, utility rebates and other incentives.

- Remove barriers to CHP development, such as utility rate structures that allow discounted electric rates to compete with CHP.  Also, interconnection standards should be designed to facilitate economical and efficient CHP connection to the grid.

- Consider the economic and environmental benefits of CHP as a resource in each electric utility’s Integrated Resource Plan.  Potential measures include training and certification of installers and contractors; net metering and other pricing arrangements; clear and consistent interconnection standards; and creation and support for biomass fuel markets.

Potential GHG Reduction:

Economic Cost:  $ million savings

Implementation Steps:

Potential Overlap: