Waste-1

Landfill Methane Displacement of Fossil Fuels

Work Plan for Potential GHG Reduction

Lead Staff Contact:  Richard Illig (717) 772-5834

Summary:  Landfill methane resources and projects will be identified, assessed, and promoted to decrease fossil fuel use in business thermal applications, or otherwise displace the use of commercial natural gas resources.  Maximizing the use of landfill methane as a fuel reduces greenhouse gas emission of methane and serves to offset emissions of carbon dioxide from the use of fossil fuels such as coal, oil, and natural gas.

Goals:  Require all active and recently closed landfills containing greater than 1 million tons of disposed waste to install gas collection systems. (note from subcommittee call: make goal based on gas generation instead of waste in place)

Implementation Period:  Need to know when controls would be applied

(for example: reach 50% of goal by 2015 and 100% of goal by 2020)

Parties Affected/Implementing Parties:  DEP, PENNDOT, PUC, & DCED, Landfill owners/operators

Data sources/Assumptions/Methods for GHG:

Landfill gas resources will be assessed to determine the degree to which fossil fuel use for the purpose of generating heat can be displaced.  Landfill gas thermal use projects include conversion to commercial grade “pipeline-quality” methane (natural gas) and direct use applications in industrial or commercial equipment.

For the purposes of this report landfill gas electricity generation projects will not be addressed.

Operating municipal waste landfills are evaluated annually.  Key data collected from DEP Solid Waste Program Landfill Annual Operation Reports includes:

- site total waste capacity and the volume of disposed waste

- landfill gas collection rates and gas quality relative to methane content

- details of landfill gas projects, and

- thermal energy benefits

Landfill gas collection systems efficiency is estimated between 60 to 85 percent by the U.S. EPA.  Efficiencies up to 90 and 95 percent have been calculated using gas measurements taken at modern landfill operations1.  For the purposes of this report landfill gas collection efficiency will be estimated at 85 percent for the following reasons:

- Landfill gas project investments rely on optimizing landfill gas volume and quality relative to methane content.

- PA landfills are well maintained.  Installed gas collection systems are relatively new.

- Improved technologies and operational practices are used in landfill construction.  Gas wells are routinely monitored and calibrated.

Emissions Estimates

Calculation assumptions:

- Evaluated landfills typically contain at least 1 million tons of disposed municipal waste

- Municipal waste disposal volume in PA landfills is anticipated to remain static or possibly decrease through 2025 for the following reasons:

- Reduced volume of out-of-state waste disposed in Pennsylvania

- Increased recycling and material recovery and reuse practices

- Increased waste pick-up and disposal costs

- Increased numbers of waste-to-energy facilities

- Decreased disposal of biomass

- A 35 percent increase in PA landfill gas generation from 2008 through 2025.

- Landfill gas beneficial use – reducing the amount of flared landfill gas - will increase from the current 69 percent to 90 percent or more.

- Thermal projects consume 27 percent of beneficially used landfill gas

- Landfill gas contains 450Btu per cubic foot

Based on 2007 report data Pennsylvania landfills collect over 62,700MMscfy (million standard cubic feet per year) of landfill gas.  Currently over 11,700MMscfy - about 19 percent - is used in thermal projects that displace fossil fuel use, over 19,500MMscfy is flared, and about 31,500MMscfy is used to generate electricity.

A 21 percent reduction in the volume of flared landfill gas would allow an additional 4095MMscfy for beneficial use projects.  Thermal projects would assume 27 19 percent of 4095MMscfy or 1106 778MMscfy.  1106 778MMscfy + 11,700MMscfy = 12,806 12,478MMscfy of landfill gas used in thermal projects.

At 450Btu per cubic foot of gas, 12,806 12,478MMscfy = 5,762,700 5,615,100MMBtu (million Btu).  Given a 35 percent increase in landfill gas generation through 2025 would yield 17,228 16,845MMscfy or 7,779,645 7,580,250MMbtu.

The beneficial use of 17,228 16,845MMscfy of landfill gas yields the following emission reductions:

- 3.88 3.79MMTCO2E

- 182,186 178,133tons of methane per year

- 450,526 440,504tons CO2 per year

7,779,645 7,580,250MMBtu is equivalent to the avoided use of:

- 7,780 7580MMscfy of natural gas, or

- 55.6 54.14million gallons of #2 fuel oil, or

- over 311,185 303,210tons of coal

Data sources/Assumptions/Methods for Costs:

- Estimating direct use project costs at $10/MMBtu, plus $0.45/MMBtu operation & maintenance costs per year.  Developing an additional 5,528MMscfy or 2,487,600MMBtu would cost over $24,876,000 plus $3,607,000 or nearly $30 million.

- Approximately $1 million per mile of pipeline based on direct use projects in PA.

- Retrofit costs for burners and boilers to utilize landfill gas for fuel approximately $30,000 - $300,000 depending on size and type of retrofit.

- State permitting costs are undetermined but may include:

  - Solid Waste beneficial use permit for landfill gas utilization

  - Air Quality Program notifications and operational permit for landfill gas processing and gas end-use equipment.

  - Storm water permitting and/or erosion and sedimentation controls may be needed.

  - Historic preservation or endangered species act may apply to pipeline right-of-ways.  Pipeline costs would increase accordingly.

- Local permitting may also apply.

Other Considerations/Notes:

- Should not apply to closed landfills.

- Dependent on landfill permitting.

- Require all active and recently closed landfills containing greater than 1 million tons of disposed waste to install gas collection systems.

- Prioritize right of way access for landfill gas pipeline projects.

- Work with landfill gas project developers to identify the nearest economical end uses.

- Prioritize landfill gas projects presenting economic development benefits or that otherwise enhance the application of renewable energy technologies.

- Require landfill gas electrical and thermal use projects to incorporate waste heat recovery.  This could help maximize fossil fuel displacement.

- Encourage projects that utilize all landfill gas generated at a site and/or projects able to grow with landfill site gas generation.

- Promote the high reliability of landfill gas projects.  Most projects are able to operate continuously over extended periods of time other than for periodic maintenance.

- Prioritize self-powered thermal landfill gas projects that include an electric generation component.

Potential Overlap

- Solid Waste Work Plan

- Recycling Work Plan

- Industrial Natural Gas BMPs

- Lost and Unaccounted for Natural Gas

Waste-2

Statewide Recycling Initiative

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact:	Gregory Harder (717) 787-0114

Larry Holley (717) 787-7382

Initiative Summary:  Support the expansion of statewide recycling to increase the amount of materials recycled and achieve GHG reductions equivalent to 86% of the Commonwealth’s total recycling potential.

Goals:  Achieve 86% of Pennsylvania's recycling potential by 2020 or 2025??

Implementation Period:

| YEAR | ACTION | % OF GOAL* | GHG REDUCTION | GHG REDUCTION |
| --- | --- | --- | --- | --- |
| 2000 | Historical |  | 2.1 MMTCE | 7.7 MMTCO2 |
| 2012 | Legislation and Regulations in Place | 20% | 3.0 MMTCE | 11 MMTCO2 |
| 2015 | Increased Non-regulatory Enhancements | 50% | 3.8 MMTCE | 14 MMTCO2 |
| 2020 | Program Maintained and Improvement | 80% | 4.5 MMTCE | 17 MMTCO2 |
| 2025 | Completion | 100% | 5.0 MMTCE | 18 MMTCO2* |

* Total in Pennsylvania, including reductions due to recycling that is already happening??  Assumes achievement of additional reductions of 2.5 MMTCE or 9.2 MMTCO2, 86% of the potential reduction of 2.9 MMTCE or 11 MMTCO2.

Parties Affected/Implementing Parties:  DEP

Data Sources/Assumptions/Methods for GHG:

Based on data analyzed by the Northeast Recycling Council’s (NERC) Environmental Benefits Calculator, Pennsylvania saved 2.5 million metric tons of carbon equivalent (MMTCE) or 9 million metric tons of carbon dioxide equivalent (MMTCO2e) as a result of recycling approximately 4.9 million tons of materials in 2005.  There is potential to reduce an additional 2.9 MMTCE or 11 MMTCO2e assuming the recycling of an additional 4 million tons of Pennsylvania generated recyclables identified as discarded in landfills and incinerators by the Statewide Municipal Waste Composition Study (April 2003).

More than 5.4 million MMTCE or 20 MMTCO2e could be avoided annually if recyclable materials being disposed were added to the materials presently recovered from the municipal waste stream through recycling programs in the Commonwealth.  These materials include newspaper, corrugated cardboard, office paper, magazines, mixed paper, plastic bottles, film plastic, rigid plastic, glass, steel and aluminum cans, steel scrap and other metals.  Additional savings above and beyond this projection could be realized if comprehensive programs were developed for the collection and recycling of wood waste, textiles, and carpet.

Energy conserved from manufacturing products using recycled feedstock rather than virgin raw materials, or non-renewable resources, resulted in the savings of 98 trillion British Thermal Units of energy in 2005, enough to power over 941,000 Pennsylvania homes for year or the equivalent of conserving 786 million gallons of gasoline.

Emission and energy credit accrued by our recycling efforts could be recognized as a tradable commodity that may help achieve the Commonwealth's sustainability goals.

PA DEP could target recycling programs to specifically begin or increase collecting those materials that provide the maximum greenhouse gas reductions.  To further stimulate recycling opportunities, PA DEP could ultimately ban those materials from disposal or processing.  Aluminum, steel, plastics, cardboard and paper should be initially targeted as these materials will yield the greatest reductions.

Act 101, the Municipal Waste, Planning Recycling and Waste Act Reduction of 1988, provides the foundation for recycling that has resulted in comprehensive environmental and economic benefits for Pennsylvania.  The Act provides for a $2 per ton recycling fee on waste disposed or processed at municipal waste landfills and resource recovery facilities in the Commonwealth.  The Recycling Fee generates approximately $47 million dollars annually to a Recycling Fund administered by Pa. DEP.  The Recycling Fund provides support to local governments for implementation of recycling programs.  The Recycling Fee also supports the stimulation of markets for recyclable materials. The Department is focusing Act 101 funds on programs geared towards financial sustainability including those that are targeting new materials that were previously disposed.  Increasing the amount of materials recycled will provide direct reduction in greenhouse gas emissions.

Pennsylvania’s recycling program provides annual economic benefits in excess of $23 billion and nearly 82,000 jobs (National Recycling Council, REI Study, 2001).  The program also provides extensive environmental benefits.  The 2.5 MMTCE eliminated in 2005 by recycling amounted to a savings of approximately 3 percent of all greenhouse gas emissions in the Commonwealth.  Also, recycling conserved considerable natural resources.  By recycling almost 1.2 million tons of steel cans, appliances and similar materials in 2005, Pennsylvania industries saved almost 1.5 million tons of iron ore, 829,786 tons of coal and 71,124 tons of limestone.  Through recycling newspapers, phone books, office paper, cardboard and mixed paper, the Commonwealth saved the equivalent of 78 million tree seedlings grown for 10 years.  These trees would sequester carbon dioxide from the atmosphere and store it in their wood.

Listed below is the baseline data that reflects the reduction of carbon equivalent since 2001.

| YEAR | GHG REDUCTION |
| --- | --- |
| 2001 | 2.1 MMTCE |
| 2002 | 1.7 MMTCE |
| 2003 | 2.1 MMTCE |
| 2004 | 1.9 MMTCE |
| 2005 | 2.5 MMTCE |

Historically, data reported to PA DEP demonstrates an annual modest increase in the tonnage of materials recycled.  In 1989, the first full year of Act 101 recycling reporting, approximately 378,000 tons of materials were recycled.  Since then the program has grown to nearly 4.9 million tons of materials recycled in 2005.  These annual increases provide a proven track record of quantifiable environmental and economic benefits.

| YEAR | POPULATION | DISPOSAL | PER CAPITA DISPOSAL PER DAY | RECYCLING |
| --- | --- | --- | --- | --- |
|  |  | IN TONS | IN TONS | IN TONS |
| 2000 | 12,281,054 | 9,324,468 | 0.76 | 3,791,433 |
| 2001 | 12,281,054 | 9,477,159 | 0.77 | 3,941,949 |
| 2002 | 12,281,054 | 9,613,250 | 0.78 | 3,927,048 |
| 2003 | 12,281,054 | 10,201,821 | 0.83 | 4,448,937 |
| 2004 | 12,281,054 | 10,373,136 | 0.84 | 4,747,332 |
| 2005 | 12,440,621 | 10,181,392 | 0.82 | 4,865,923 |

Pennsylvania’s recycling data was analyzed in the NERC Environmental Benefits Calculator.  The raw 2005 data inputs used for the analysis are displayed in Attachment 1.   Attachment 2 shows GHG reductions estimated by the calculator for 2005.  Attachment 3 shows GHG reductions based on the recycling of recyclable materials that were identified as disposed in the Statewide Waste Characterization Study (April 2003).  Attachment 4 is the NERC Environmental Benefits Calculator in spreadsheet form including five worksheets reflecting 2005 Pa. recycling data.

### Total Reduction: 10.3 MMTCO2e

18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  This has been determined to be a feasible goal.  Baseline reductions have been subtracted to reveal the additional reductions gained by this measure (10.3 MMTCO2e).

Data Sources/Assumptions/Methods for Costs:

The overall cost to the Commonwealth needed to increase recycling to achieve the increased greenhouse gas reductions could be funded partially through the Recycling Fund, provided it is reauthorized by the General Assembly. The Commonwealth should realize an overall economic benefit from avoided waste disposal cost, increased numbers of jobs from an increased recycling industry, taxes from new business and some increased revenues from the sales of the new materials being recycled.

Industry may need to make some capital investments to facilitate increased collection.  The capital expenditures should be recouped in a reasonable amount of time based on the avoided disposal costs.  The avoided disposal costs in concert with the greenhouse gas reductions make any increased recycling expenditures a solid investment.

Implementation Steps:  Pa. DEP has a three-pronged strategy to facilitate increased recycling in the Commonwealth.  The separation into distinct areas will allow the Department to better monitor government progress with internal mechanisms.  To ensure that industry and the general public have meaningful input into the new recycling mandates the Department will utilize the regulatory process.

- The first prong is focused on ensuring that we as state government are taking a leadership role and maximizing our recycling efforts.  These efforts will be initiated with a new comprehensive management directive that will ensure all Commonwealth Agencies, Boards and Commissions are implementing recycling and waste reduction programs, as well as purchasing environmentally preferable products.

- Secondly, the Department depends on county governments to report recycling activities within their jurisdiction, as required by Act 101.  To facilitate more timely and improved reporting the Department will implement or procure a new or modified reporting system to capture much of the recycling data that currently goes unreported.

- The third prong is focused on industry and waste companies.  The Department will be making significant changes to the municipal and residual waste regulations that will prevent the disposal of certain materials and require new collection programs for a host of materials.  This regulatory reform will take 18-36 months until a final rulemaking is in place.   During that time the Department will continue its work in building increased capacity to recycle those materials banned from disposal.  The Department will use existing Recycling Fund monies to support the development of infrastructure.

In addition to the three steps identified above, some consideration could be given to the elimination of the Sunset date (December 31, 2011) for the recycling fees.  This would increase available funds for this and other related initiatives.

The following table depicts targeted achievements for additional Greenhouse Gas Reductions by increased recycling through 2025:

| YEAR | ACTION | % OF GOAL* | GHG REDUCTION | GHG REDUCTION |
| --- | --- | --- | --- | --- |
| 2000 | Historical |  | 2.1 MMTCE | 7.7 MMTCO2 |
| 2012 | Legislation and Regulations in Place | 20% | 3.0 MMTCE | 11 MMTCO2 |
| 2015 | Increased Non-regulatory Enhancements | 50% | 3.8 MMTCE | 14 MMTCO2 |
| 2020 | Program Maintained and Improvement | 80% | 4.5 MMTCE | 17 MMTCO2 |
| 2025 | Completion | 100% | 5.0 MMTCE | 18 MMTCO2* |

* Assumes achievement of additional reductions of 2.5 MMTCE or 9.2 MMTCO2, 86% of the potential reduction of 2.9 MMTCE or 11 MMTCO2.

18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  This has been determined to be a feasible goal.  Baseline reductions have been subtracted to reveal additional reductions gained by this measure.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Solid Waste Initiative

Other Considerations/Notes:

Attachment 1:

| Pa. Materials Recycled, 2005 |  |  |  |
| --- | --- | --- | --- |
| MATERIAL | DEP Code(s) | Breakout | TONS |
| FOOD WASTE | FW1 |  | 66,481.70 |
| GLASS |  |  |  |
| GLASS: CLEAR | GL1 | 15,577.80 |  |
| GLASS: MIXED | GL2 | 21,866.30 |  |
| GLASS: GREEN | GL3 | 6,311.40 |  |
| GLASS: BROWN | GL4 | 6,681.50 |  |
| GLASS: PLATE | GL5 | 5,153.20 |  |
| GLASS: OTHER | GL6 | 1,929.30 |  |
| Subtotal Glass |  |  | 57,519.50 |
| BATTERY: LEAD-ACID | B01 |  | 22,169.90 |
| METALS |  |  |  |
| ALUMINUM CANS | AA1 | 17,590.00 |  |
| FERROUS | F01 | 580,142.10 |  |
| STEEL & BIMETALLIC (TIN) CANS | F02 | 13,935.90 |  |
| WHITE GOODS | F03 | 56,383.30 |  |
| MIXED METALS | MM1 | 174,797.40 |  |
| MIXED CANS | MX2 | 2,547.00 |  |
| NON FERROUS | N01 | 48,413.40 |  |
| COPPER | N02 | 4,524.60 |  |
| BRASS | N03 | 2,349.60 |  |
| LEAD | N04 | 167.5 |  |
| STAINLESS STEEL | N05 | 203,794.40 |  |
| NICKEL | N10 | 48.7 |  |
| WIRE/CABLE | W01 | 1,455.30 |  |
| Subtotal Metals |  |  | 1,106,149.20 |
| PAPER |  |  |  |
| PAPER: CARDBOARD | C01 | 713,552.00 |  |
| PAPER: BROWN BAGS & SACKS | C02 | 3,749.60 |  |
| PAPER: MAGAZINE | PA1 | 24,682.80 |  |
| PAPER: NEWSPRINT | PA2 | 244,252.40 |  |
| PAPER: MIX | PA3 | 230,483.50 |  |
| PAPER: OFFICE PAPER | PA4 | 76,303.80 |  |
| PAPER: COMPUTER | PA5 | 3,807.70 |  |
| PAPER: PHONE BOOKS | PA6 | 1,242.50 |  |
| Subtotal Papers |  |  | 1,298,074.30 |
| PLASTICS |  |  |  |
| DRUM PLASTIC | DR1 | 791.2 |  |
| PLASTIC: PET | PL1 | 6,754.60 |  |
| PLASTIC: HDPE | PL2 | 6,955.40 |  |
| PLASTIC: PVC (POLYVINYL/CHLORIDE) | PL3 | 15,206.50 |  |
| PLASTIC: LPDE (LOW DENSITY POLYETHYLENE) | PL4 | 2,598.90 |  |
| PLASTIC: PP (POLYPROPLENE) | PL5 | 3,236.20 |  |
| PLASTIC: PS (POLYSTYRENE) | PL6 | 1850.2 |  |
| PLASTIC: MIXED | PL7 | 16,225.60 |  |
| PLASTIC: FILM | PL8 | 5,747.40 |  |
| PLASTIC: OTHER | PL9 | 4,594.90 |  |
| Subtotal Plastics |  |  | 63,960.90 |
| SINGLE STREAM | SS1 |  | 43,645.80 |
| TEXTILES | M03 |  | 25,182.70 |
| TIRES | M01 |  | 55,416.50 |
| WOOD | WW1 |  | 213,284.90 |
| YARD TRIMMAGE | Y03 |  | 585,681.50 |
| OTHER RECYCLABLES |  |  |  |
| CIRCUIT BOARDS | CB1 | 61.6 |  |
| CONSUMER ELECTRONICS | CRT | 2,900.00 |  |
| FLUORESCENT TUBES | FL1 | 261 |  |
| HOUSEHOLD HAZARDOUS WASTE | HHW | 1,353.90 |  |
| MATTRESSES | MT1 | 116.6 |  |
| ANTIFREEZE | O02 | 1,342.20 |  |
| OIL FILTERS | OL3 | 798.9 |  |
| COMMINGLED MATERIALS | XXX | 228,699.80 |  |
| Subtotal Other Recyclables |  |  | 235,534.00 |
| 904 excess |  |  | 25,929.00 |
| Tire excess |  |  | 72,770.00 |
| ISRI excess |  |  | 51,795.00 |
| Lancaster County (RE-Trac) | INCORPORATED |  |  |
| TOTAL STANDARD |  |  | 3,923,594.90 |
| TOTAL NON-STANDARD |  |  | 942,328.10 |
| GRAND TOTAL |  |  | 4,865,923.00 |

Attachment 2:

| Reductions in Greenhouse Gas Emissions as a Result of 2005 Recycling Tons Recycled Greenhouse Gas Emissions Associated with Recycling (MTCE) Greenhouse Gas Emissions if Recyclables Had Been Disposed (MTCE) Net Greenhouse Gas Emissions from Recycling as Compared to Disposal (MTCE) Reporting Year 2005 Aluminum Cans 33,619 -124,418 381 -124,799 Steel Cans 44,590 -21,817 -2,494 -19,323 Glass 201,097 -15,239 2,194 -17,433 HDPE 40,115 -15,230 1,923 -17,152 LDPE 2,599 -1,201 125 -1,326 PET 39,736 -16,667 2,161 -18,828 Corrugated Cardboard 714,526 -606,295 46,378 -652,673 Magazines/Third-class Mail 25,935 -21,718 -2,313 -19,405 Newspaper 276,048 -210,163 -63,883 -146,280 Office Paper 76,652 -59,629 32,309 -91,939 Phonebooks 1,721 -1,246 -398 -848 Textbooks 0 0 0 0 Whole Computers 0 0 0 0 Food Scraps 66,482 -3,600 10,599 -14,199 Yard Trimmings 585,682 -31,717 -35,002 3,286 Grass 0 0 0 0 Leaves 0 0 0 0 Branches 213,285 -11,550 -25,957 14,407 Ferrous Scrap Metal 650,458 -318,251 -36,376 -281,875 Aluminum Scrap Metal 31,681 -117,246 359 -117,605 Copper Wire 0 0 0 0 Tires 128,187 -63,783 2,101 -65,884 Construction & Demolition 688,211 NA NA NA Carpet 0 0 0 0 Dimensional Lumber 0 0 0 0 Medium-density Fiberboard 0 0 0 0 Clay Bricks 0 NA NA NA Aggregate 0 0 0 0 Fly Ash 0 0 0 0 Mixed Paper, Broad Definition 244,234 -235,593 12,891 -248,484 Mixed Metals 490,360 -703,102 -17,722 -685,380 Mixed Plastics 47,652 -19,418 2,407 -21,825 Mixed Recyclables 0 0 0 0 Mixed Organics 0 0 0 0 Other Recyclables 263,279 NA NA NA Total as a Result of Recycling 4,866,149 -2,597,884 -70,318 -2,527,566 |  |  |  |
| --- | --- | --- | --- |

Attachment 3:

# Potential GHG Reductions if recyclable materials disposed were recycled

|  | Potential Tons Recyclable | Greenhouse Gas Emissions Associated with Recycling (MTCE) |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Reporting Year | (MSW Composition Study, April 2003) |  |  |  |  |
| Aluminum Cans | 48,844 | -180,763 |  |  |  |
| Steel Cans | 102,532 | -50,166 |  |  |  |
| Glass | 234,629 | -17,780 |  |  |  |
| HDPE | 68,082 | -25,848 |  |  |  |
| LDPE | 0 | 0 |  |  |  |
| PET | 87,601 | -36,743 |  |  |  |
| Corrugated Cardboard | 785,032 | -666,121 |  |  |  |
| Magazines/Third-class Mail | 251,027 | -210,208 |  |  |  |
| Newspaper | 389,263 | -296,357 |  |  |  |
| Office Paper | 341,975 | -266,029 |  |  |  |
| Phonebooks | 0 | 0 |  |  |  |
| Textbooks | 0 | 0 |  |  |  |
| Whole Computers | 0 | 0 |  |  |  |
| Food Scraps | 0 | 0 |  |  |  |
| Yard Trimmings | 0 | 0 |  |  |  |
| Grass | 0 | 0 |  |  |  |
| Leaves | 0 | 0 |  |  |  |
| Branches | 0 | 0 |  |  |  |
| Ferrous Scrap Metal | 282,131 | -138,039 |  |  |  |
| Aluminum Scrap Metal | 43,057 | -159,347 |  |  |  |
| Copper Wire | 0 | 0 |  |  |  |
| Tires | 0 | 0 |  |  |  |
| Construction & Demolition | 0 | NA |  |  |  |
| Carpet | 0 | 0 |  |  |  |
| Dimensional Lumber | 0 | 0 |  |  |  |
| Medium-density Fiberboard | 0 | 0 |  |  |  |
| Clay Bricks | 0 | NA |  |  |  |
| Aggregate | 0 | 0 |  |  |  |
| Fly Ash | 0 | 0 |  |  |  |
| Mixed Paper, Broad Definition | 433,821 | -418,473 |  |  |  |
| Mixed Metals | 32,138 | -46,081 |  |  |  |
| Mixed Plastics | 906,653 | -369,457 |  |  |  |
| Mixed Recyclables | 0 | 0 |  |  |  |
| Mixed Organics | 0 | 0 |  |  |  |
| Other Recyclables | 0 | NA |  |  |  |
| Total as a Result of Recycling | 4,006,785 | -2,881,412 |  |  |  |

Attachment 4:

NERC Environmental Benefits Calculator, 2005 Pa. Recycling Data

Waste-3

Solid Waste Management Initiative

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Mike Texter (717) 783-6006 or TBD ? (717) 787-2783

Initiative Summary:  The Solid Waste Management Initiative is comprised of three (3) strategies:

- Alternative Fuels Derived from Waste

- Waste to Energy (WTE)

- Reduced Transportation of Waste

These strategies aim to utilize the energy potential of residual and municipal waste and decrease the energy used to transport waste to landfills.  Reduction numbers result as conventional energy sources (fossil fuels) are displaced by energy derived from waste, and reductions of transportation energy.  Utilizing these waste materials for energy will also prevent a significant amount of material from being disposed of in landfills.

Goals:  Need goal for the third element - Reduced Transportation of Waste

Implementation Period:  See table for implementation for the first two elements. Need to know when goal for third element would be reached

(for example: reach 50% of goal by 2015 and 100% of goal by 2020)

Parties Affected/Implementing Parties:  DEP

Data Sources/Assumptions/Methods for GHG:

Alternative Fuels: In 2005, Pennsylvania saved ~2.5 Million Metric Tons of Carbon Dioxide Equivalent (MMTCOe) as a result of direct use of 1.26 million tons of waste as alternative fuels.  The Commonwealth can reduce an additional ~5.4 MMTCOe by using an additional 2.71 million tons of Pennsylvania generated municipal and residual wastes as alternative fuels. These materials include non-recyclable paper, wood, mixed paper, plastic, textiles and carpet.  The alternative fuels that would be generated would be solid fuels for use in cement kilns, large industrial boilers or waste coal facilities (any wood waste used at waste coal facilities would be a double count with AEPS Tier I reductions).

There is potential to reduce an additional ~4.5 MMTCOe assuming the use of an additional 2.23 tons of recyclable materials that are currently being land filled. These materials include cardboard, film plastic, newspaper, office paper and magazines.

Waste to Energy (WTE): In 2006, Pennsylvania saved 2.3 MMTCOe as a result of recovering energy from 2.92 million tons of municipal and residual waste.  The Commonwealth can reduce an additional 4.1 MMTCOe by recovering energy from an additional 5.2 million tons of Pennsylvania municipal and residual wastes from metropolitan areas with sufficient waste generation to justify a waste to energy facility. These metropolitan areas include Allegheny, Berks, Chester, Lackawanna, Lehigh, Luzerne, Montgomery, Northampton and Philadelphia counties.

There is potential to reduce an additional 10.1 MMTCOe assuming the recovery of energy from all of the remaining 12.9 million tons of municipal and residual waste with energy value currently being land filled in Pennsylvania. This includes 6.6 MMTCOe from 8.4 million tons of out-of-state waste with energy value that could occur outside of Pennsylvania, which is not included in the 2025 goal.

Waste Transportation: In 2006, the transportation of waste from the Allentown/Bethlehem/Easton area, New Jersey, New York and Philadelphia to disposal facilities in Pennsylvania outside of these areas consumed 39.2 million gallons of fuel. Providing waste management options near the point of generation would save 0.42 MMTCOe.

The GHG reductions assumed that sold waste growth rates would be constant in the future.  In actuality we know that solid waste will experience growth, which could possibly increase the GHG reductions realized by these initiatives.  The constant growth assumption reduces the GHG reduction potential of this initiative, which appropriately accounts for the overlap effect of the expanded recycling and landfill methane recovery initiatives.

GHG emissions will result from the burning of solid alternative fuel and the operation of waste to energy facilities.  However, reductions in GHGs are realized from avoided landfill emissions and the displacement of traditional energy sources with solid waste derived energy sources.

Alternative Fuels: As part of the Waste Futures initiative, the Department identified the current and future market for alternative fuels.  The Department is currently working on additional general permits to facilitate the use of alternative fuels. Long-term actions include regulatory changes to further reduce obstacles to use of waste as an energy source. These actions will result in the reduction of 5.4 MMTCOe.

WTE: The recent Oneida-Herkimer Supreme Court Decision should encourage regional solid waste authorities to revisit the role of waste to energy as a waste management option. As remaining landfill capacity is exhausted in Bucks, Chester, Lehigh, Montgomery and Northampton counties there will be additional incentives for these regions to invest in waste to energy capacity. The Department will work with these counties to update their solid waste management plans to include waste to energy facilities. Concurrently, the Department will also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials. Subsequent efforts will focus on Allegheny, Berks, Lackawanna, and Luzerne counties as their remaining landfill capacity is exhausted.  These actions will result in the reduction of 4.05 MMTCOe.

Waste Transportation: Excessive waste disposal capacity and low tipping fees in western Pennsylvania encourage the long distance transportation of waste. The Waste Futures initiative will identify legislative, regulatory and other actions the Department can take to reduce excess waste disposal capacity. These actions will result in the reduction of 0.42 MMTCOe.

# Total Reductions: 9.87 MMTCO2e

Data Sources/Assumptions/Methods for Costs: From 2009-2011(?), WTE facilities will be supported by funds already committed to the solid waste program via the Recycling Fund.  These funds will not divert dollars away from the expanded recycling initiative because they come from a dedicated funding stream that is separate from recycling funding.  In 2015, it is assumed that significant market potential will have been created for WTE facilities that will cause counties and private industry to invest in construction to increase WTE capacity.  This market potential is a result potential profitability from: sale of electricity generated, funds earned through collection of tipping fees, and savings from avoided landfill construction costs.  The Department should work with PA counties to update their solid waste management plans to include waste to energy facilities. Concurrently, the Department should also work on legislative and regulatory changes to reduce or ban the disposal of certain types of materials.

Long-term actions include regulatory changes to further reduce obstacles to use of waste as an energy source.  The Waste Futures initiative will identify legislative, regulatory and other actions the Department can take to reduce excess waste disposal capacity.

The following table depicts implementation steps and targeted achievements for additional greenhouse gas reductions from solid waste management through 2025:

| YEAR | ACTION | % OF GOAL | GHG REDUCTION | COST ESTIMATE |
| --- | --- | --- | --- | --- |
| 2009 | Alternative Fuels - Increase use of alternative fuels by developing general permits for alternative fuels. |  | 2.5MMTCOe (baseline) | None |
|  | WTE – Work with counties to include WTE in their solid waste plans |  | 2.3 MMTCOe (baseline) | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2010 | Alternative Fuels - Increased use of waste as fuels by developing general permits for alternative fuels, start revising regulations to reduce obstacles to the use of waste as fuel. | 10% | 5.8 MMTCOe | None |
|  | WTE – Work with counties to include WTE in their solid waste plans. Initiate legislation and regulations to ban disposal of selected materials |  |  | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2012 | Alternative Fuels - Increased use of alternative fuels by finalizing regulations to reduce obstacles to the use of waste as fuel. | 25% | 7.3 MMTCOe | None |
|  | WTE - Legislation and Regulations in Place, Continue to update county plans. Counties will start process to construct additional WTE |  |  | The Department reimburses counties for 90% of the cost to revise county plans from the Recycling Fund. Annual costs are $850,000 |
| 2015 | WTE - Increased use of Waste to Energy. Additional waste to energy capacity of 2.6 million tons per year in place. | 50% | 9.8 MMTCOe | Approximately $700 - 900 million of public or private funds would be used to construct additional capacity. |
|  | Transportation - Reduce excess disposal capacity |  |  | None |
| 2020 | WTE - Increased use of Waste to Energy. Additional waste to energy capacity of 2.6 million tons per year in place. | 80% | 12.2 MMTCOe | Approximately $700 - 900 million of public or private funds would be used to construct additional capacity. |
| 2025 | Completion | 100% | 14.7 MMTCOe |  |

Potential Overlap:

- Increased Landfill Methane Capture Work Plan

- Fuels for Schools Work Plan

- Recycling Work Plan

- AEPS Tier I (@8%, 15%, 20%) Work Plans

Other Considerations/Notes:

Waste-4

Improved Efficiency at Wastewater Treatment Facilities

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact: Nicki Kasi (717) 772-4053

Initiative Summary:  Improving Efficiency at Wastewater Treatment Facilities through outreach programs based on Sustainable Infrastructure principals.

Goals:  Assist 6-8 treatment plans per year to improve efficiency

Implementation Period:  6-8 treatment plans per year starting in 2010? through 2020?

Parties Affected/Implementing Parties:  DEP, Outreach Assistance Provider Program (OAPP), Wastewater system owners/operators

Data sources/Assumptions/Methods for GHG:

The Office of Water Management proposes several methods to improve efficiency in order to maintain sustainable infrastructure (SI) within wastewater treatment systems.  The efficient use of energy is crucial for sustaining infrastructure and national security.  Electrical energy rate cap expirations set for 2010 further exacerbate this issue.

Wastewater treatment plants typically are the largest consumer of electricity on most municipal bills, often consuming more than 1/3 of the energy consumed for all municipal services.  In many instances, opportunities exist to reduce energy consumption at these facilities.  In order to assist treatment plants in improving efficiency, DEP provides outreach to these facilities, teaching system operators how to use the system in the most efficient manner for treatment and suggesting ways to reduce the amount of energy required to operate the facility.

There are three basic types of treatment plants in use today, activated sludge, fixed film and lagoon systems.  Of the many treatment facilities in Pennsylvania, approximately 70% are activated sludge facilities.  These facilities inject diffused air into an aeration basin to sustain a biological growth in order to treat the wastewater.  The aeration basins that these facilities require are the largest consumer of electricity in wastewater treatment systems.  Opportunities exist to improve efficiency in many of these facilities throughout the state.

The Outreach Assistance Provider Program (OAPP) uses part-time wage payroll instructors who are certified operators or specialists in a given field.  These instructors provide on-site technical, managerial, and financial assistance to wastewater system owners and operators.  The program responds to system needs identified by DEP regional staff, local government associations, or system personnel.  On-site assistance and training is provided through a combination of videos, classroom and web-based training, and one-on-one assistance to address specific system problems.  In the coming fiscal year,  OAPP  plans on accomplishing the following:

- Continuing on-site technical assistance for facilities requesting assistance with energy efficiency.   The average activated sludge wastewater treatment plant consumes 6,000 KWH per million gallons of wastewater treated.  At approximately $0.08 per KWH, the energy consumption is estimated at $500 per million gallons treated.  Using energy audits under the auspices of the OAPP, DEP proposes to assist 6 to 8 wastewater systems in reducing energy consumption in FY 2008-2009, with a focus on doing at least one per DEP region.  On average, these audits will result in an estimated annual energy savings of 10 to 15% in the cost of KWH per treatment plant.   It must be kept in mind that due to the relatively low cost of electricity in the past, the preference for wastewater treatment has been aerobic treatment processes.  This will no longer be the most cost-effective solution once the expected sharp increases in costs per KWHs take place.  Therefore, a further focus of this outreach effort will be to encourage and re-educate the owners and operators of wastewater treatment systems on the benefits of more energy efficient and effective wastewater treatment processes related to anaerobic treatment.

- Continuing collaboration with Central and Regional staff in providing training opportunities for operators in conjunction with various associations.

- Integrating the principles of SI in all technical assistance provided by the Outreach Assistance Provider Program.  This would include providing training in regard to all aspects of SI.

- Distributing the DVD on energy efficiency and other tools for SI.

- In conjunction with the Pennsylvania Water Environment Association, another special Nutrient Reduction Technology conference is scheduled for this fall in the Scranton area on September 10 - 12, 2008. This year’s conference will include energy efficiency, improvements to water quality and other principals of SI.

- Enhancements to the operator information center website "Technical Corner" as it relates to SI, energy efficiency and other operational issues.

The DEP Wastewater Outreach Program has provided assistance in energy efficiency since 1993.  Unfortunately, in the 1990's energy costs were not high enough to cause a significant amount of interest.  While we had several success stories in the past, many people simply were not tuned into the idea of energy efficiency.  In one case, we saved a municipality over $100,000 annually (approximately 6.0 MGD system).  By today's standards this type of savings would be greatly magnified.  With the pending expiration of electrical energy rate caps and the spiraling cost of oil, people are now starting to pay attention and ask questions.

Below are examples of our past accomplishments:

- On site technical assistance to Ridgeway Borough on energy efficiency and process control.  This project utilized the process of denitrification to save energy and chemical costs.  This process utilizes the nitrate that is produced in the process of nitrification for facultative organism respiration.   This results in improved water quality by reducing total nitrogen released to the receiving stream and saves money.  With an investment of $500, Ridgeway was able to document savings of $31,000 annually in energy and chemical costs in addition to improving the quality of their effluent.

- On site technical assistance to the City of Warren in regard to energy efficiency.  In this system older sparge ring diffusers were used for mixing and aeration.   By changing the cycles of mixing and aeration, the system could realize a savings of several thousand dollars per month.  This project is still underway.

- DEP Central and Regional office staff collaborated to produce a continuing education training program titled "Flush Away High Energy Costs".  In conjunction with PA Rural Water, this training session was piloted in the NW region and was well received by operators all over the region.  This session provides the operators with the tools they need to reduce energy costs within their system while maintaining or improving water quality.

- In 1996, a video was produced jointly between DEP, and the Maryland Center for Environmental Training in regard to energy efficiency in wastewater treatment systems.  In the past year, this video was upgraded and digitized to a DVD format so it can be widely distributed.

- A training session was held for DEP Central and Regional Office staff on energy efficiency in water/wastewater systems. This session was held in the State College area and followed a format similar to the operator training session known as "Flush Away High Energy Costs". This session will help regional staff to further spread the word in regard to energy efficiency.

- A special conference on Total Nutrient Reduction was held in the Lancaster area last fall.  This sold out event provided operators and managers with tools needed to improve reduction of nutrients and increase efficiency.

- Assistance was provided to program staff involved in a pilot project with Montgomery County Community College to create a certificate program focusing on water and wastewater treatment.   Based on the input provided, the pilot program will be modified to include basics of SI with an emphasis on energy efficiency, as well as effective process control.

All treatments plants produce excess solids, often referred to as sludge or biosolids.  These excess solids have to be treated before ultimate disposal. There are two basic types of treatment for these solids, aerobic digestion and anaerobic digestion.  Anaerobic treatment tends to be more energy neutral or even produce energy as the methane produced through this process can be used as a fuel.  Unfortunately, this technology is not used in many instances in Pennsylvania due to past problems with the operation, mostly due to problems in handling the gases produced in the treatment process.  Technology in this arena has improved in recent years, making the management of these systems safer and more efficient.  PA DEP currently has a pilot project in the works that will use anaerobic treatment and, depending on the outcome of this project, expects that other facilities may consider this option moving forward.

In the past fiscal year, we had several projects in this arena.  These projects are closely tied into the overall goal of SI.  In many cases, treatment systems have operated in a fashion set forth by previous generations where energy consumption was not a large concern.  Taking a moment and asking why we operate in this fashion can lead to significant opportunities for reduced energy costs and improved water quality.   By today's standard, any treatment facility that is required to nitrify should also consider denitrification, as it can lead to reduced operating costs, lower sludge production and improved water quality.

Based on past program performance, treatment facilities visited by this program tend to treat around 1 to 2 million gallons of water per day.  By visiting 6 to 8 facilities, it is expected that we will reach facilities that when combined, treat the equivalent of 6 to 7 million gallons of water treated per day.  Calculations on savings are as follows:

- 6,000 KWH/Million gallons treated x 1.5 million gallon/day facility = 9,000 Kwh/day

- 9,000 KWH x 365 days = 3,285,000 kWH/yr or 3,285 mWH/yr

Savings at these facilities is estimated at 10%, so

- 3,285 mWH/yr x .10 = 328.5 MWH savings per facility

Converting to CO2 emissions

- 328.5 MWH x 1278.9 (conversion factor) = 420,120 lbs/yr

Conversion to tons

- 420,120/2000  = 210 tons/year

- 210 x .907 (conversion factor) = 190.5 metric tons/yr per facility

By visiting 6 facilities per year we can save 1143 metric tons/year through this program or .001143 million metric tons of CO2e per year.

Data Sources/Assumptions/Methods for Costs:

Need clarification for costs to owners/operators.

- Cost to DEP

  - Energy efficiency is an integral part of the OAPP, where the cost for implementing this strategy will be minimal.  Interest in this program is expected to increase as people start to realize two factors, the first being that energy prices are rising sharply and second factor is that rate caps expire in 2010.  DEP is starting to receive more requests.

- Cost to Commonwealth

  - The cost here would be to do nothing.  Rising energy prices will force utilities to raise prices.  The most efficient first step is to use energy wisely.

- The savings realized by energy efficient measures could easily be used to fund improved water quality.  In fact, in cases where a facility starts using denitrification for the beneficial uptake of NO3, there would be a recovery of 60% of the cost of nitrification and improved water quality at the same time.  Cost savings are certain, and the savings could escalate as energy costs continue to rise.  It is a goal for systems to be self-sustaining in the water/wastewater industry.  The single largest cost for a wastewater system is the cost of aeration.  Fine bubble aeration could reduce those costs by 50%. This money could be incorporated into sustainable infrastructure.

Implementation Steps:  None.   This program is already in existence.

Potential Overlap:

- Most Electricity Sector Initiatives

Notes/Other Considerations:

Waste-5

Waste-to-Energy Digesters

Work Plan for Potential GHG Reduction Measure

Strategy Name: Waste-to-Energy Digesters

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary:  This initiative encourages an expansion of the basic on-farm or sewage treatment plant digester that can offer larger scale and higher technology treatment.

Goals:  Need specific goals

Implementation Period:  Need to know when goals would be reached

(for example: reach 50% of goal by 2015 and 100% of goal by 2020)

Parties Affected/Implementing Parties:  DEP, communities and local governments, businesses, food companies

Data sources/Assumptions/Methods for GHG:

Need data on digesters - how much they can digest, the amount of biogas produced

In the regional model,

- New feedstocks for digesters include food waste and yard waste as well as conventional manure and sludge.

- Waste-to-energy digesters produce electrical power along with high grade solid and liquid end-products.

- The business community can participate as both users and investors.

- Food companies would have an outlet for food waste.

- Concept expands upon local on-farm digesters that produce power for farm use and treated solid and liquid fertilizers.

Data Sources/Assumptions/Methods for Costs:  Need costs of implementation and costs of energy replaced

Implementation Steps:

Potential Overlap:

Notes/Other Considerations:

Waste-6

Waste-to-Energy MSW

Work Plan for Potential GHG Reduction Measure

Strategy Name: Waste-to-Energy Municipal Solid Waste

Lead Staff Contact: Kim Hoover (717-772-5161)

Summary:  This initiative encourages more waste-to-energy projects and waste volume in the energy mix.

Goals:  Need specific goals

Implementation Period:  Need to know when goals would be reached

(for example: reach 50% of goal by 2015 and 100% of goal by 2020)

Parties Affected/Implementing Parties:  DEP, power stations, ??

Data sources/Assumptions/Methods for GHG:

Need data on WTE GHG savings once there are specific goals in place

Data Sources/Assumptions/Methods for Costs:  Costs of implementing, $ million savings from energy displaced

Implementation Steps:

Potential Overlap:

Notes/Other Considerations:

# Footnotes

From Landfill Gas-to-Energy Economics by Tom Kerr, EPA Climate Protection Division

http://www.dep.state.pa.us/dep/deputate/airwaste/wm/recycle/waste_comp/study.htm

1.26 million tons waste as alternate fuel – from April 2003 R. W. Beck “Final Report: Statewide Waste Composition Study.” Used multiplier of 2 to yield 2.5 MMTCO2-e.

http://www.dep.state.pa.us//dep/subject/advcoun/solidwst/swac2007.htm

2.71 million tons municipal/residual waste - April 11, 2007 meeting – “Presentation on Waste-to-Energy. Link is “PPT.” 22-slide Power Point presentation. Slide 16 “Potential Supply of Alternative Fuels.” Used multiplier of 2 to yield 5.4 MMTCO2-e.

http://www.dep.state.pa.us//dep/subject/advcoun/solidwst/swac2007.htm

May 10, 2007 meeting – link is at “Waste as an Alternative Fuel” presented by Brian Bahor, Covanta Energy (23-slide Power Point presentation).

2.92 million tons of MSW is from slide 10 – 2005 data – EfW (Energy from Waste).

2.3 MMTCO2-e is from slide 13 – EfW 2.34 MMTCO2-e/year (Used a multiplier of 0.788 tons CO2-e generated per ton MSW combusted.).

http://www.depweb.state.pa.us/landrecwaste/cwp/view.asp?A=1216&Q=488974

link is at “2006 Residual Waste Biennial Report Data” (Excel spreadsheet – 2006_rw.xls).

5.3 million tons is probably combustible portion of the total 19.4 million tons of residual waste (“2006 PA RW” tab of spreadsheet).

Additional 4.1 MMTCO2-e is 0.788 times 5.2 million tons residual waste (same multiplier as that used by Covanta).

Based on 2006 county waste disposal information posted on DEP website.