| Number (temp.) From Summary of Work Plans | Grouping | Work Plan Industry | Implementation Period | Goals | Parties Affected | Implementing Parties | Data sources / assumptions / methods for GHGs | Data sources / assumptions / methods for Costs | Notes (including quantifiable and combinations |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Industry #1 |  | Coal Mine Methane (CMM) Recovery | Through 2025 | Capture 10% of methane by 2025, intermediate targets unspecified | Foundation and Consol 5 long wall mines | PA DEP Bur of Mining and Rec., Deep Mine Safety, US EPA Coalbed Methane Outreach Program (CMOP), MSHA. | coal production, assumption about ft3 methane/ton coal. | CMM electricity generation(?) / district or mine heating capital costs | Costs based on assumptions about CMM uses, baseline costs |
| Industry #2 |  | Industrial Natural Gas Consumption Best Management Practices | Through 2025 | Efficiency improvements of 5-25% in process heating, 5 to 15% in steam systems. Intermediate targets unspecified | Industrial fuel customers, energy service companies, utilities | US DOE, PA DEP | US EIA Mfg Energy Consumption Survey, PA market segmentation, industrial Gas Forecast | KEMA, ACEEE installed efficiency measure cost estimates | Quantification to include residual fuel oil, propane? What entities will perform assessments and benchmarking of best practices? |
| Industry #3 |  | Reduce Lost and Unaccounted for Natural Gas | 2010-2020 Linear implementation | Reduce fugitive gas emissions by 15%. | Gas utilities, electricity generators, PA PUC, EPA Gas Star Program, US DOT, construction companies (pipeline ruptures) | US EPA, PA PUC, PA DEP |  | Costs based on EPA Gas Star member costs |  |

Strategy Name:  Coal Mine Methane Recovery

Lead Staff Contact:  Robin G. Lighty (717-783-9588), email: rolighty@state.pa.us

Initiative Summary:  The release of methane gas to the atmosphere is a major component of Greenhouse Gas emissions.  Methane gas is a fossil fuel and energy source, commonly known as natural gas, which occurs in various geologic formations in Pennsylvania, including coal formations.  When coal is mined and processed for use, substantial amounts of methane gas are released.  Coal bed methane (CBM) is methane contained within coal formations and may be extracted by gas exploration methods or released as part of coal mining operations.  This workplan deals with coal mine methane (CMM), the methane within the coal that can be vented or recovered prior to mining the coal, during mining, and immediately after mining as some gas escapes to the service through post-mining vents or boreholes.  Methane gas that remains sequestered within an abandoned underground coal mine does not contribute to Greenhouse Gas emissions, but could be and sometimes is recovered by subsequent gas exploration operations.

Currently and in recent years approximately 85% of the methane gas released during the mining of coal in Pennsylvania occurs from mining in deep underground coal mines.  The five large longwall underground coal mines now operating in Pennsylvania extract more than 60% of the more than 68 million tons of coal mined each year.  These high amounts of longwall mine production and the fact that the longwall mines recover coal from greater depths than other mines, make longwall mining the predominant current source of coal mine methane release and an important contributor to Greenhouse Gas emissions.  The present capturing by industry of more than 10% of this gas within several of these large underground mines has already resulted in approximately an 8% reduction since 2000 in methane emissions from all coal mining in Pennsylvania.

Surface mining of coal currently releases about 9% of all coal mine methane emissions in Pennsylvania.  However, with the continuing drastic decline in annual surface mining production and the near final depletion of the state’s shallow coal reserves, there could be a reduction of coal mine methane emissions from surface mining of approximately 70% by 2025.

Other Involved Agencies:  N/A

Possible New Measure(s):

There are no specific measurements of methane gases released from mining at individual surface coal mine sites.  There are several published reports with estimates of methane released by surface coal mining activities.  This analysis uses the highest published emission factor per ton of coal mined.  This emission factor for surface and low-methane room and pillar underground mines is 127.1 cubic feet of methane released per ton of coal mined.  The high-level room and pillar underground mines emissions factor is 165 cu ft CH4 per ton of coal mined.  The longwall underground mines emission factor is 440 cu ft CH4 per ton of coal mined.  Estimates of coal mine methane released during mining is based on methane liberation and capture measurements recorded and provided by the coal industry and by the federal Mine Health and Safety Administration (MSHA), and on emission factor estimates published in the 2004 Emission Inventory Improvement Program Report, Vol. VIII, Chapter 4, “Methods for Estimating Methane Emissions from Coal Mining.”  These emission factors were applied to recently reported annual tons of coal mined and to projections of tonnages that are estimated to be mined in years 2010, 2015, 2020, and 2025.

The Coal Mine Methane Recovery Initiative would encourage owners/operators of current longwall mines, and of any new deep gaseous underground coal mine mined by any method, to capture 10% of the methane that is released into the atmosphere during and immediately after mining operations.

Projected 2025 Reduction (Million Metric Tons of CO2 Equivalents):

Concentrations of released methane are expressed as cubic feet per ton (2,000 lbs) of coal mined.  One unit of methane (cubic ft) is considered equal to 21 units (21 cubic ft) of CO2 equivalent Greenhouse Gas.  One million cubic feet of methane is equal to 404.5 metric tons of CO2 equivalent Greenhouse Gas.  Estimates of coal mine methane released during mining is based on methane liberation and capture measurements recorded and provided by the coal industry and by the federal Mine Health and Safety Administration (MSHA), and on emission factor estimates published in the 2004 Emission Inventory Improvement Program Report, Vol. VIII, Chapter 4, “Methods for Estimating Methane Emissions from Coal Mining.”  For all types of coal mines, the release of methane determined and predicted in this analysis is expressed as cubic feet of methane per ton of coal mined.  Total annual methane concentrations are also expressed as metric tons of CO2 equivalent.

Coal mine production for the years 2000 through 2008, and also 1997-1999 coal production used to determine 2025 estimates through trend analysis, are based on actual tonnages reported quarterly and annually to the DEP Bureau of Mining and Reclamation.  Coal mine production information is available to the public for the years 1980 through 2008 on the DEP Bureau of Mining and Reclamation website:

http://www.dep.state.pa.us/dep/deputate/minres/bmr/historicalminingreports/index.html

(Tables of Estimates and Projections for 2000 and 2025 are presented at end of this document.)

- Year 2000 Estimated Emissions (no Methane Capture):  10,142,393 metric tons CO2 equivalent

- Year 2025 Estimated Emissions (with 10% Methane Capture in Deep Gaseous Bituminous Underground Mines):  7,244,985 metric tons CO2 equivalent (28.6% decrease)

Total = 10.1 – 7.2 = 2.9 MMTCO2e Reduction

Economic Cost:  This initiative would be purely industry driven.

Implementation Steps:  The Commonwealth recommends that operators of deep gaseous underground coal mines continue to capture or begin capturing approximately 10% of the total coal mine methane by 2025.  This could be accomplished by pre-mining gas exploration into the coal formation to be mined, capturing methane during active underground mining operations, or possibly capturing methane from post-mining areas of underground mines, where for a brief period of time gas is still making its way to the surface through existing boreholes.  DEP annual coal production numbers and MSHA gas liberation numbers will be reassessed annually, as well as new technological developments, with revised trend forecasts on future coal production and revisions to estimates of methane gas released per ton of coal mined.

# Summary of Estimated and Projected Coal Mine Methane Emissions from Pennsylvania Coal Mines

|  | Methane |  | 2000 | 2000 | 2000 |
| --- | --- | --- | --- | --- | --- |
|  | Emission Factor |  |  | no capture |  |
|  | (cubic ft per ton) |  | tons | ft3 CH4 | MTCO2e |
| Anthracite Underground Mines | 127.1 |  | 220,462 | 28,020,720 | 11,334 |
| Anthracite Surface Mines | 127.1 |  | 2,332,828 | 296,502,439 | 119,935 |
| Bituminous Surface Mines | 127.1 |  | 14,936,924 | 1,898,483,040 | 767,936 |
| Room & Pillar Bituminous Underground Mines |  |  | 8,665,475 |  |  |
| Room & Pillar Mines with Low Methane | 127.1 |  | 5,805,868 | 737,925,855 | 298,491 |
| Room & Pillar Mines with High Methane | 165.0 |  | 2,859,607 | 471,835,114 | 190,857 |
| Longwall Bituminous Underground Mines | 440.0 |  | 49,184,398 | 21,641,135,120 | 8,753,839 |
| Totals for Coal Mining in Pennsylvania |  |  | 75,340,087 | 25,073,902,288 | 10,142,393 |

|  | Methane |  | 2025 | 2025 | 2025 |
| --- | --- | --- | --- | --- | --- |
|  | Emission Factor |  |  | no capture |  |
|  | (cubic ft per ton) |  | tons | ft3 CH4 | MTCO2e |
| Anthracite Underground Mines | 127.1 |  | 100,000 | 12,710,000 | 5,141 |
| Anthracite Surface Mines | 127.1 |  | 800,000 | 101,680,000 | 41,130 |
| Bituminous Surface Mines | 127.1 |  | 4,400,000 | 559,240,000 | 226,213 |
| Room & Pillar Bituminous Underground Mines |  |  | 10,000,000 |  |  |
| Room & Pillar Mines with Low Methane | 127.1 |  | 6,666,667 | 847,333,376 | 342,746 |
| Room & Pillar Mines with High Methane | 165.0 |  | 3,333,333 | 549,999,945 | 222,475 |
| Longwall Bituminous Underground Mines | 440.0 |  | 40,000,000 | 17,600,000,000 | 7,119,200 |
| Totals for Coal Mining in Pennsylvania |  |  | 55,300,000 | 19,670,963,321 | 7,956,905 |

|  | Methane |  | 2025 | 2025 | 2025 |
| --- | --- | --- | --- | --- | --- |
|  | Emission Factor |  | 10% capture in deep bituminous mines |
|  | (cubic ft per ton) |  | tons | ft3 CH4 | MTCO2e |
| Anthracite Underground Mines | 127.1 |  | 100,000 | 12,710,000 | 5,141 |
| Anthracite Surface Mines | 127.1 |  | 800,000 | 101,680,000 | 41,130 |
| Bituminous Surface Mines | 127.1 |  | 4,400,000 | 559,240,000 | 226,213 |
| Room & Pillar Bituminous Underground Mines |  |  | 10,000,000 |  |  |
| Room & Pillar Mines with Low Methane | 127.1 |  | 6,666,667 | 847,333,376 | 342,746 |
| Room & Pillar Mines with High Methane | 165.0 |  | 3,333,333 | 549,999,945 | 222,475 |
| Longwall Bituminous Underground Mines | 440.0 |  | 40,000,000 | 15,840,000,000 | 6,407,280 |
| Totals for Coal Mining in Pennsylvania |  |  | 55,300,000 | 17,910,963,321 | 7,244,985 |

Lead Staff Contact:  Richard Illig (717) 772-5834

Summary:  Implement DOE Industrial Technology Program (ITP) Best Management Practices (BMPs) to process heating and steam system operation to reduce the consumption of natural gas or other fossil fuels, such as coal and oil by 5-15% per year for industrial steam systems, and 5-25% for process heating systems.  Program begins in the year XX through 2025.  Interim targets for industrial gas consumption are XX% in the year XX.

Other Involved Agencies:  U.S. DOE and PADEP

Possible New Measures:  By implementing DOE BMPs, the DEP expects efficiency improvements between 5 to 25 percent and between 5 to 15 percent can be achieved in industrial process heating and steam systems, respectively.

The direct combustion of fossil fuel such as natural gas, fuel oil, and coal comprise 92 percent of the energy used in industrial process heating systems.  The Energy Information Administration reports U.S. industrial energy consumption in 2005 was 1,297,799BBtu.  Process heating reportedly used 17 percent of the total energy use or 220,625,000MMBtu.  Fossil fuel combustion then equals 202,975,000MMBtu in 2005 for process heating.

The thermal efficiency of process heating equipment varies broadly between 15 and 80 percent.  This large range in efficiency allows fuel reduction opportunities between 5 to 25 percent through the application of ITP best operational practices.

The direct combustion of fossil fuels such as natural gas, fuel oil, and coal comprise at least 71 percent of the boiler fuels used to raise steam for industrial processes.  The inclusion of propane and waste fuels is estimated to increase this percentage to at least 85 percent.

The Energy Information Administration reports industrial energy consumption in 2005 as 1,297,799BBtu.  An estimated 45 percent of industrial energy use is used to raise steam or 584,009,000MMBtu.  Fossil fuel combustion in 2005 should then equal about 496,407,650MMBtu for steam systems.

The thermal efficiency of industrial steam systems reportedly range from 65 to 85 percent.  This range in efficiency allows fuel reduction opportunities between 5 to 15 percent through the application of ITP BMPs.

Process Heating Best Management Practices

| System Aspect | Savings Potential (%) | Typical Payback (months) | Cost Range |
| --- | --- | --- | --- |
| Heat Generation | 5 - 25 | 1 - 6 |  |
| Minimize excess air |  |  | Nominal |
| Control air-fuel ratio |  |  | Nominal |
| Minimize air leakage |  |  | Nominal - Low |
| Heat Transfer | 5 - 15 | 3 - 12 |  |
| Burner selection & furnace design |  |  | Moderate - High |
| Replace indirect heating systems |  |  | Moderate - High |
| Heat Containment | 2 - 15 | 3 - 12 |  |
| Optimize insulation |  |  | Low - Moderate |
| Maintain door and tube seals |  |  | Nominal |
| Heat Recovery | 10 - 25 | 3 - 6 |  |
| Pre-heat combustion air |  |  | Moderate |
| Preheat or dry load |  |  | Moderate |
| Cascade heat to second process |  |  | Moderate |
| Sensors / Controls | 5 - 15 | 1 - 6 |  |
| Routine calibration or maintenance |  |  | Low |
| Proper location |  |  | Low |
| Process Modeling and Tools | 5 - 10 | 1 - 6 |  |
| Temperature settings / part load operation |  |  | Low |
| Advanced Materials | 10 - 25 | 1 - 3 |  |
| Load support materials and design |  |  | Moderate |

Steam System Best Practices

| System Aspect | Savings Potential (%) | Typical Payback (months) | Cost Range |
| --- | --- | --- | --- |
| Generation | 5 - 15 | 1 - 12 |  |
| Minimize excess air |  |  | Nominal |
| Control air-fuel ratio |  |  | Nominal |
| Clean heat transfer surfaces |  |  | Low |
| Improve water treatment |  |  | Low - Moderate |
| Maintain refractory |  |  | Moderate - High |
| Optimize de-aeration |  |  | Low - Moderate |
| Condensate recovery |  |  | Low - Moderate |
| Distribution | 5 - 15 | 1 - 12 |  |
| Optimize insulation |  |  | Low - Moderate |
| Leak repair |  |  | Low |
| Minimize venting |  |  | Low |
| Steam trap maintenance |  |  | Moderate |
| Close unused lines |  |  | Nominal |
| Replace PRVs w/backpressure turbine |  | Longer than 1-year | High |
| Convert high-pressure condensate to low-pressure steam |  |  | Moderate |
| End Use | 5 - 10 | 1 - 12 |  |
| Minimize pressure |  |  | Nominal |
| Heat Recovery | 5 - 15 | 6 - 18 |  |
| Install economizer |  |  | Moderate |
| Pre-heat combustion air |  |  | Moderate |
| Blowdown heat capture |  |  | Moderate |

Potential GHG Reduction: Pennsylvania’s industrial energy use has declined over the past decade both in terms of the number of customers and total natural gas consumption.  Flat growth or possibly a continued decline in the natural gas market is expected through 2025.  This is in part due to the development of alternative energy systems and potentially increased equipment efficiency.

If industrial process heating consumes 202,975,000MMBtu annually a 5 to 25 percent reduction could save between 10,148,750MMBtu and 50,743,750MMBtu.  Assuming a 15 percent average reduction yields 30,446,250MMBtu.

If industrial steam systems consume 496,407,650MMBtu annually a 5 to 15 percent reduction could save between 24,820,382MMBtu and 74,461,147MMBtu.  Assuming a 10 percent average reduction yields 49,640,765MMBtu.

Total energy savings from the implementation of process heating and steam system best operational practices could equal 30,446,250MMBtu + 49,640,765MMBtu or 80,087,015MMBtu.  Fossil fuel equivalents equal:

- Over 572 million gallons #2 fuel oil

- Over 3.2 million tons of coal

- Over 80,087 million cubic feet of natural gas

Emission reduction is estimated as MMTCO2E/yr = 4.02257.  (Tons CO2/yr = 4,657,981)

Economic Costs:

- Efficiency improvement costs (that result in fuel savings up to 10%) are very low and often part of routine maintenance costs

- 10 to 15 percent fuel savings may result from small to medium cost system improvements

- Fuel savings greater than 20 percent may result from medium to high cost system improvements

- Energy savings pay back time frames are typically very good.

Savings Identified by Industry U.S. DOE Energy Assessments

| Industry (# assessed) | Average Energy-Savings (MMBtu/yr) | Avg. Savings ($/yr) |
| --- | --- | --- |
| Chemicals (1) | 330,000 | $1,565,000 |
| Forest Products (5) | 199,500 | $366,000 |
| Mining (2) | 20,100 | $102,500 |
| Petroleum (3) | 98,500 | $466,000 |
| Steel (2) | 226,700 | $690,000 |

Implementation Steps

- Conduct DOE workshops that advance best practice implementation for process heating and steam systems.

- Advance the use of DOE process heating and steam system analysis tools.

- Require assessment and benchmarking of all process heating and steam systems utilizing state and federal assessment resources.

- Require review, and implementation when cost effective, of best practices for all large natural gas systems.

- Curtail service to any large un-assessed process heating or steam system in an emergency.

- Partner with utilities to develop energy use reduction programs for large energy users.

Potential Overlap

- Lost and Unaccounted for Natural Gas, Landfill Methane Capture, Recycling, Solid Waste, etc.

Lead Staff Contact: Mark Hand (717) 787-9377

Summary: Reduce lost and unaccounted (L&U) for natural gas from retail operations by 15% by the year 2020.  The program begins in the year 2010 and fugitive emissions are assumed to be implemented linearly.

Other Involved Agencies: PUC, U.S. Department of Transportation, and EPA Gas STAR Program

Possible New Measure(s): Reduce Lost and Unaccounted for Natural Gas from retail operations by 15% through various actions, such as: improved operation and maintenance, replacement of aging pipes, replacement of inaccurate metering, reducing the number of accidental line breaks and thefts, and requiring more accurate reporting of L&U natural gas. Reported L&U natural gas in 2005 was 19.6 billion cubic feet.

Natural Gas Consumers in Pennsylvania – 2,839,282

Residential – 2,600,574 (91 percent)

Commercial – 233,132 (8 percent)

Industrial – 5,576 (0.2 percent)

Pennsylvania Natural Gas Consumption by End User:

Residential – 245 Bcf (40 percent)

Commercial – 145 Bcf (24 percent)

Industrial – 185 Bcf (30 percent)

Electric Power Generation – 33 Bcf (6 percent)

Natural gas (NG) companies report L&U natural gas to the Public Utility Commission.  The American Gas Association defines L&U as the difference between the total gas available from all sources, and the total gas accounted for as sales, net interchange, and company use. It is important to reduce natural gas losses because natural gas (methane) is approximately 21 times more powerful greenhouse gas emission than carbon dioxide.

NG is released to the atmosphere through fugitive and vented emissions. Fugitive emissions are methane leaks often through pipeline and system components (such as compressor seals, pump seals, and valve packing). Vented emissions are methane leaks from a variety of equipment and operational practices directly attributed to an organization’s actions (e.g., purge and blow down activities from operation) or accidental line breaks/thefts.

The reported L&U values are not accurately estimating gas companies’ individual contributions to fugitive or vented emissions for the following reasons:

- End-use consumer meters (likely to be residential sector meters) do not accurately measure delivered volumes. This is because some meters do not accurately account for temperature and pressure sensitivities. It is thought that consumer meters are approximately + or – 3% in measurement accuracy.

- Natural gas companies use a portion of their product in various stages of the transmission process (i.e. compressors), which is not separately quantified.

- Gas theft may also be occurring, although it is assumed to be a relatively minor loss with regard to L&U reporting.

- The PUC does not have standardized calculation/reporting procedures for L&U. Some utilities report gains instead of losses in L&U. This means that it is not possible to draw conclusions from the PUC’s statewide L&U statistics.

- The PUC indicates there are approximately 6,000 line breaks per year due to accidents (i.e. digging-up a line during construction). These individual accidents that cause releases have not been quantified.

Therefore there are three primary areas that need to be addressed to improve our understanding L&U natural gas:

- Accurate measurement and reporting;

- Operations and maintenance improvements (or replacements) to lines and aging parts; and

- Minimization of accidental losses through line breaks.

Projected 2025 Reduction: 		0.2 MMT CO2e

| Lost & Unaccounted-for Natural Gas for Major Pennsylvania Gas Distribution Utilities + |  |  |  |
| --- | --- | --- | --- |
| Company | Total Lost & Unaccounted-for (mcf) | Total Deliveries (mcf) | Percent L & U |  |  | Assume 15% of L & U is Preventable |
| Columbia | 1,252,493 | 112,953,730 | 1.1% |  | 15% | 2,939,754.90 |
| Dominion - Peoples | 4,767,103 | 93,059,502 | 5.1% |  | CO2e MM Tons** | 161,143 |
| Equitable | 6,871,103 | 67,142,740 | 10.2% |  |  |  |
| National Fuel | 163,550 | 53,079,559 | 0.3% |  | ** At equivalent 120.593 lb/mcf |
| PECO Gas | 2,493,685 | 87,908,874 | 2.8% |  |  |  |
| PG Energy * | 119,512 | 48,117,054 | 0.2% |  |  |  |
| Phila. Gas Works | 3,106,403 | 91,469,723 | 3.4% |  |  |  |
| PPL Gas | 1,203,005 | 27,642,650 | 4.4% |  |  |  |
| UGI - Gas* | (378,488) | 95,817,773 | -0.4% |  |  |  |
| Totals | 19,598,366 | 677,191,605 | 2.9% |  |  |  |
| + There are no PUC standards for lost and unaccounted for gas |  |  |  |
| * Both companies, owned by UGI, report in a way that results in little or even negative lost gas. The PUC staff has proposed that reporting be standardized… |  |  |  |

Economic Cost: The PUC states that about 12,000 miles of aging gas mains need replacing (3,278 miles of cast iron, 8,907 miles of unprotected bare steel-see table below).   The estimated cost of replacing gas mains is $1 million/mile.  Assuming a straight-line relationship between lost gas and pipe replacement, this is approximately $12 billion. It is also expected to take approximately 20 years, at normal levels of replacement, to complete these replacements. The PUC believes there may be future federal government requirements to eliminate these older pipes.  Pipeline replacements are not assumed to be performed solely due to the GHG benefits under this measure, but rather due to other regulatory requirements and business operations decisions.

Pennsylvania Distribution Sector – Report on Cast Iron and Unprotected Steel

|  | Miles of | Miles of | Total Miles | % of Statewide | % of Statewide |
| --- | --- | --- | --- | --- | --- |
|  | Cast Iron | Unprotected | Distribution | Total Cast Iron | Total Unprotected |
| Company |  | Bare Steel |  |  | Bare Steel |
| Columbia Gas of PA | 74 | 2,188 | 7,260 | 2.3% | 25% |
| Dominion Peoples | 66 | 1,908 | 6,566 | 2.0% | 21% |
| Equitable Gas | 47 | 830 | 3,307 | 1.4% | 9% |
| National Fuel Gas | 93 | 1,051 | 4,916 | 2.8% | 12% |
| PECO | 836 | 369 | 6,614 | 25.5% | 4% |
| UGI Penn Natural | 82 | 305 | 2,562 | 2.5% | 3% |
| PGW | 1,624 | - | 3,019 | 49.5% | 0% |
| PPL Gas | 28 | 661 | 3,619 | 0.9% | 7% |
| T.W. Phillips | - | 1,295 | 2,955 | 0.0% | 15% |
| UGI | 428 | 300 | 5,012 | 13.1% | 3% |

Replacing all customer meters with “temperature and pressure compensated” meters may cost $100 per meter (PUC estimate). There are about 2.6 million households using natural gas (not including commercial and industrial consumers which may have temperature/pressure meters). This will result in improved metering and a reduction in the measuring of L&U.

Improved reporting requirements from all utilities on L&U losses. This would require PUC staff to develop standardized accurate reporting methods.

Reduce accidental line breaks throughout Pennsylvania. Stricter enforcement of the Pennsylvania One Call System could help reduce these losses. This could require additional staff time to enforce, but may be offset by fines and penalties.

Encourage utilities to participate in existing voluntary industry programs. EPA’s Natural Gas STAR Program is focused on reducing methane emissions through technology transfer using best practices in operation and maintenance.  Natural Gas STAR provides analytical tools and services to assist in calculating companies methane emissions.

Implementation Steps:

- Encourage utilities to regularly perform self-assessments and report (to the PUC) operation and maintenance practices that have resulted in environmental savings.

- Require improved and standardized reporting to the PUC on L&U, so that atmospheric system losses can be better understood and separated from non-atmospheric losses.

- Investigate the savings from increased enforcement of the Pennsylvania One Call system.

- Possible phase-out of older metering devices with more accurate “pressure and temperature compensated” metering.

Potential Overlap:

- Demand Side Management – Natural Gas

- Increased Use of Landfill Methane

# Footnotes

Statistics taken from U.S. DOE Energy Information Administration

Units of measurement: MMBtu = million Btu; BBtu = billion Btu; MMTCO2E = million metric tons CO2 equivalent.

See http://www1.eere.energy.gov/industry/bestpractices/pdfs/em_proheat_bigpict.pdf

See http://industrial-energy.lbl.gov/files/industrial-energy/active/0/Steam%20Sourcebook.pdf

US EPA. (2007). Project Opportunities Study for Partner X. Natural Gas Star Program.

Gas Consumers and Gas Consumption information was provided through an American Gas Association query - 2005 Data.

Developed by the PUC using U.S. Department of Transportation Data

# Text boxes

Industry 3: Reduce Lost and Unaccounted for Natural Gas

Work Plan for Potential GHG Reduction Measure

Industry 1: Coal Mine Methane Recovery

Work Plan for Potential GHG Reduction Measure

Industry 2: Industrial Natural Gas Consumption Best Management Practices Work Plan for Potential GHG Reduction Measure