Industrial Natural Gas Consumption Best Management Practices

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact:  Richard Illig (717) 772-5834

Summary:  Implement DOE Industrial Technology Program (ITP) Best Management Practices (BMPs) to process heating and steam system operation to reduce the consumption of natural gas or other fossil fuels, such as coal and oil.

Other Involved Agencies:  U.S. DOE and PADEP

Possible New Measures:  By implementing DOE BMPs, the DEP expects efficiency improvements between 5 to 25 percent and between 5 to 15 percent can be achieved in industrial process heating and steam systems, respectively.

The direct combustion of fossil fuel such as natural gas, fuel oil, and coal comprise 92 percent of the energy used in industrial process heating systems.  The Energy Information Administration reports U.S. industrial energy consumption in 2005 was 1,297,799BBtu.  Process heating reportedly used 17 percent of the total energy use or 220,625,000MMBtu.  Fossil fuel combustion then equals 202,975,000MMBtu in 2005 for process heating.

The thermal efficiency of process heating equipment varies broadly between 15 and 80 percent.  This large range in efficiency allows fuel reduction opportunities between 5 to 25 percent through the application of ITP best operational practices.

The direct combustion of fossil fuels such as natural gas, fuel oil, and coal comprise at least 71 percent of the boiler fuels used to raise steam for industrial processes.  The inclusion of propane and waste fuels is estimated to increase this percentage to at least 85 percent.

The Energy Information Administration reports industrial energy consumption in 2005 as 1,297,799BBtu.  An estimated 45 percent of industrial energy use is used to raise steam or 584,009,000MMBtu.  Fossil fuel combustion in 2005 should then equal about 496,407,650MMBtu for steam systems.

The thermal efficiency of industrial steam systems reportedly range from 65 to 85 percent.  This range in efficiency allows fuel reduction opportunities between 5 to 15 percent through the application of ITP BMPs.

Process Heating Best Management Practices

| System Aspect | Savings Potential (%) | Typical Payback (months) | Cost Range |
| --- | --- | --- | --- |
| Heat Generation | 5 - 25 | 1 - 6 |  |
| Minimize excess air |  |  | Nominal |
| Control air-fuel ratio |  |  | Nominal |
| Minimize air leakage |  |  | Nominal - Low |
| Heat Transfer | 5 - 15 | 3 - 12 |  |
| Burner selection & furnace design |  |  | Moderate - High |
| Replace indirect heating systems |  |  | Moderate - High |
| Heat Containment | 2 - 15 | 3 - 12 |  |
| Optimize insulation |  |  | Low - Moderate |
| Maintain door and tube seals |  |  | Nominal |
| Heat Recovery | 10 - 25 | 3 - 6 |  |
| Pre-heat combustion air |  |  | Moderate |
| Preheat or dry load |  |  | Moderate |
| Cascade heat to second process |  |  | Moderate |
| Sensors / Controls | 5 - 15 | 1 - 6 |  |
| Routine calibration or maintenance |  |  | Low |
| Proper location |  |  | Low |
| Process Modeling and Tools | 5 - 10 | 1 - 6 |  |
| Temperature settings / part load operation |  |  | Low |
| Advanced Materials | 10 - 25 | 1 - 3 |  |
| Load support materials and design |  |  | Moderate |

Steam System Best Practices

| System Aspect | Savings Potential (%) | Typical Payback (months) | Cost Range |
| --- | --- | --- | --- |
| Generation | 5 - 15 | 1 - 12 |  |
| Minimize excess air |  |  | Nominal |
| Control air-fuel ratio |  |  | Nominal |
| Clean heat transfer surfaces |  |  | Low |
| Improve water treatment |  |  | Low - Moderate |
| Maintain refractory |  |  | Moderate - High |
| Optimize de-aeration |  |  | Low - Moderate |
| Condensate recovery |  |  | Low - Moderate |
| Distribution | 5 - 15 | 1 - 12 |  |
| Optimize insulation |  |  | Low - Moderate |
| Leak repair |  |  | Low |
| Minimize venting |  |  | Low |
| Steam trap maintenance |  |  | Moderate |
| Close unused lines |  |  | Nominal |
| Replace PRVs w/backpressure turbine |  | Longer than 1-year | High |
| Convert high-pressure condensate to low-pressure steam |  |  | Moderate |
| End Use | 5 - 10 | 1 - 12 |  |
| Minimize pressure |  |  | Nominal |
| Heat Recovery | 5 - 15 | 6 - 18 |  |
| Install economizer |  |  | Moderate |
| Pre-heat combustion air |  |  | Moderate |
| Blowdown heat capture |  |  | Moderate |

Potential GHG Reduction: Pennsylvania’s industrial energy use has declined over the past decade both in terms of the number of customers and total natural gas consumption.  Flat growth or possibly a continued decline in the natural gas market is expected through 2025.  This is in part due to the development of alternative energy systems and potentially increased equipment efficiency.

If industrial process heating consumes 202,975,000MMBtu annually a 5 to 25 percent reduction could save between 10,148,750MMBtu and 50,743,750MMBtu.  Assuming a 15 percent average reduction yields 30,446,250MMBtu.

If industrial steam systems consume 496,407,650MMBtu annually a 5 to 15 percent reduction could save between 24,820,382MMBtu and 74,461,147MMBtu.  Assuming a 10 percent average reduction yields 49,640,765MMBtu.

Total energy savings from the implementation of process heating and steam system best operational practices could equal 30,446,250MMBtu + 49,640,765MMBtu or 80,087,015MMBtu.  Fossil fuel equivalents equal:

- Over 572 million gallons #2 fuel oil

- Over 3.2 million tons of coal

- Over 80,087 million cubic feet of natural gas

Emission reduction is estimated as MMTCO2E/yr = 4.02257.  (Tons CO2/yr = 4,657,981)

Economic Costs:

- Efficiency improvement costs (that result in fuel savings up to 10%) are very low and often part of routine maintenance costs

- 10 to 15 percent fuel savings may result from small to medium cost system improvements

- Fuel savings greater than 20 percent may result from medium to high cost system improvements

- Energy savings pay back time frames are typically very good.

Savings Identified by Industry U.S. DOE Energy Assessments

| Industry (# assessed) | Average Energy-Savings (MMBtu/yr) | Avg. Savings ($/yr) |
| --- | --- | --- |
| Chemicals (1) | 330,000 | $1,565,000 |
| Forest Products (5) | 199,500 | $366,000 |
| Mining (2) | 20,100 | $102,500 |
| Petroleum (3) | 98,500 | $466,000 |
| Steel (2) | 226,700 | $690,000 |

Implementation Steps

- Conduct DOE workshops that advance best practice implementation for process heating and steam systems.

- Advance the use of DOE process heating and steam system analysis tools.

- Require assessment and benchmarking of all process heating and steam systems utilizing state and federal assessment resources.

- Require review, and implementation when cost effective, of best practices for all large natural gas systems.

- Curtail service to any large un-assessed process heating or steam system in an emergency.

- Partner with utilities to develop energy use reduction programs for large energy users.

Potential Overlap

- Lost and Unaccounted for Natural Gas, Landfill Methane Capture, Recycling, Solid Waste, etc.

# Footnotes

Statistics taken from U.S. DOE Energy Information Administration

Units of measurement: MMBtu = million Btu; BBtu = billion Btu; MMTCO2E = million metric tons CO2 equivalent.

See http://www1.eere.energy.gov/industry/bestpractices/pdfs/em_proheat_bigpict.pdf

See http://industrial-energy.lbl.gov/files/industrial-energy/active/0/Steam%20Sourcebook.pdf