Pennsylvania CCAC

Res/Com subcommittee, April 17, 2009

We are looking for input from the Res/Com subcommittee on the performance goals for buildings – note that these will cover a number of individual workplans, each moving toward the overall goal.

Performance Goals for Buildings

Overall goals (based on Architecture 2030 GHG goals), these values provide specific energy savings and years and were suggested as high level goal. Policies needed to achieve the goals will require links to specific building performance standards or technologies (see below)

- All new buildings, developments and major renovations shall be designed to meet a fossil fuel, GHG-emitting, energy consumption performance standard of 50% of the regional (or country) average for that building type.

- At a minimum, an equal amount of existing building area shall be renovated annually to meet a fossil fuel, GHG-emitting, energy consumption performance standard of 50% of the regional (or country) average for that building type.

- The fossil fuel reduction standard for all new buildings shall be increased to:

60% in 2010
70% in 2015
80% in 2020
90% in 2025 
Carbon-neutral in 2030 (using no fossil fuel GHG emitting energy to operate).

These targets may be accomplished by implementing innovative sustainable design strategies, generating on-site renewable power and/or purchasing (20% maximum) renewable energy and/or certified renewable energy credits.

The following tables report on the overall goal, and suggestions for building performance standards for four building types (commercial (private), commercial (Commonwealth-funded/operated), commercial (schools/colleges/universities) plus differences for new and existing.

New Buildings Goals and standards

|  |  | 2010 | 2020 | 2030 |
| --- | --- | --- | --- | --- |
| New Commercial (private) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 75 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildings |
| New Commercial (Commonwealth owned or operated) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 85 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildngs |
| New Commercial (Schools) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | LEED Silver ENERGY STAR 85 | LEED Silver ENERGY STAR 85 | ?? |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildngs |
| New Residential | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | HERS 50 | HERS 40 | HERS 30 |
|  | Fraction of buildings that meet standard | 100% of new buildings | 100% of new buildings | 100% of new buildngs |

Notes: Overall goals reflect 2030 GHG goals

Looking for input from subcommittee on Performance standards that will help set policies to achieve the Overall goals

Fraction of buildings that meet standard is currently set to 100% to reflect a mandate policy (rather than incentives that would likely reach a smaller fraction of buildings)

Existing Buildings Goals and standards

|  |  | 2010 | 2020 | 2030 |
| --- | --- | --- | --- | --- |
| Existing Commercial (private) | Overall goal (relative to 2007 building) | 50% fossil fuel reduction | 50% fossil fuel reduction | 50% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
| Existing Commercial (Commonwealth owned or operated) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
| Existing Commercial (Schools) | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 | LEED EB Silver ENERGY STAR 75 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |
| Existing Residential | Overall goal (relative to 2007 building) | 60% fossil fuel reduction | 80% fossil fuel reduction | 100% fossil fuel reduction |
|  | Performance standard | HERS 50 | HERS 50 | HERS 50 |
|  | Fraction of buildings that meet standard | 20% of existing buildings | 50% of existing buildings | 100% of existing buildings |

Notes: Overall goals reflect 2030 GHG goals

Looking for input from subcommittee on Performance standards that will help set policies to achieve the Overall goals

Fraction of buildings that meet standard is currently set to 100% to reflect a mandate policy (rather than incentives that would likely reach a smaller fraction of buildings)

INFORMATION SOURCES

Center for Climate Strategies requires additional information to estimate the costs for building and renovating homes and buildings to meet the performance standardsr.

Resources that will be reviewed include

ACEEE 2009. Potential for Energy Efficiency, Demand Response, and Onsite Solar energy in Pennsylvania.

[provides Levelized Cost of Saved Energy (capital cost of energy efficiency improvements divided by amount of energy saved over lifetime of equipment. The following estimates are provided:

| Electricity | Levelized Cost of Saved Energy ($/kWh) |
| --- | --- |
| Residential – Improved Housing Shell Performance | $0.021 |
| Residential – single family, HVAC equipment | $0.005 |
| Residential – multi family, HVAC equipment | $0.01 |
| Commercial - heating and cooling (building shell) | $0.013 |
| Commercial - heating and cooling (equipment) | $0.028 |

| Natural gas | Levelized Cost of Saved Energy ($/BTU) |
| --- | --- |
| Residential – single family, space heating | $3.70 |
| Residential – single family, water heating | $7.90 |
| Residential – multi family, space heating | $6.86 |
| Residential – multi family, water heating | $3.04 |
| Commercial - heating and cooling (building shell) | $0.30 |
| Commercial - heating and cooling (equipment) | $2.39 |

Green Building Costs and Financial Benefits – Gregory Katz 2003

http://www.cap-e.com/ewebeditpro/items/O59F3259.pdf

PLEASE PROVIDE OTHER SOURCES OF FINANCIAL COSTS AND BENEFITS OF GREEN BUILDINGS