Statewide Recycling Initiative

Work Plan for Potential GHG Reduction Measure

Lead Staff Contact:	Gregory Harder (717) 787-0114

Larry Holley (717) 787-7382

Initiative Summary:  Support the expansion of statewide recycling to increase the amount of materials recycled and achieve GHG reductions equivalent to 86% of the Commonwealth’s total recycling potential.

Other Involved Agencies: N/A

Possible New Measure(s): Based on data analyzed by the Northeast Recycling Council’s (NERC) Environmental Benefits Calculator, Pennsylvania saved 2.5 million metric tons of carbon equivalent (MMTCE) or 9 million metric tons of carbon dioxide equivalent (MMTCO2e) as a result of recycling approximately 4.9 million tons of materials in 2005.  There is potential to reduce an additional 2.9 MMTCE or 11 MMTCO2e assuming the recycling of an additional 4 million tons of Pennsylvania generated recyclables identified as discarded in landfills and incinerators by the Statewide Municipal Waste Composition Study (April 2003).

More than 5.4 million MMTCE or 20 MMTCO2e could be avoided annually if recyclable materials being disposed were added to the materials presently recovered from the municipal waste stream through recycling programs in the Commonwealth.  These materials include newspaper, corrugated cardboard, office paper, magazines, mixed paper, plastic bottles, film plastic, rigid plastic, glass, steel and aluminum cans, steel scrap and other metals.  Additional savings above and beyond this projection could be realized if comprehensive programs were developed for the collection and recycling of wood waste, textiles, and carpet.

Energy conserved from manufacturing products using recycled feedstock rather than virgin raw materials, or non-renewable resources, resulted in the savings of 98 trillion British Thermal Units of energy in 2005, enough to power over 941,000 Pennsylvania homes for year or the equivalent of conserving 786 million gallons of gasoline.

Emission and energy credit accrued by our recycling efforts could be recognized as a tradable commodity that may help achieve the Commonwealth's sustainability goals.

PA DEP could target recycling programs to specifically begin or increase collecting those materials that provide the maximum greenhouse gas reductions.  To further stimulate recycling opportunities, PA DEP could ultimately ban those materials from disposal or processing.  Aluminum, steel, plastics, cardboard and paper should be initially targeted as these materials will yield the greatest reductions.

Act 101, the Municipal Waste, Planning Recycling and Waste Act Reduction of 1988, provides the foundation for recycling that has resulted in comprehensive environmental and economic benefits for Pennsylvania.  The Act provides for a $2 per ton recycling fee on waste disposed or processed at municipal waste landfills and resource recovery facilities in the Commonwealth.  The Recycling Fee generates approximately $47 million dollars annually to a Recycling Fund administered by Pa. DEP.  The Recycling Fund provides support to local governments for implementation of recycling programs.  The Recycling Fee also supports the stimulation of markets for recyclable materials. The Department is focusing Act 101 funds on programs geared towards financial sustainability including those that are targeting new materials that were previously disposed.  Increasing the amount of materials recycled will provide direct reduction in greenhouse gas emissions.

Pennsylvania’s recycling program provides annual economic benefits in excess of $23 billion and nearly 82,000 jobs (National Recycling Council, REI Study, 2001).  The program also provides extensive environmental benefits.  The 2.5 MMTCE eliminated in 2005 by recycling amounted to a savings of approximately 3 percent of all greenhouse gas emissions in the Commonwealth.  Also, recycling conserved considerable natural resources.  By recycling almost 1.2 million tons of steel cans, appliances and similar materials in 2005, Pennsylvania industries saved almost 1.5 million tons of iron ore, 829,786 tons of coal and 71,124 tons of limestone.  Through recycling newspapers, phone books, office paper, cardboard and mixed paper, the Commonwealth saved the equivalent of 78 million tree seedlings grown for 10 years.  These trees would sequester carbon dioxide from the atmosphere and store it in their wood.

Projected GHG Reductions:  Listed below is the baseline data that reflects the reduction of carbon equivalent since 2001.

| YEAR | GHG REDUCTION |
| --- | --- |
| 2001 | 2.1 MMTCE |
| 2002 | 1.7 MMTCE |
| 2003 | 2.1 MMTCE |
| 2004 | 1.9 MMTCE |
| 2005 | 2.5 MMTCE |

Historically, data reported to PA DEP demonstrates an annual modest increase in the tonnage of materials recycled.  In 1989, the first full year of Act 101 recycling reporting, approximately 378,000 tons of materials were recycled.  Since then the program has grown to nearly 4.9 million tons of materials recycled in 2005.  These annual increases provide a proven track record of quantifiable environmental and economic benefits.

| YEAR | POPULATION | DISPOSAL | PER CAPITA DISPOSAL PER DAY | RECYCLING |
| --- | --- | --- | --- | --- |
|  |  | IN TONS | IN TONS | IN TONS |
| 2000 | 12,281,054 | 9,324,468 | 0.76 | 3,791,433 |
| 2001 | 12,281,054 | 9,477,159 | 0.77 | 3,941,949 |
| 2002 | 12,281,054 | 9,613,250 | 0.78 | 3,927,048 |
| 2003 | 12,281,054 | 10,201,821 | 0.83 | 4,448,937 |
| 2004 | 12,281,054 | 10,373,136 | 0.84 | 4,747,332 |
| 2005 | 12,440,621 | 10,181,392 | 0.82 | 4,865,923 |

Pennsylvania’s recycling data was analyzed in the NERC Environmental Benefits Calculator.  The raw 2005 data inputs used for the analysis are displayed in Attachment 1.   Attachment 2 shows GHG reductions estimated by the calculator for 2005.  Attachment 3 shows GHG reductions based on the recycling of recyclable materials that were identified as disposed in the Statewide Waste Characterization Study (April 2003).  Attachment 4 is the NERC Environmental Benefits Calculator in spreadsheet form including five worksheets reflecting 2005 Pa. recycling data.

### Total Reduction: 10.3 MMTCO2e

18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  This has been determined to be a feasible goal.  Baseline reductions have been subtracted to reveal the additional reductions gained by this measure (10.3 MMTCO2e).

Economic Cost:  The overall cost to the Commonwealth needed to increase recycling to achieve the increased greenhouse gas reductions could be funded partially through the Recycling Fund, provided it is reauthorized by the General Assembly. The Commonwealth should realize an overall economic benefit from avoided waste disposal cost, increased numbers of jobs from an increased recycling industry, taxes from new business and some increased revenues from the sales of the new materials being recycled.

Industry may need to make some capital investments to facilitate increased collection.  The capital expenditures should be recouped in a reasonable amount of time based on the avoided disposal costs.  The avoided disposal costs in concert with the greenhouse gas reductions make any increased recycling expenditures a solid investment.

Implementation Steps:  Pa. DEP has a three-pronged strategy to facilitate increased recycling in the Commonwealth.  The separation into distinct areas will allow the Department to better monitor government progress with internal mechanisms.  To ensure that industry and the general public have meaningful input into the new recycling mandates the Department will utilize the regulatory process.

- The first prong is focused on ensuring that we as state government are taking a leadership role and maximizing our recycling efforts.  These efforts will be initiated with a new comprehensive management directive that will ensure all Commonwealth Agencies, Boards and Commissions are implementing recycling and waste reduction programs, as well as purchasing environmentally preferable products.

- Secondly, the Department depends on county governments to report recycling activities within their jurisdiction, as required by Act 101.  To facilitate more timely and improved reporting the Department will implement or procure a new or modified reporting system to capture much of the recycling data that currently goes unreported.

- The third prong is focused on industry and waste companies.  The Department will be making significant changes to the municipal and residual waste regulations that will prevent the disposal of certain materials and require new collection programs for a host of materials.  This regulatory reform will take 18-36 months until a final rulemaking is in place.   During that time the Department will continue its work in building increased capacity to recycle those materials banned from disposal.  The Department will use existing Recycling Fund monies to support the development of infrastructure.

In addition to the three steps identified above, some consideration could be given to the elimination of the Sunset date (December 31, 2011) for the recycling fees.  This would increase available funds for this and other related initiatives.

The following table depicts targeted achievements for additional Greenhouse Gas Reductions by increased recycling through 2025:

| YEAR | ACTION | % OF GOAL* | GHG REDUCTION | GHG REDUCTION |
| --- | --- | --- | --- | --- |
| 2000 | Historical |  | 2.1 MMTCE | 7.7 MMTCO2 |
| 2012 | Legislation and Regulations in Place | 20% | 3.0 MMTCE | 11 MMTCO2 |
| 2015 | Increased Non-regulatory Enhancements | 50% | 3.8 MMTCE | 14 MMTCO2 |
| 2020 | Program Maintained and Improvement | 80% | 4.5 MMTCE | 17 MMTCO2 |
| 2025 | Completion | 100% | 5.0 MMTCE | 18 MMTCO2* |

* Assumes achievement of additional reductions of 2.5 MMTCE or 9.2 MMTCO2, 86% of the potential reduction of 2.9 MMTCE or 11 MMTCO2.

18 MMTCO2e represents 86% of the state’s total recycling potential of 20 MMTCO2e.  This has been determined to be a feasible goal.  Baseline reductions have been subtracted to reveal additional reductions gained by this measure.

Potential Overlap:

- Increased Capture and Use of Landfill Methane

- Solid Waste Initiative

Attachment 1:

| Pa. Materials Recycled, 2005 |  |  |  |
| --- | --- | --- | --- |
| MATERIAL | DEP Code(s) | Breakout | TONS |
| FOOD WASTE | FW1 |  | 66,481.70 |
| GLASS |  |  |  |
| GLASS: CLEAR | GL1 | 15,577.80 |  |
| GLASS: MIXED | GL2 | 21,866.30 |  |
| GLASS: GREEN | GL3 | 6,311.40 |  |
| GLASS: BROWN | GL4 | 6,681.50 |  |
| GLASS: PLATE | GL5 | 5,153.20 |  |
| GLASS: OTHER | GL6 | 1,929.30 |  |
| Subtotal Glass |  |  | 57,519.50 |
| BATTERY: LEAD-ACID | B01 |  | 22,169.90 |
| METALS |  |  |  |
| ALUMINUM CANS | AA1 | 17,590.00 |  |
| FERROUS | F01 | 580,142.10 |  |
| STEEL & BIMETALLIC (TIN) CANS | F02 | 13,935.90 |  |
| WHITE GOODS | F03 | 56,383.30 |  |
| MIXED METALS | MM1 | 174,797.40 |  |
| MIXED CANS | MX2 | 2,547.00 |  |
| NON FERROUS | N01 | 48,413.40 |  |
| COPPER | N02 | 4,524.60 |  |
| BRASS | N03 | 2,349.60 |  |
| LEAD | N04 | 167.5 |  |
| STAINLESS STEEL | N05 | 203,794.40 |  |
| NICKEL | N10 | 48.7 |  |
| WIRE/CABLE | W01 | 1,455.30 |  |
| Subtotal Metals |  |  | 1,106,149.20 |
| PAPER |  |  |  |
| PAPER: CARDBOARD | C01 | 713,552.00 |  |
| PAPER: BROWN BAGS & SACKS | C02 | 3,749.60 |  |
| PAPER: MAGAZINE | PA1 | 24,682.80 |  |
| PAPER: NEWSPRINT | PA2 | 244,252.40 |  |
| PAPER: MIX | PA3 | 230,483.50 |  |
| PAPER: OFFICE PAPER | PA4 | 76,303.80 |  |
| PAPER: COMPUTER | PA5 | 3,807.70 |  |
| PAPER: PHONE BOOKS | PA6 | 1,242.50 |  |
| Subtotal Papers |  |  | 1,298,074.30 |
| PLASTICS |  |  |  |
| DRUM PLASTIC | DR1 | 791.2 |  |
| PLASTIC: PET | PL1 | 6,754.60 |  |
| PLASTIC: HDPE | PL2 | 6,955.40 |  |
| PLASTIC: PVC (POLYVINYL/CHLORIDE) | PL3 | 15,206.50 |  |
| PLASTIC: LPDE (LOW DENSITY POLYETHYLENE) | PL4 | 2,598.90 |  |
| PLASTIC: PP (POLYPROPLENE) | PL5 | 3,236.20 |  |
| PLASTIC: PS (POLYSTYRENE) | PL6 | 1850.2 |  |
| PLASTIC: MIXED | PL7 | 16,225.60 |  |
| PLASTIC: FILM | PL8 | 5,747.40 |  |
| PLASTIC: OTHER | PL9 | 4,594.90 |  |
| Subtotal Plastics |  |  | 63,960.90 |
| SINGLE STREAM | SS1 |  | 43,645.80 |
| TEXTILES | M03 |  | 25,182.70 |
| TIRES | M01 |  | 55,416.50 |
| WOOD | WW1 |  | 213,284.90 |
| YARD TRIMMAGE | Y03 |  | 585,681.50 |
| OTHER RECYCLABLES |  |  |  |
| CIRCUIT BOARDS | CB1 | 61.6 |  |
| CONSUMER ELECTRONICS | CRT | 2,900.00 |  |
| FLUORESCENT TUBES | FL1 | 261 |  |
| HOUSEHOLD HAZARDOUS WASTE | HHW | 1,353.90 |  |
| MATTRESSES | MT1 | 116.6 |  |
| ANTIFREEZE | O02 | 1,342.20 |  |
| OIL FILTERS | OL3 | 798.9 |  |
| COMMINGLED MATERIALS | XXX | 228,699.80 |  |
| Subtotal Other Recyclables |  |  | 235,534.00 |
| 904 excess |  |  | 25,929.00 |
| Tire excess |  |  | 72,770.00 |
| ISRI excess |  |  | 51,795.00 |
| Lancaster County (RE-Trac) | INCORPORATED |  |  |
| TOTAL STANDARD |  |  | 3,923,594.90 |
| TOTAL NON-STANDARD |  |  | 942,328.10 |
| GRAND TOTAL |  |  | 4,865,923.00 |

Attachment 2:

| Reductions in Greenhouse Gas Emissions as a Result of 2005 Recycling Tons Recycled Greenhouse Gas Emissions Associated with Recycling (MTCE) Greenhouse Gas Emissions if Recyclables Had Been Disposed (MTCE) Net Greenhouse Gas Emissions from Recycling as Compared to Disposal (MTCE) Reporting Year 2005 Aluminum Cans 33,619 -124,418 381 -124,799 Steel Cans 44,590 -21,817 -2,494 -19,323 Glass 201,097 -15,239 2,194 -17,433 HDPE 40,115 -15,230 1,923 -17,152 LDPE 2,599 -1,201 125 -1,326 PET 39,736 -16,667 2,161 -18,828 Corrugated Cardboard 714,526 -606,295 46,378 -652,673 Magazines/Third-class Mail 25,935 -21,718 -2,313 -19,405 Newspaper 276,048 -210,163 -63,883 -146,280 Office Paper 76,652 -59,629 32,309 -91,939 Phonebooks 1,721 -1,246 -398 -848 Textbooks 0 0 0 0 Whole Computers 0 0 0 0 Food Scraps 66,482 -3,600 10,599 -14,199 Yard Trimmings 585,682 -31,717 -35,002 3,286 Grass 0 0 0 0 Leaves 0 0 0 0 Branches 213,285 -11,550 -25,957 14,407 Ferrous Scrap Metal 650,458 -318,251 -36,376 -281,875 Aluminum Scrap Metal 31,681 -117,246 359 -117,605 Copper Wire 0 0 0 0 Tires 128,187 -63,783 2,101 -65,884 Construction & Demolition 688,211 NA NA NA Carpet 0 0 0 0 Dimensional Lumber 0 0 0 0 Medium-density Fiberboard 0 0 0 0 Clay Bricks 0 NA NA NA Aggregate 0 0 0 0 Fly Ash 0 0 0 0 Mixed Paper, Broad Definition 244,234 -235,593 12,891 -248,484 Mixed Metals 490,360 -703,102 -17,722 -685,380 Mixed Plastics 47,652 -19,418 2,407 -21,825 Mixed Recyclables 0 0 0 0 Mixed Organics 0 0 0 0 Other Recyclables 263,279 NA NA NA Total as a Result of Recycling 4,866,149 -2,597,884 -70,318 -2,527,566 |  |  |  |
| --- | --- | --- | --- |

Attachment 3:

# Potential GHG Reductions if recyclable materials disposed were recycled

|  | Potential Tons Recyclable | Greenhouse Gas Emissions Associated with Recycling (MTCE) |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Reporting Year | (MSW Composition Study, April 2003) |  |  |  |  |
| Aluminum Cans | 48,844 | -180,763 |  |  |  |
| Steel Cans | 102,532 | -50,166 |  |  |  |
| Glass | 234,629 | -17,780 |  |  |  |
| HDPE | 68,082 | -25,848 |  |  |  |
| LDPE | 0 | 0 |  |  |  |
| PET | 87,601 | -36,743 |  |  |  |
| Corrugated Cardboard | 785,032 | -666,121 |  |  |  |
| Magazines/Third-class Mail | 251,027 | -210,208 |  |  |  |
| Newspaper | 389,263 | -296,357 |  |  |  |
| Office Paper | 341,975 | -266,029 |  |  |  |
| Phonebooks | 0 | 0 |  |  |  |
| Textbooks | 0 | 0 |  |  |  |
| Whole Computers | 0 | 0 |  |  |  |
| Food Scraps | 0 | 0 |  |  |  |
| Yard Trimmings | 0 | 0 |  |  |  |
| Grass | 0 | 0 |  |  |  |
| Leaves | 0 | 0 |  |  |  |
| Branches | 0 | 0 |  |  |  |
| Ferrous Scrap Metal | 282,131 | -138,039 |  |  |  |
| Aluminum Scrap Metal | 43,057 | -159,347 |  |  |  |
| Copper Wire | 0 | 0 |  |  |  |
| Tires | 0 | 0 |  |  |  |
| Construction & Demolition | 0 | NA |  |  |  |
| Carpet | 0 | 0 |  |  |  |
| Dimensional Lumber | 0 | 0 |  |  |  |
| Medium-density Fiberboard | 0 | 0 |  |  |  |
| Clay Bricks | 0 | NA |  |  |  |
| Aggregate | 0 | 0 |  |  |  |
| Fly Ash | 0 | 0 |  |  |  |
| Mixed Paper, Broad Definition | 433,821 | -418,473 |  |  |  |
| Mixed Metals | 32,138 | -46,081 |  |  |  |
| Mixed Plastics | 906,653 | -369,457 |  |  |  |
| Mixed Recyclables | 0 | 0 |  |  |  |
| Mixed Organics | 0 | 0 |  |  |  |
| Other Recyclables | 0 | NA |  |  |  |
| Total as a Result of Recycling | 4,006,785 | -2,881,412 |  |  |  |

Attachment 4:

NERC Environmental Benefits Calculator, 2005 Pa. Recycling Data