ANNEX A

TITLE 25. ENVIRONMENTAL PROTECTION

PART I. DEPARTMENT OF ENVIRONMENTAL PROTECTION

Subpart C. PROTECTION OF NATURAL RESOURCES

ARTICLE II. WATER RESOURCES

CHAPTER 16. WATER QUALITY TOXICS MANAGEMENT STRATEGY—

STATEMENT OF POLICY

******

# Subchapter A. GUIDELINES FOR DEVELOPMENT OF CRITERIA

# FOR TOXIC SUBSTANCES AND WATER QUALITY CRITERIA

# FOR TOXIC SUBSTANCES

******

### APPENDIX A

******

### TABLE 1A

# SITE-SPECIFIC WATER QUALITY CRITERIA FOR TOXIC SUBSTANCES

The following table contains water quality criteria that were developed based on a need for a site-specific water quality criterion, and according to the guidelines for criteria development, as contained in this chapter. The sources the Department of Environmental Protection (Department) uses to obtain relevant risk assessment values for these criteria include, but is not limited to, United States Environmental Protection Agency agency-wide supported data systems such as Integrated Risk Information System (IRIS) and ECOTOX; the Great Lakes’ Tier II [acquatic] aquatic life criteria guidelines; and other nationally developed criteria as reviewed and approved by the Department for Statewide use. A criterion placed in this table will remain a site-specific criterion as originally developed and be incorporated into the appropriate portion of § §  93.9a—93.9z that relates to ‘‘exceptions to specific criteria’’ unless, during rulemaking, it is determined that the same criteria has general Statewide applicability.

| PP NO | Chemical Name | CAS Number | Fish and [Acquatic] Aquatic Life Criteria | Human Health Criteria [(ug/l)] (ug/L) | Health Effect | Drainage List | Water Body/County |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Criteria Continuous Concentrations [(ug/l)] (ug/L) | Criteria Maximum Concentration [(ug/l)] (ug/L) |  |  |  |  |
| [- | 1,4 Dioxane | 123911 | 103000 | 515000 | 3.0 | CRL | F | West Branch Perkiomen Creek, Berks County |
| - | Acrylamide | 79061 | N/A | N/A | .008 | CRL | S | Stump Creek, Henderson Township, Jefferson County] |
| Acronyms and Footnotes to Table 1A |
|  | CAS—Chemical Abstract Service number CRL—Cancer risk level at 1 x 10-6 H—Threshold effect human health criterion; incorporates additional uncertainty factor for some Group C carcinogens. 1n [H]—Natural Logarithm of the Hardness of stream as mg/l CaCO3 ug/L—Micrograms per liter N/A—Criterion not developed PP NO—Priority Pollutant Number |

******

### TABLE  2A

### APPROVED EPA AND DEP ACCREDITED ANALYTICAL METHODS AND DETECTION LIMITS: INORGANICS

| Parameter (CAS) | Method Number (Description) *Source | Detection Limit (MDL) (µg/[l]L) |
| --- | --- | --- |

******

| 11M | SILVER (07440224) | 3111 B or C (AA, flame) | 10 |
| --- | --- | --- | --- |
|  |  | 3113 B (AA, furnace) | 0.2 |
|  |  | 200.7 (ICP/AES) | 2 |
|  |  | 200.8 (ICP/MS) | 0.1 |
|  |  | 200.9 (STGFAA) | 0.6 |
|  |  | —*3 (DCP) | NA |
| — | STRONTIUM (07440246) | 200.7 (ICP/AES) | 0.01 |
|  |  | 200.8 (ICP/MS) | 2.0 |
|  |  | 6010B (ICP/AES) | 0.01 |
|  |  | 6020(ICP/MS) | 1.0 |

* * * * *

### TABLE  2B

### APPROVED EPA AND DEP ACCREDITED ANALYTICAL METHODS AND DETECTION LIMITS: ORGANICS

| Parameter (CAS) | Method Number (Description) *Source | Detection Limit (MDL) (µg/[l]L) |
| --- | --- | --- |

* * * * *

| — | BENZENE METADISULFONIC ACID (00098486) | OR 357A Test America, HPLC/UV or LC/MS/MS | 50 |
| --- | --- | --- | --- |
| — | BENZENE MONOSULFONIC ACID (00098113) | OR 357A Test America, HPLC/UV or LC/MS/MS | 50 |
| 1A | 2-CHLOROPHENOL (00095578) | 604—GC/FID 604—GC/ECD 625—GC/MS 1625B—GC/MS(isotope) | 0.31 0.58 3.3 10 |

* * * * *

| 7A | 4-NITROPHENOL (00100027) | 604—GC/FID 604—GC/ECD 625—GC/MS 1625B—GC/MS(isotope) | 2.8 0.70 2.4 50 |
| --- | --- | --- | --- |
| — | NONYLPHENOL (00104405) | 7065-06M—GC/MS D7485-09 – LC/LC/TANDEM MS | 2.0 .033 |

* * * * *

| 10A | PHENOL (00108952) | 604—GC/FID 604—GC/ECD 625—GC/MS 1625B—GC/MS(isotope) | 0.14 2.2 1.5 10 |
| --- | --- | --- | --- |
| — | P-PHENOL SULFONIC ACID (00098679) | OR 357A Test America, HPLC/UV or LC/MS/MS | 50 |
| — | RESORCINOL (01084603) | 8270D—GC/MS | 100 |

* * * * *

| 3V | BENZENE (00071432) | 602—GC/PID 624—GC/MS 1624B—GC/MS(isotope) | 0.20 4.4 10 |
| --- | --- | --- | --- |
| — | BENZYL CHLORIDE (00100447) | 8021B—GC 8260B—GC/MS | 1.0 .005-5.0 |
| 5V | BROMOFORM (00075252) | 601—GC/Hal. 624—GC/MS 1624B—GC/MS(isotope) | 0.20 4.7 10 |
| — | 2-BUTOXYETHANOL (00111762) | EPA R5/6LC – LC/MS/MS (DIRECT INJECT) | 125 |

* * * * *

| 26V | 1,2-trans-DICHLOROETHYLENE (00156605) | 601—GC/Hal. 624—GC/MS 1624B—GC/MS(isotope) | 0.10 1.6 10 |
| --- | --- | --- | --- |
| — | 1,2-cis-DICHLOROETHYLENE (00156592) | 601—GC/Hal. 624—GC/MS 1624B—GC/MS(isotope) | 0.10 1.6 10 |

* * * * *

| 29V | TRICHLOROETHYLENE (00079016) | 601—GC/Hal. 624—GC/MS 1624B—GC/MS(isotope) | 0.12 1.9 10 |
| --- | --- | --- | --- |
| — | 1,2,4-TRIMETHYLBENZENE (00095636) | 524.2 – GC/MS 624 – GC/MS 8021B—GC 8260B—GC/MS | 0.5 1.0 1.0 2.0 |
| — | 1,3,5-TRIMETHYLBENZENE (00108678) | 524.2 – GC/MS 624 – GC/MS 8021B—GC 8260B—GC/MS | 0.5 1.0 1.0 2.0 |

* * * * *

| 2B | ACENAPHTHYLENE (00208968) | 610—GC/FID 610—HPLC 625—GC/MS 1625B—GC/MS(isotope) | NA 2.3 3.5 10 |
| --- | --- | --- | --- |
| — | ACRYLAMIDE (00079061) | 8032A (GC) 8316 (HPLC) | .032 10 |

* * * * *

| 18B | CHRYSENE (00218019) | 610—GC/FID 610—HPLC 625—GC/MS 1625B—GC/MS(isotope) | NA 0.15 2.5 10 |
| --- | --- | --- | --- |
| — | CYCLOHEXYLAMINE (00108918) | 8270B—GC/MS | .01 |

* * * * *

| 29B | DI-N-OCTYL PHTHALATE (00117840) | 606—GC/ECD 625—GC/MS 1625B—GC/MS(isotope) | 3.0 2.5 10 |
| --- | --- | --- | --- |
| — | 1,4-DIOXANE (00123911) | 624—GC/MS 625—GC/MS 8260B —GC/MS 8270L—GC/MS | 1.0 5.0 0.1 0.2 |

* * * * *